## Slide 1: Course on Computer Communication and Networks Lecture 15 Summary (flashback) and Projection (related topics – continuation of study)
EDA344/DIT 420, CTH/GU

## Slide 2: Important for the exam
When/where: wednesday March 16, 14.00-18.00, M-building
You may have with you:
English-X dictionary
no calculators, PDAs, etc (if/where numbers matter, do rounding)
Grading
30-40, 41-50, 51-60 (out of 60)= 3, 4, 5 (CTH)
30-44, 45-60 (out of 60) = G, VG (GU)
To think during summary-study
Have overview, critical eye; explain; ask yourselves: why is this so? / how does it work (or not work)?

## Slide 3: Flashback

## Slide 4: Principles, Organisation
Network Problems (in the order faced in the 1st intro):
Mobility, performance, security, …, …
serving different types of traffic,
connecting transparently different networks,
routing, congestion control,
access to shared (broadcast) transmission medium
producer-consumer problems, flow and error control
Layering : principle, why

## Slide 5: Highlights
Software-defined networks
network security issues
TCP/IP, LAN protocol stack
delays performance
routing, also with mobility
multiple access protocols (wired, wireless)
reliable data transfer
datagram vs VC
congestion control

## Slide 6: Types of delay; performance
Propagation, transmission, queueing, processing
Throughput -- effective bandwidth
Utilization -- efficiency
Packet-switching: impact of store&forward, pipelines, space-time diagrams
Sliding windows performance
Relation between delays-losses
A
B
propagation
transmission
nodal
processing
queuing

## Slide 7: Reliable data transfer
Guaranteed, in-order, correct delivery:
  stop&wait
  sliding windows
  sequence numbers
  window sizes
  dynamic windows (TCP)
  performance
  Flow control
Error detection: checksums
Error control: go-back-n, selective repeat, FEC methods

## Slide 8
Congestion
Control
RT traffic/streaming
Datagram vs VC end-to-end comm.

## Slide 9: Datagram vs VC end-to-end communication
Conceptual differences
Decisions, comparison

## Slide 10: Congestion control (CC)
why, how congestion occurs
CC in TCP and performance; implied weaknesses
CC in other ways, e.g. VC-based networks
  Real-time (RT)-traffic resource reservation:
    traffic shaping and policing
  rate-based

## Slide 11: RT/streaming traffic
Conceptual needs:
packet/flow marking
Admission control
Traffic shaping & policing
Packet scheduling
Internet context
Application-level solutions (playout delay, forward-error-control, caching-CDN)
Intserv, Diffserv, traffic engineering

## Slide 12: Highlights
Software-defined networks
network security issues
TCP/IP, LAN protocol stack
delays performance
routing, also with mobility
multiple access protocols (wired, wireless)
reliable data transfer
datagram vs VC
congestion control

## Slide 13: Routing, also with mobility
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Routing algorithms, protocols
Forwarding in routers
Resource, policy issues
Addressing mobility, tunneling
Mobile
Switching
Center
Public telephone
network, and
Internet
Mobile
Switching
Center
Complementary video links
- IP addresses and subnets http://www.youtube.com/watch?v=ZTJIkjgyuZE&list=PLE9F3F05C381ED8E8&feature=plcp
- How does BGP choose its routes http://www.youtube.com/watch?v=RGe0qt9Wz4U&feature=plcp

## Slide 14: Medium access: multiple access methods
Strategies: (functionality, appropriateness)
Contention-based (random access), wired/wireless:
  Aloha, CSMA(CD/CA)
Collision-free:
  Channel partitioning: TDMA, FDMA, CDMA
  Taking turns: e.g. tokens, reservation-based
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 15: Highlights
Software-defined networks
network security issues
TCP/IP, LAN protocol stack
delays performance
routing, also with mobility
multiple access protocols (wired, wireless)
reliable data transfer
datagram vs VC
congestion control

## Slide 16: TCP/IP protocol stack, applications, evolution
Instantiation of network- solutions
(Routing, Congestion Control, Flow & error control, applications, link layer technologies)
Advantages, limitations, updates
New types of applications and how they function given the existing state of Internet: multimedia/streaming applications, CDNs, P2P applications, overlays

## Slide 17: LANs & related link technologies
Protocol Examples: wired, wireless
  Ethernet, 802.xy, GSM:
    Functionality, performance under low/high load
Connecting devices;
  functionalities and differences (Hubs, switches)
  Algorithms for switch-”routing”: learning& forwarding of packets
ARP
switch

## Slide 18: Highlights
Software-defined networks
network security issues
TCP/IP, LAN protocol stack
delays performance
routing, also with mobility
multiple access protocols (wired, wireless)
reliable data transfer
datagram vs VC
congestion control

## Slide 19: Security issues
C, I, A and methods to achieve them
  The language of cryptography
  Message integrity, signatures
Instantiation in Internet: SSL, IPsec
Firewalls
secure
sender
s
secure
receiver
channel
data, control messages
data
data
Alice
Bob
Trudy

## Slide 20: Overlays, software-defined networks
P2P/streaming applications-infrastructure (application-layer networking)
traffic engineering, tunneling
Software-defined networks: separation of control and execution planes; virtualization of ”layers”: eg. routing table updates implemented elsewhere (not in particular routers)
5G; Internet of things concepts
… complement the networking infrastructure …
…taking advantage of the network resources at the edge of the network…

## Slide 21: Synthesis: a day in the life of a web request
putting-it-all-together: synthesis!
  goal: identify, review protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 22: A day in the life …. : scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page

## Slide 23: A day in the life… connecting to the Internet
connecting laptop needs to get its own IP address: use DHCP
router
(runs DHCP)
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demux’ed to IP demux’ed to UDP demux’ed to DHCP

## Slide 24: A day in the life… connecting to the Internet
DHCP server formulates DHCP ACK containing client’s IP address (and also IP address of first-hop router for client, name & IP address of DNS server)
router
(runs DHCP)
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 25: A day in the life… ARP (before DNS, before HTTP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encasulated in Eth. In order to send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 26: A day in the life… using DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network to destination (DNS-server) network, routed (tables created by RIP, OSPF and BGP routing protocols) to DNS server
demux’ed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 27: A day in the life… TCP connection carrying HTTP
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK

## Slide 28: A day in the life… HTTP request/reply
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datgram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 29: Synthesis cont. 1. Reflections, prespectives 2. Networking constantly evolving

## Slide 30: The Internet: virtualizing networks
1974: multiple unconnected nets
  ARPAnet
  data-over-cable networks
  packet satellite network (Aloha)
  packet radio network
… differing in:
  addressing conventions
  packet formats
  error recovery
  routing
ARPAnet
satellite net
"A Protocol for Packet Network Intercommunication",
V. Cerf, R. Kahn, IEEE Transactions on Communications,
May, 1974, pp. 637-648.

## Slide 31: The Internet: virtualizing networks
Gateway:
“embed internetwork packets in local packet format”
route (at internetwork level) to next gateway
ARPAnet
satellite net
gateway
Internetwork layer (IP):
addressing: internetwork appears as single, uniform entity, despite underlying local network heterogeneity
network of networks

## Slide 32: Cerf & Kahn’s Internetwork Architecture
What is virtualized?
two layers of addressing: internetwork and local network
new layer (IP) makes everything homogeneous at internetwork layer
underlying local network technology
  Cable, satellite, 56K telephone modem
  Ethernet, other LAN
  ATM/ MPLS (Multiprotocol Label Switching Protocol)
… “invisible” at internetwork layer. Looks like a link layer technology to IP

## Slide 33: e.g. IP-Over-ATM
“Classic” IP over eg Ethernet
3 “networks” (e.g., LAN segments)
MAC (eg802.3) and IP addresses
IP over ATM
replace “network” (e.g., LAN segment) with ATM network
ATM addresses (as MAC addresses), IP addresses
ATM
network
Ethernet
LANs
Ethernet
LANs

## Slide 34: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 35: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.

## Slide 36: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit (imaginary) ISP? Customer and provider ISPs have economic agreement.
global ISP

## Slide 37: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C

## Slide 38: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
peering link
(no payment to each-other)
Internet exchange point
(ca 300 in the world;
multiple ISPs peering/switching;
3rd company)

## Slide 39: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
regional net

## Slide 40: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
regional net
Content provider network

## Slide 41: Internet structure: network of networks
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., AT&T, NTT, TeliaSonera, DeutcheTelecom), national & international coverage
  A new form of content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP

## Slide 42: Synthesis cont. 1. Reflections, prespectives 2. Networking constantly evolving

## Slide 43: Data center networks
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  managing/balancing load, networking, data bottlenecks
Inside a 40-ft Microsoft container,
Chicago data center

## Slide 44
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
Load
balancer
Load
balancer
B
1
2
3
4
5
6
7
8
A
C
Border router
Access router
Internet
Data center networks
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)
  Distributed systems & networks working together

## Slide 45
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Data center networks
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy
  Distributed systems & networks working together

## Slide 46
Extra (guest) lecture (joint with Adv. Distributed Systems course), Friday 10-11 room EE
Niklas Gustavsson, backend engineering team leader at Spotify, Gothenburg
Title:
“Gossiping (ie randomized multicast routing)
and
Conflict-free_replicated_data_types” (eg distributed hash tables and/or related)

## Slide 47: More examples: a story in progress + possible followup course... Overlays useful here, too:

## Slide 48: New power grids: be adaptive!
Bidirectional power and information flow
  – Micro-producers or “prosumers”, can share resources
  – Distributed energy resources
Communication + resource-administration (distributed system) layer: IoT
Notes: Bidirectional power flow
Communications layer
= From “water pipes” model to “traffic network” model

## Slide 49: El-networks as distributed cyber-physical systems
Cyber system
El- link and/or communication link
Overlay network
Physical system
Computing+ communicating device
Why adding “complexity” in the infrastructure?
Motivation: enable renewables, better use of el-power
Notes: Info-centered ElNet: information overlay on the energy distribution system

## Slide 50: Course/Masterclass: (DAT300, LP1) ICT Support for Adaptiveness and Security in the Smart Grid
Goals
  Students (CSE and other disciplines) get introduced to advanced interdisciplinary concepts related to the smart grid, thus
  building an understanding of essential notions in the individual disciplines, and
  investigating a domain-specific problem relevant to the smart grid that need an understanding beyond the traditional ICT field.

## Slide 51: Environment
Based on both the present and future design of smart systems.
  How can techniques from networks/distributed systems be applied to large, heterogeneous systems where a massive amount of data must be collected/processed?
  How can such a system, containing legacy components with no security primitives, be made secure when the communication is added by interconnecting the systems?
The students will have access to a hands-on lab, where they can run and test their design and code.

## Slide 52: Course Setup
The course is given on an advanced master’s level, resulting in 7.5 points.
Study Period 1
  Can also define individual, “research internship courses”, 7.5, 15p or MS thesis, starting earlier
The course structure
  lectures to introduce the two disciplines (“crash course-like”); invited talks by industry and other collaborators
  second part: seminar-style where research papers from both disciplines are presented & discussed.
  At the end of the course the students are also expected to present their projects.
Notes: Different lectures are given by teachers with different competences (will have teachers from power systems)

## Slide 53: Thank you
Recall, important for the exam:
When/where: wednesday March 16, 14.00-18.00, M
You may have with you:
English-X dictionary
no calculators, PDAs, etc (if/where numbers matter, do rounding)
To think during last, summary-study
Overview; critical eye; explain; ask yourselves: why is this so? / How does it work?
Good luck with all your efforts!!!
“If you hear a voice within you say ‘you cannot paint,’ then by all means paint, and that voice will be silenced.” – Vincent Van Gogh