## Slide 1: Course on Computer Communication and Networks Lecture 5 Chapter 3; Transport Layer, Part B
EDA344/DIT 420, CTH/GU

## Slide 2: Internet transport-layer protocols
reliable, in-order delivery: TCP; also provides
  flow control
  congestion control
  connection setup
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP

## Slide 3: Roadmap Transport Layer
transport layer services
multiplexing/demultiplexing
connectionless transport: UDP
principles of reliable data transfer
connection-oriented transport: TCP
  reliable transfer
    Acknowledgements
    Retransmissions
    Connection management
    Flow control and buffer space
  Congestion control
    Principles
    TCP congestion control

## Slide 4: TCP: Overview RFCs: 793,1122,1323, 2018, 5681
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) inits sender & receiver state before data exchange
flow control:
  sender will not overwhelm receiver
congestion control:
  sender will not flood network with traffic (but still try to maximize throughput)
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
pipelined:
  TCP congestion and flow control set window size
Notes: Mod TO

## Slide 5: TCP segment structure
dest port #
32 bits
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
ACK: ACK # valid
URG: urgent data
(generally not used)
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)
# bytes
rcvr willing
to accept (flow control)
application
data
(variable length)
source port #

## Slide 6: Roadmap Transport Layer
transport layer services
multiplexing/demultiplexing
connectionless transport: UDP
principles of reliable data transfer
connection-oriented transport: TCP
  reliable transfer
    Acknowledgements
    Retransmissions
    Connection management
    Flow control and buffer space
  Congestion control
    Principles
    TCP congestion control

## Slide 7: TCP seq. numbers, ACKs
sequence numbers:
  “number” of first byte in segment’s data
acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
incoming segment to sender
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
outgoing segment from sender

## Slide 8: TCP seq. numbers, ACKs
User
types
‘C’
host ACKs
receipt
of echoed ‘C’
host ACKs receipt of ‘C’, echoes back ‘C’
Simple example scenario
Based on telnet msg exchange
Host B
Host A
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Always ack next in-order expected byte

## Slide 9: TCP: cumulative Ack - retransmission scenarios
Cumulative ACK
(Premature) timeout
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8
bytes of data
timeout
ACK=120
Seq=100, 20 bytes of data
ACK=120
SendBase=100
SendBase=120
SendBase=120
SendBase=92
X
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=120, 15 bytes of data
timeout
Seq=100, 20 bytes of data
ACK=120

## Slide 10: TCP ACK generation [RFC 1122, RFC 5681]
Event
in-order segment arrival,
no gaps,
everything else already ACKed
in-order segment arrival,
no gaps,
one delayed ACK pending
out-of-order segment arrival
higher-than-expect seq. #
gap detected
arrival of segment that
partially or completely fills gap
TCP Receiver action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single
cumulative ACK
send (duplicate) ACK, indicating seq. #
of next expected byte
immediate send ACK if segment starts
at lower end of gap
Notes: Mod TO

## Slide 11: From RFC 1122
TCP SHOULD implement a delayed ACK, but an ACK should not be excessively delayed; in particular, the delay MUST be less than 0.5 seconds, and in a stream of full-sized segments there SHOULD be an ACK for at least every second segment.
A delayed ACK gives the application an opportunity to update the window and perhaps to send an immediate response. In particular, in the case of character-mode remote login, a delayed ACK can reduce the number of segments sent by the server by a factor of 3 (ACK, window update, and echo character all combined in one segment).
In addition, on some large multi-user hosts, a delayed ACK can substantially reduce protocol processing overhead by reducing the total number of packets to be processed.
However, excessive delays on ACK's can disturb the round-trip timing and packet "clocking" algorithms.
We also emphasize that this is a SHOULD, meaning that an implementor should indeed only deviate from this requirement after careful consideration of the implications.
Notes: TO

## Slide 12: Roadmap Transport Layer
transport layer services
multiplexing/demultiplexing
connectionless transport: UDP
principles of reliable data transfer
connection-oriented transport: TCP
  reliable transfer
    Acknowledgements
    Retransmissions
    Connection management
    Flow control and buffer space
  Congestion control
    Principles
    TCP congestion control

## Slide 13: TCP round trip time, timeout (1)
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
segment
segment
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss

## Slide 14: TCP round trip time, timeout (2)
EstimatedRTT = (1-)*EstimatedRTT + *SampleRTT
exponential weighted moving average: influence of past sample decreases exponentially fast
typical value:  = 0.125
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)

## Slide 15: TCP fast retransmit (RFC 5681)
time-out period often relatively long:
  long delay before resending lost packet
IMPROVEMENT: detect lost segments via duplicate ACKs
if sender receives 3 duplicate ACKs for same data
resend unacked segment with smallest seq #
  likely that unacked segment lost, so don’t wait for timeout
TCP fast retransmit
Implicit NAK!
Q: Why need at least 3?
X
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
Notes: Mod TO
RFC 2581 obsolete…

## Slide 16: Roadmap Transport Layer
transport layer services
multiplexing/demultiplexing
connectionless transport: UDP
principles of reliable data transfer
connection-oriented transport: TCP
  reliable transfer
    Acknowledgements
    Retransmissions
    Connection management
    Flow control and buffer space
  Congestion control
    Principles
    TCP congestion control

## Slide 17: Connection Management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();

## Slide 18: Setting up a connection: TCP 3-way handshake
SYN=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYN=1, Seq=y
ACK=1; ACKnum=x+1
choose init seq num, y
send TCP SYN/ACK
msg, acking SYN
Reserve buffer
ACK=1, ACKnum=y+1
received SYN/ACK(x)
indicates server is live;
send ACK for SYN/ACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
server state
LISTEN
Notes: Mod TO

## Slide 19: TCP: closing a connection
FIN_WAIT_2
CLOSE_WAIT
FIN=1, seq=y
ACK=1; ACKnum=y+1
ACK=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIME_WAIT
timed wait
(typically 30s)
CLOSED
FIN_WAIT_1
FIN=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB
simultaneous FINs
can be handled
RST: alternative way to close connection
immediately, when error occurs
Notes: Mod TO

## Slide 20: TCP – Closing a connection: Reset
RST is used to signal an error condition and causes an immediate close of the connection on both sides
RST packets are not supposed to carry data payload, except for an optional human-readable description of what was the reason for dropping this connection.
Examples:
  A TCP data segment when no session exists
  Arrival of a segment with incorrect sequence number
  Connection attempt to non-existing port
  Etc.
RST
Notes: TO

## Slide 21: Is TCP stateful or stateless?

## Slide 22: Roadmap Transport Layer
transport layer services
multiplexing/demultiplexing
connectionless transport: UDP
principles of reliable data transfer
connection-oriented transport: TCP
  reliable transfer
    Acknowledgements
    Retransmissions
    Connection management
    Flow control and buffer space
  Congestion control
    Principles
    TCP congestion control

## Slide 23: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application
might remove data from
TCP socket buffers ….
… slower than TCP
is delivering
(i.e. slower than sender is sending)
from sender
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control

## Slide 24: TCP flow control
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
receiver “advertises” free buffer space by including rwnd value in TCP header of receiver-to-sender segments
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unacked (“in-flight”) data to receiver’s rwnd value
guarantees receive buffer will not overflow
receiver-side buffering
3-24
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
A
To sender

## Slide 25: Roadmap Transport Layer
transport layer services
multiplexing/demultiplexing
connectionless transport: UDP
principles of reliable data transfer
connection-oriented transport: TCP
  reliable transfer
    Acknowledgements
    Retransmissions
    Connection management
    Flow control and buffer space
  Congestion control
    Principles
    TCP congestion control

## Slide 26: Principles of congestion control
congestion:
informally: “too many sources sending too much data too fast for network to handle”
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)

## Slide 27
Need for flow control
Need for congestion control
Fig. A. Tanenbaum
Computer Networks

## Slide 28: Causes/costs of congestion: scenario 1 (unrealistic)
two senders, two receivers, average rate of data is lin
one router, infinite buffers
output link capacity: R
(no retransmission in the “picture” yet)
maximum per-connection throughput: R/2
unlimited shared output link buffers
Host A
original data: lin
Host B
throughput: lout
R/2
R/2
lout
lin
R/2
delay
lin
large delays as arrival rate, lin, approaches capacity

## Slide 29: Causes/costs of congestion: scenario 2
R/2
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
“costs” of congestion:
more work (retrans) for given “goodput” (application-level throughput)
unneeded retransmissions: links carry multiple copies of pkt
R/2
lin
Realistic buffers bounded =>: duplicates
packets can be lost, dropped at router due to full buffers
sender times out, sending two copies

## Slide 30: Causes/costs of congestion: scenario 3
another cost of congestion:
when packets dropped, any “upstream transmission capacity used for that packet was wasted!
C/2
lout
lin’(incl. Retransmisions)
Consider 4 streams

## Slide 31: Approaches towards congestion control
two broad approaches towards congestion control:
end-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
network-assisted congestion control:
routers provide feedback to end systems eg.
  a single bit indicating congestion
  explicit rate for sender to send at

## Slide 32: Roadmap Transport Layer
transport layer services
multiplexing/demultiplexing
connectionless transport: UDP
principles of reliable data transfer
connection-oriented transport: TCP
  reliable transfer
    Acknowledgements
    Retransmissions
    Connection management
    Flow control and buffer space
  Congestion control
    Principles
    TCP congestion control

## Slide 33: TCP congestion control: additive increase multiplicative decrease
end-end control (no network assistance), sender limits transmission
How does sender perceive congestion?
  loss = timeout or 3 duplicate acks
  TCP sender reduces rate (Congestion Window) then
  Additive Increase: increase cwnd by 1 MSS every RTT until loss detected
  Multiplicative Decrease: cut cwnd in half after loss
  To start with: slow start
AIMD saw tooth
behavior: probing
for bandwidth
cwnd: TCP sender
congestion window size
additively increase window size …
…. until loss occurs (then cut window in half)
time
rate
~
~
cwnd
RTT
bytes/sec

## Slide 34: TCP Slow Start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 35: TCP cwnd: from exp. to linear growth + reacting to loss
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh (slow start threshold)
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
Reno: loss indicated by timeout or 3 duplicate ACKs:
cwnd is cut in half; then grows linearly
Non-optimized: loss indicated by timeout:
cwnd set to 1 MSS;
window then grows as in slow start, to threshold, then grows linearly
Notes: Mod TO

## Slide 36: Fast recovery (Reno)
Session’s experience
Notes: TO

## Slide 37: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!

## Slide 38: TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2

## Slide 39: How many windows does a TCP’s sender maintain?
Need for flow control
Need for congestion control
Fig. A. Tanenbaum
Computer Networks

## Slide 40: TCP combined flow-ctrl, congestion ctrl windows
sender limits transmission:
cwnd is dynamic, function of perceived network congestion,
rwnd dymanically limited by receiver’s buffer space
TCP sending rate:
roughly: send min {cwnd, rwnd} bytes, wait RTT for ACKS, then send more bytes
Min{cwnd, rwnd}
last byte
ACKed
sent, not-yet ACKed
(“in-flight”)
last byte sent
LastByteSent-
LastByteAcked
<
Min{cwnd, rwnd}
sender sequence number space

## Slide 41: Roadmap Transport Layer
transport layer services
multiplexing/demultiplexing
connectionless transport: UDP
principles of reliable data transfer
connection-oriented transport: TCP
  reliable transfer
    Acknowledgements
    Retransmissions
    Connection management
    Flow control and buffer space
  Congestion control
    Principles
    TCP congestion control

## Slide 42: Chapter 3: summary
principles behind transport layer services:
  Addressing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
next:
leaving the network “edge” (application, transport layers)
into the network “core”

## Slide 43: Some review questions on this part
Describe TCP’s flow control
Why does TCp do fast retransmit upon a 3rd ack and not a 2nd?
Describe TCP’s congestion control: principle, method for detection of congestion, reaction.
Can a TCP’s session sending rate increase indefinitely?
Why does TCP need connection management?
Why does TCP use handshaking in the start and the end of connection?
Can an application have reliable data transfer if it uses UDP? How or why not?

## Slide 44: Reading instructions chapter 3
KuroseRoss book
Other resources (further study)
  Eddie Kohler, Mark Handley, and Sally Floyd. 2006. Designing DCCP: congestion control without reliability. SIGCOMM Comput. Commun. Rev. 36, 4 (August 2006), 27-38. DOI=10.1145/1151659.1159918 http://doi.acm.org/10.1145/1151659.1159918
  http://research.microsoft.com/apps/video/default.aspx?id=104005
  Exercise/throughput analysis TCP in following slides
Careful | Quick
3.1, 3.2, 3.4-3.7 | 3.3

## Slide 45: Extra slides, for further study

## Slide 46: TCP throughput
avg. TCP throughput as function of window size, RTT?
  ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. trhoughput is 3/4W per RTT
W
W/2
avg TCP trhoughput =
3
4
W
RTT
bytes/sec

## Slide 47: TCP Futures: TCP over “long, fat pipes”
example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
requires W = 83,333 in-flight segments
throughput in terms of segment loss probability, L [Mathis 1997]:
  ➜ to achieve 10 Gbps throughput, need a loss rate of L = 2·10-10 – a very small loss rate!
new versions of TCP for high-speed
TCP throughput =
1.22
.
MSS
RTT
L

## Slide 48: Why is TCP fair?
two competing sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2

## Slide 49: Fairness (more)
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this
e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2

## Slide 50: TCP delay modeling (slow start – related)
Q: How long does it take to receive an object from a Web server after sending a request?
TCP connection establishment
data transfer delay
Notation, assumptions:
Assume one link between client and server of rate R
Assume: fixed congestion window, W segments
S: MSS (bits)
O: object size (bits)
no retransmissions (no loss, no corruption)
Receiver has unbounded buffer

## Slide 51: TCP delay Modeling: simplified, fixed window
Case 1: WS/R > RTT + S/R:
ACK for first segment in window returns before window’s worth of data nsent
delay = 2RTT + O/R
Case 2: WS/R < RTT + S/R:
wait for ACK after sending window’s worth of data sent
delay = 2RTT + O/R
+ (K-1)[S/R + RTT - WS/R]
K:= O/WS

## Slide 52: TCP Delay Modeling: Slow Start
Example:
O/S = 15 segments
K = 4 windows
Q = 2
Server idles P = min{K-1,Q} = 2 times
Delay components:
2 RTT for connection estab and request
O/R to transmit object
time server idles due to slow start
Server idles: P = min{K-1,Q} times
where
Q = #times server stalls until cong. window is larger than a “full-utilization” window (if the object were of unbounded size).
- K = #(incremental-sized) congestion-windows that “cover” the object.

## Slide 53: TCP Delay Modeling (slow start - cont)

## Slide 54: TCP Delay Modeling
Calculation of Q, number of idles for infinite-size object,
is similar.
Recall K = number of windows that cover object
How do we calculate K ?