## Slide 1: Stream-Based Electricity Load Forecast
Authors:
Joao Gama
Pedro Pereira Rodrigues
Presented by:
Viktor Botev

## Slide 2: Problem area
Sensor data received at high speed
Dynamic and non-stationary environment
Companies buy and cell energy based on load profiles and forecasts
Load forecast in SCADA/DMS system help find critical points

## Slide 3: Existing methods
Forecasting using Adaptive neural networks (ANN)
Static iteration training for ANN is not applicable for high speed data
Predictive systems over thousands of sensor

## Slide 4: Solution presented
Incremental Clustering (Variable Clustering)
Incremental Learning of ANN
Other techniques for preprocessing and postprocessing
  Data aggregation engine
  Kalman Filter

## Slide 5: Technical goal
Incremental system to continuously predict in real time the electricity load demand
At time t:
  receive data from all sensors
  predict the sensor value of each sensor for time t+k
  back propagate the measurement corresponding to the prediction at t-k

## Slide 6: Preprocessing
Server based approach for:
  Gathering data from sensors
  Aggregation
  Synchronization
< date, time, sensor,measure, value >

## Slide 7: Clustering of Data Streams
Using ODAC algorithm (Online Divisive-Agglomerative Clustering)
  based on dissimilarities between streams
Similarity equation
  Pearson’s correlation coeﬃcient
Guarantees
  Hoeﬀding bounds

## Slide 8: Clustering of Data Streams
Building a clustering hierarchy
Measures taken for relax the assumption that
” In a hierarchical structure of clusters, considering that the data streams are produced by a stable concept, the intra-cluster dissimilarity should decrease with each split”

## Slide 9: Clustering of Data Streams

## Slide 10: MLP ANN predictive model
Time horizons
  1 hour
  24 hours
  168 hours
Muti-layered perceptron
  10 input neurons
  4 hidden neurons
  1 linear output
Input vector
  {1, 2, 3, 4}
  {7, 14}
  4 cyclic variables (sin + cos)

## Slide 11: MLP ANN predictive model How it works?
Read Buffer (size is defined by experts)
Structure – input into buffer, real value and old prediction comparison, input the ANN, store predictions, delete from buffer

## Slide 12: MLP ANN problems and solutions
Slow learning rate
  Propagating an example only once
Overfitting
  Dual perturb and combine algorithm
    Processing one example several times
    Adding noise to the examples
    Avaraging all the predictions produced
(Pesonal opinion is that the main reason for dealing with overfitting is convincing the companies)

## Slide 13: Improving predictions
Kalman Filter
  Simple one dimensional Kalman Filter
  Using for combining inexact measurement with inexact predictions
  Common technique is when at time t to predict value at time t-k

## Slide 14: Online learning and preprocessing
Missing data
  Accomodate homologue technique
Problems
  When sensors do not send data for a long time
Consequences
  Overfitting
  Concept damaging

## Slide 15: Evaluation and results
Test setup
  2500 sensors
  565 High Tension
  1629 Mean Tension
  299 Power Transformers
Measure of interest
  Current intensity
Data
  Gathered data for 3 years in an hourly bases
Quality measures of the forecasts
  MAPE (Mean Absolute Percentage Error)
  MEDAPE (Median Absolute Percentage Error)
Windows used
  Weekly
  Monthly

## Slide 16: Evaluation and results

## Slide 17: Evaluation and results

## Slide 18: Summary
We have discussed a system that can deal with large number of sensor data and predict their values within a given time horizon
The predictive model discussed eliminates the need for batch clustering and periodic ANN training
Future work could be adding more information in the model as temperature, holiday, and special events.

## Slide 19
Thank you