## Slide 1: Course on Computer Communication and Networks Lecture 1 & part of lecture 2 Chapter 1: Introduction
EDA344/DIT 420, CTH/GU

## Slide 2: Roadmap
what’s the Internet
  protocol layers
    Communication through layers
edge & core of any big network:
  types of service, ways of information transfer, routing
Internet layers & Logical vs physical communication
Performance:
  delays, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 3: the Internet: “nuts and bolts” view (1)
millions of connected computing devices: hosts = end systems
  running network apps
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers: forward packets (chunks of data)

## Slide 4: the Internet: “nuts and bolts” view (2)
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, Ethernet
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Home network
Institutional network
Mobile network
Global ISP
Regional ISP

## Slide 5: the Internet: service view
communication infrastructure enables distributed applications:
  Web, VoIP, email, games, e-commerce, file sharing
communication services provided to apps:
  reliable data delivery from source to destination
  “best effort” (unreliable) data delivery
Internet standards
RFC: Request for comments
IETF: Internet Engineering Task Force

## Slide 6: Roadmap
what’s the Internet
  protocol layers
    Communication through layers
edge & core of any big network:
  types of service, ways of information transfer, routing
Internet layers & Logical vs physical communication
Performance:
  delays, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 7
Networks are complex
many “pieces”:
  hosts
  routers
  links of various media
  applications
  hardware, software
Question:
Is there any hope of organizing structure, study, development of networks?

## Slide 8: Layers of abstraction
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance/es
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system

## Slide 9: Terminology: Protocols, Interfaces
Each layer offers services to the upper layers (shielding from the implementation details)
  service interface: across layers in same host
Layer n on a host carries a conversation with layer n on another host
  host-to-host interface: defines messages exchanged with peer entity
Network architecture (set of layers, interfaces) vs protocol stack (protocol implementation)

## Slide 10: What’s a protocol?
a human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
req.
TCP connection
reply.
Get http://gaia.cs.umass.edu/index.htm
<file>
time
host-to-host interface: defines
messages exchanged with peer entity: format, order of msgs sent and received among network entities
actions taken on msg transmission, receipt

## Slide 11: Roadmap
what’s the Internet
  protocol layers
    Communication through layers
edge & core of any big network:
  types of service, ways of information transfer, routing
Internet layers & Logical vs physical communication
Performance:
  delays, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 12: A closer look at (any big) network’s structure:
network edge: applications and hosts
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks

## Slide 13: The network edge:
end systems (hosts):
run application programs e.g. in Internet Web, email, …
… based on network services available at the edge
Basic types of service offered by the network to applications:
  connection-oriented: reliable delivery of the data in the order they are sent
  connectionless: “best effort” delivery of the data in arbitrary order
Q: can we think of more types of service?

## Slide 14: The Network Core
mesh of interconnected routers
fundamental question: how is data transferred through net?
  packet-switching: data sent thru net in discrete “chunks”

## Slide 15: Network Core: Packet Switching
A
B
C
10 Mbs
Ethernet
1.5 Mbs
45 Mbs
D
E
queue of packets
waiting for output
link
each end-end data stream divided into packets
packets share network resources
resources used as needed
store and forward:
packets move one hop at a time
  transmit over link; wait turn at next link
http://www.youtube.com/watch?v=O7CuFlM4V54
nice animation; note some of the terms in narration are not accurate (wrt protocol specifications)

## Slide 16: Packet-switched networks: routing
What is routing’s goal? find routes from source to destination
  (Challenge 1) path selection algorithms
  (Challenge2) Important design issue/type of service offered:
    datagram network:
      destination address determines next hop
      routes may change during session
    virtual circuit network:
      fixed path determined at call setup time, remains fixed thru session
      routers maintain per-call state

## Slide 17: Virtual circuits:
“source-to-dest path behaves almost like a physical circuit”
call setup, teardown for each call before data can flow
  signaling protocols to setup, maintain, teardown VC
every router maintains “state” for each passing connection
resources (bandwidth, buffers) may be allocated to VC
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 18: Network Taxonomy
Telecommunication
networks
Circuit-switched
networks
Packet-switched
networks
Networks
with VCs
Datagram
Networks
Datagram network (eg Internet) cannot be characterized either connection-oriented or connectionless.
  Internet provides both connection-oriented (TCP) and
connectionless services (UDP), at the network edge, to apps.

## Slide 19: Roadmap
what’s the Internet
  protocol layers
    Communication through layers
edge & core of any big network:
  types of service, ways of information transfer, routing
Internet layers & Logical vs physical communication
Performance:
  delays, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 20: Layering – Some “histrory”: The OSI Reference Model
ISO (International Standards Organization) defined the OSI (Open Systems Inerconnect) model to help vendors create interoperable network implementation
Reduced the problem into smaller and more manageable problems: 7 layers
  a layer should be created where a different level of abstraction is needed; each layer should perform a well defined function)
  The function of each layer should be chosen with an eye toward defining internationally standardized protocols
``X dot" series (X.25, X. 400, X.500) OSI model implementation (protocol stack)
Did not really “fly”…

## Slide 21: Internet protocol stack
application: ftp, smtp, http, etc
transport:
  connection-oriented, reliable data delivery from source to destination (TCP);
  connectionless, “best effort” (unreliable) data delivery (UDP)
network: routing of datagrams from source to destination; best effort service
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, WiFi, …
physical: bits “on the physical medium”
application
transport
network
link
physical

## Slide 22: Internet protocol stack
Architecture simple but not as thoroughly thought as OSI‘s
  no clear distinction between interface-design and implementations;
  hard to re-implement certain layers
Successful protocol suite (de-facto standard)
  was there when needed (OSI implementations were too complicated)
  freely distributed with UNIX

## Slide 23: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
Each layer:
distributed
“entities” implement layer functions at each node
entities perform actions, exchange messages with peers

## Slide 24: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
take data from app
add addressing, form “datagram”
send datagram to peer
(possibly wait for peer to ack receipt)
data
transport
transport
ack

## Slide 25: Layering: physical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 26: Protocol layering and data
Each layer takes data from above
adds header information to create new data unit
passes new data unit to layer below
application
transport
network
link
physical
application
transport
network
link
physical
source
destination
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
message
segment
datagram
frame

## Slide 27: Roadmap
what’s the Internet
  protocol layers
    Communication through layers
edge & core of any big network:
  types of service, ways of information transfer, routing
Internet layers & Logical vs physical communication
Performance:
  delays, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 28: Delay in packet-switched networks
1. nodal processing:
  check bit errors
  determine output link
2. queuing
  time waiting at output link for transmission
  depends on congestion level of router
A
B
propagation
transmission
nodal
processing
queueing
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s

## Slide 29: Network Core: Circuit Switching
End-end resources reserved/dedicated for “call” (analogue telephony)
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required
A nice video for Circuit vs packet switching
  http://www.youtube.com/watch?v=Dq1zpiDN9k4&feature=related

## Slide 30: Visualize delays: Circuit, message, packet switching
store and forward behavior + other delays’ visualization (fig. from “Computer Networks” by A. Tanenbaum,)

## Slide 31: Packet switching versus classical circuit switching
1 Mbit link
each user/connection:
  100Kbps when “active”
  active 10% of time (bursty behaviour)
circuit-switching how many users/connections?:
  10
packet switching:
  with 35 users, probability > 10 active less than 0.0004 ( almost all of the time, same the queuing behaviour is as in circuit switching)
Packet switching allows more users to use the network!
N users
1 Mbps link
Hint: The probability of k out of n users active (p=0.1 in our example)

## Slide 32: Queueing delay (revisited) …
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite! Queues may grow unlimited, packets can be lost

## Slide 33: Related with delays… - packet loss - throughput

## Slide 34: Packet loss
queue (aka buffer) preceding link has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 35: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe

## Slide 36: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
link on end-end path that constrains end-end throughput
bottleneck link

## Slide 37: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link of R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10 (if fair))
in practice: Rc or Rs is often bottleneck

## Slide 38: … “Real” Internet delays and routes (1)…
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 39: …“Real” Internet delays and routes (2)…
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no reponse (probe lost, router not replying)
trans-oceanic
link

## Slide 40: Packet switching properties
PS: Good: Great for bursty data
  resource sharing
  no call setup
PS: Not so good? Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees are needed for some apps
  Some routing policies can help???
    Cf virtual circuit

## Slide 41: Roadmap
what’s the Internet
  protocol layers
    Communication through layers
edge & core of any big network:
  types of service, ways of information transfer, routing
Internet layers & Logical vs physical communication
Performance:
  delays, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 42: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Considerations:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 43: Dial-up Modem
telephone
network
Internet
home dial-up
modem
ISP modem
(e.g., AOL)
home
PC
central office
Uses existing telephony infrastructure
  Home is connected to central office
up to 56Kbps direct access to router (often less)
Can’t surf and phone at same time: not “always on”

## Slide 44: Digital Subscriber Line (DSL)
telephone
network
DSL
modem
home
PC
home
phone
Internet
DSLAM
Existing phone line:
splitter
Central Office:
multiplexer
  Also uses existing telephone infrastructure
    dedicated physical line to telephone central office
  Asymmertic: commonly up to 2.5 Mbps upstream; up to 24 Mbps downstream

## Slide 45
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
ISP
cable modem
termination system
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream transmission rate, 2 Mbps upstream transmission rate
network of cable, attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office
  Related: fiber to the home
Access net: cable network

## Slide 46: Institutional access: local area networks
local area network (LAN) connects end system to edge router
E.g. Ethernet:
  10 Mbs, 100Mbps, Gigabit Ethernet
deployment: institutions, home LANs
(a lot more on this later in the course)

## Slide 47: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”, or “adhoc”
wireless LANs:
  802.11b/g (WiFi): 11 or 54 Mbps
wider-area wireless access
  provided by telco operator
  ~1Mbps over cellular system
  WiMAX (10’s Mbps) over wide area
base
station
mobile
hosts
router
(a lot more on this later in the course)

## Slide 48: Home networks
Typical home network components:
DSL or cable modem or Fiber to the home
router/firewall/NAT
Ethernet
wireless access point
wireless
access
Point (54 Mbps)
wireless
devices
router/
Firewall
NAT
Cable or DSL
modem
to/from
cable
headend
Ethernet

## Slide 49: Physical Media
physical link: transmitted data bit propagates across link
  guided media:
    signals propagate in solid media: copper, fiber
  unguided media:
    signals propagate freely e.g., radio

## Slide 50: Physical media: wireless
signal carried in electromagnetic spectrum
Omnidirectional: signal spreads, can be received by many antennas
Directional: antennas communicate with focused el-magnetic beams and must be aligned (requires higher frequency ranges)
propagation environment effects:
  reflection
  obstruction by objects
  interference

## Slide 51: Wireless: properties Attenuation, Multipath propagation
Signal can fade with distance, can get obstructed, can take many different paths between sender and receiver due to reflection, scattering, diffraction
signal at sender
signal at receiver

## Slide 52: Physical Media: coax, fiber, twisted pair
Coaxial cable:
wire (signal carrier) within a wire (shield)
  baseband: single channel on cable (common use in 10Mbs Ethernet)
  broadband: multiple channels multiplexed on cable(commonly used for cable TV)
Fiber optic cable:
glass fiber carrying light pulses
low attenuation
high-speed operation:
  100Mbps Ethernet
  high-speed point-to-point transmission (e.g., 5 Gps)
low error rate
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5 TP: more twists, higher insulation: high-speed Ethernet

## Slide 53: Roadmap
what’s the Internet
  protocol layers
    Communication through layers
edge & core of any big network:
  types of service, ways of information transfer, routing
Internet layers & Logical vs physical communication
Performance:
  delays, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 54: Internet structure: network of networks
roughly hierarchical
national/international backbone providers (NBPs)- tier 1 providers
  e.g. BBN/GTE, Sprint, AT&T, IBM, UUNet/Verizon, TeliaSonera
  interconnect (peer) with each other privately, or at public Network Access Point (NAPs: routers or NWs of routers)
regional ISPs, tier 2 providers
  connect into NBPs; e.g. Tele2
local ISP, company
  connect into regional ISPs
NBP A
NBP B
NAP
NAP
regional ISP
regional ISP
local
ISP
local
ISP

## Slide 55: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other.

## Slide 56: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 57: Internet structure: network of networks
a packet passes through many networks
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 58: Roadmap
what’s the Internet
  protocol layers
    Communication through layers
edge & core of any big network:
  types of service, ways of information transfer, routing
Internet layers & Logical vs physical communication
Performance:
  delays, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 59: Network Security
The field of network security is about:
  how adversaries can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  Security considerations in all layers!

## Slide 60: Bad guys can put malware into hosts via Internet
Malware can get in host from a virus, worm, or trojan horse.
Spyware malware can record keystrokes, web sites visited, upload info to collection site.
Infected host can be enrolled in a botnet, used for spam and DDoS attacks.
Malware is often self-replicating: from an infected host, seeks entry into other hosts

## Slide 61: Example types of malware
Trojan horse
  Hidden part of some otherwise useful software
  Today often on a Web page (Active-X, plugin)
Virus
  infection by receiving object (e.g., e-mail attachment), actively executing
  self-replicating: propagate itself to other hosts, users
Worm:
  infection by passively receiving object that gets itself executed
  self- replicating: propagates to other hosts, users
Sapphire Worm: aggregate scans/sec
in first 5 minutes of outbreak (CAIDA, UWisc data)

## Slide 62: Bad guys can attack servers and network infrastructure
Denial of service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
select target
break into hosts around the network (see botnet)
send packets toward target from compromised hosts
target

## Slide 63: The bad guys can sniff packets
Packet sniffing:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords) passing by
A
B
C
src:B dest:A payload
  Wireshark software used for end-of-chapter labs is a (free) packet-sniffer

## Slide 64: The bad guys can use false source addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload

## Slide 65: The bad guys can record and playback
record-and-playback: sniff sensitive info (e.g., password), and use later
  password holder is that user from system point of view
A
B
C
src:B dest:A user: B; password: foo

## Slide 66: Roadmap
what’s the Internet
  protocol layers
    Communication through layers
edge & core of any big network:
  types of service, ways of information transfer, routing
Internet layers & Logical vs physical communication
Performance:
  delays, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 67: Chapter 1: Summary
Covered a “ton” of material!
what’s the Internet
what’s a protocol?
protocol layers, service models
network edge (types of service)
network core (ways of transfer, routing)
performance, delays, loss
access net, physical media
backbones, NAPs, ISPs
Security concerns
(history: read more corresponding section, interesting & fun )
You now hopefully have:
context, overview, “feel” of networking
A point of reference for context in the focused discussions to come

## Slide 68: Reading instructions
Careful | Quick
4/e,5/e,6/e: 1.3, 1.4, 1.5 | 4/e,5/e,6/e: the rest
1. Kurose Ross book
Extra Reading (optional)
Computer and Network Organization: An Introduction,
by Maarten van Steen and Henk Sips, Prentice Hall
(very good introductory book for non-CSE students

## Slide 69: Review questions
Review questions from Kurose-Ross book, chapter 1 (for basic study)
R11, R12, R13, R16, 17, R18, R19, R20, R21, R22, R23, R24, R25, R28.
Extra questions, for further study: delay analysis in packet switched networks:
http://www.comm.utoronto.ca/~jorg/teaching/ece466/material/466-SimpleAnalysis.pdf