## Slide 1: An Introduction to Software-Defined Networking (SDN)
Zhang Fu

## Slide 2: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
SDN components
Use cases
Challenges and research problems
Little bite of Openflow

## Slide 3: Reviewing traditional networking
Network layers
Application layer
transport layer
network layer
Data-link layer
physical layer
Application layer
transport layer
network layer
Data-link layer
physical layer
source
destination
Why layers? Good abstraction, transparency…

## Slide 4: Reviewing traditional networking
Design principles of Internet
  Simple
  Intelligent end-points
  Distributed control
Resulting in huge complex network and hard to manage
Billions of computers
Tens of thousands of ASes
Great business for selling routers

## Slide 5: Reviewing traditional networking
Complex routers
Million of lines of source code
Hard to extend
Tens of billions of transistors
10Gbytes RAM
Power Hungry
Vertically integration with many complex functions: OSPF, BGP, multicast, QoS, Traffic Engineering, NAT, firewalls, MPLS…
Hardware
Router
Software

## Slide 6: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
SDN components
Use cases
Challenges and research problems
Little bite of Openflow

## Slide 7: Example: oscillation problem
Link cost equals the amount of carried traffic
A
D
C
B
1
1+e
e
0
e
1
1
0
0
initially
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
A
D
C
B
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
How to achieve optimal routing dynamically?

## Slide 8: Example: mitigating attacks
Checking the validity of packets by middle boxes
Internet
How to route the packets through a series of middle boxes?

## Slide 9: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
SDN components
Use cases
Challenges and research problems
Little bite of Openflow

## Slide 10: Software development VS Network diagnosing
Various tools for code analysis, verification, debugging
Software Specification
Testing
Coding
Diagnosing tools? Ping, traceroute, SNMP
Networking Specification
Testing ?
Coding ?
The life cycle for network protocols is much longer than that for software
Timely research does not find its way into practice

## Slide 11: Network substrate
We want to mimic the success in software industry
  Has simple common substrate
  Building OS on top the hardware, which enables easy deployment of networking applications
SDN
A network in which the control plane is physically separate from the data plane.
A single control plane controls several forwarding devices.

## Slide 12: Separate data and control plane
hardware
software
hardware
software
hardware
software
hardware
software

## Slide 13: Separate data and control plane
hardware
hardware
hardware
hardware
software
software
software
software
Control plane

## Slide 14: Separate data and control plane
hardware
hardware
hardware
hardware
Control plane

## Slide 15: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
SDN components
Use cases
Challenges and research problems
Little bite of Openflow

## Slide 16: SDN architecture

## Slide 17: SDN architecture
The data plane consists of network elements, which expose their capabilities to the control plane via southbound interface
The SDN applications are in the application plane and communicate their network requirements toward the control plane via northbound interface
The control plane sits in the middle
  translate the applications’ requirements and exerts low-level control over the network elements
  Provide network information to the applications
  Orchestrate different applications

## Slide 18: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
SDN components
Use cases
Challenges and research problems
Little bite of Openflow

## Slide 19: Data-plane
Data sources and sinks
Traffic forwarding/processing engine
  May have the ability to handle some types of protocols
Provide interfaces communicating to the control plane
  Programmatic control of all functions offered by the network element
  Capability advertisement
  Event notification

## Slide 20: Control-plane
Logically centralized
Core functionality
  Topology and network state information
  Device discovery
  Path computation
  Security mechanism
Coordination among different controllers
Interfaces to the application plane

## Slide 21: Application-plane
Applications specify the resources and behaviors required from the network, with the context of business and policy agreement
It may need to orchestrate multiple-controllers to achieve the objectives
Programming languages help developing applications, e.g. Pyretic, FatTire,etc.

## Slide 22: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
SDN components
Use cases
Challenges and research problems
Little bite of Openflow

## Slide 23: Use cases
Traffic engineering
Mobility and wireless
Security
Data center networking

## Slide 24: Example: routing
App: build path
<a,b,QoS>
Controller:
Find path <a,b>,
set QoS requirements,
Commands to devices
Devices:
Configure hardware,
Installing forwarding rules
Internet

## Slide 25: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
SDN components
Use cases
Challenges and research problems
Little bite of Openflow

## Slide 26: Challenges and research problems
Switch design
  Find common abstraction
  Flow table capacity
  Throughput
Controller platform
  Distributed vs centralized
  Flexibility
Dependability and security
  Attack to data plane
  Attack to control plane
  Trust, privacy issues

## Slide 27: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
SDN components
Use cases
Challenges and research problems
Little bite of Openflow

## Slide 28: Openflow
An southbound standard:
Provide specification to implement Openflow-enabled forwarding devices
Communication channel between data and control plane

## Slide 29: Mininet
Provide tools to create virtualized network with OVS
CLI for manipulating network dynamically
Virtualized hosts
CONTROLLER
Virtual
Switch
Virtual
Switch
h
h
h
h
Openflow traffic
App

## Slide 30: References
"The road to SDN" http://queue.acm.org/detail.cfm?ref=rss&id=2560327
Kreutz, D., Ramos, F. M., Verissimo, P. E., Rothenberg, C. E., Azodolmolky, S., & Uhlig, S. (2015). Software-defined networking: A comprehensive survey.proceedings of the IEEE, 103(1), 14-76.
“SDN Architecture 1.0 - Open Networking Foundation”, https://www.opennetworking.org/images/stories/downloads/sdn-resources/technical-reports/TR_SDN_ARCH_1.0_06062014.pdf
Openflow specification v1.0, https://www.opennetworking.org/images/stories/downloads/sdn-resources/onf-specifications/openflow/openflow-spec-v1.0.0.pdf
Mininet, mininet.org
POX controller, http://www.noxrepo.org/