## Slide 1: Course on Computer Communication and Networks Lecture 2-cont Chapter 2 (part a): applications, http
EDA344/DIT 420, CTH/GU

## Slide 2: Chapter 2: Application Layer
Chapter goals:
conceptual + implementation aspects of network application protocols
  client server, p2p paradigms (we will study the latter seperately)
  service models
learn about protocols by examining basic application-level protocols (more will come later, when studying real-time traffic aspects)
specific protocols:
  http, (ftp), smtp, pop, dns, p2p file sharing
programming network applications
  socket programming

## Slide 3: Roadmap
Applications and their needs, vs Internet trasport layer services
The http protcocol
  General description and functionality
  Authentication, cookies and related aspects
  Caching andp roxies
(continuation with more applications: next lecture)

## Slide 4: Applications and application-layer protocols
Application: communicating, distributed processes
  running in network hosts in “user space”
  exchange messages
  e.g., email, file transfer, the Web
Application-layer protocols
  Are only one “piece” of an application -others are e.g. user agents.
    Web:browser
    E-mail: mail reader
    streaming audio/video: media player
  define messages exchanged by apps and actions taken
  use services provided by lower layer protocols
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 5: Client-server paradigm
Typical network app has two pieces: client and server
application
transport
network
data link
physical
application
transport
network
data link
physical
Client:
initiates contact with server (“speaks first”)
typically requests service from server,
for Web, client is implemented in browser; for e-mail, in mail reader
Server:
provides requested service to client
e.g., Web server sends requested Web page, mail server delivers e-mail
request
reply

## Slide 6: Auxiliary terms ++
socket: Internet application programming interface
  2 processes communicate by sending data into socket, reading data out of socket (like sending out, receiving in via doors)
Q: how does a process “identify” the other process with which it wants to communicate?
  IP address of host running other process
  “port number” - allows receiving host to determine to which local process the message should be delivered
… more: later, withTCP/UDP + cf programming project guidelines

## Slide 7: Properties of transport service of interest to the app
Data loss
some apps (e.g., audio) can tolerate some loss
other apps (e.g., file transfer, telnet) require 100% reliable data transfer
Connection-oriented vs connectionless services
Bandwidth, Timing, Security
some apps (e.g., multimedia) require minimum amount of bandwidth
some apps (e.g., Internet telephony, interactive games) require low delay and/or low jitter
other apps (elastic apps, e.g. file transfer) make use of whatever bandwidth, timing they get
some apps also require confidentiality and integrity (more in network security)

## Slide 8: Transport service requirements of common apps
Application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video
interactive games
financial apps
Data loss
no loss
no loss
no-loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
Bandwidth
elastic
elastic
elastic
audio: 5Kb-1Mb
video:10Kb-5Mb
rather similar
few Kbps up
elastic
Time Sensitive
no
no
no
yes, 100’s msec
yes, few secs
yes, 100’s msec
yes and no

## Slide 9: Services by Internet transport protocols
TCP service:
connection-oriented: setup required between client, server
reliable transport between sending and receiving process
+ a bit more, to focus in the TCP study
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum bandwidth guarantees
UDP service:
connectionless
unreliable transport between sending and receiving process
does not provide: flow control, congestion control, timing, or bandwidth guarantee
Q: why bother? Why is there a UDP?

## Slide 10: Internet apps: their protocols
Application
e-mail
remote terminal access
Web
file transfer
streaming multimedia
remote file server
Internet telephony
nslookup and many others
Application
layer protocol
» smtp [RFC 821]
telnet [RFC 854]
» http [RFC 2068]
ftp [RFC 959]
proprietary
(e.g. RealNetworks)
NSF
SIP, RTP,
proprietary (e.g., Skype)
» DNS
[RFC 882, 883,1034,1035]
Underlying
transport protocol
TCP
TCP
TCP
TCP
TCP or UDP
TCP or UDP
typically UDP, TCP also possible
UDP

## Slide 11: Roadmap
Applications and their needs, vs Internet trasport layer services
The http protcocol
  General description and functionality
  Authentication, cookies and related aspects
  Caching andp roxies
(continuation with more applications: next lecture)

## Slide 12: The Web: some jargon
Web page:
  consists of “objects”
  addressed by a URL
Most Web pages consist of:
  base HTML page, and
  several referenced objects.
URL has two components: host name and path name:
User agent for Web is called a browser:
  MS Internet Explorer
  Netscape Communicator
Server for Web is called Web server:
  Apache (public domain)
  MS Internet Information Server
  Netscape Enterprise Server
www.someSchool.edu/someDept/pic.gif

## Slide 13: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
PC running
Firefox browser
server
running
Apache Web
server
iphone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 14: HTTP overview (continued)
uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 15: http example
Suppose user enters URL www.someSchool.edu/someDepartment/home.index
1a. http client initiates TCP connection to http server (process) at www.someSchool.edu. Port 80 is default for http server.
2. http client sends http request message (containing URL) into TCP connection socket
1b. http server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. http server receives request message, forms response message containing requested object (someDepartment/home.index), sends message into socket
time
(contains text,
references to 10
jpeg images)

## Slide 16: http example (cont.)
5. http client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. http server closes TCP connection.
time

## Slide 17: Non-persistent and persistent connections
Non-persistent
HTTP/1.0
server parses request, responds, and closes TCP connection
new TCP connection for each object => extra overhead per object
Persistent
default for HTTP/1.1
on same TCP connection: server parses request, responds, parses new request,..
Client sends requests for all referenced objects as soon as it receives base HTML;
Less overhead per object
Objects are fetched sequentially
But can also pipeline requests, to parallelize (resembles non-persistent optimised behaviour)
But most 1.0 browsers use
parallel TCP connections.

## Slide 18: http request message: general format

## Slide 19: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
request line
(GET, POST,
HEAD commands)
header
lines
carriage return,
line feed at start
of line indicates
end of header lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Firefox/3.6.10\r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Accept-Charset: ISO-8859-1,utf-8;q=0.7\r\n
Keep-Alive: 115\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character

## Slide 20: Method types
HTTP/1.0:
GET
POST
HEAD
  asks server to leave requested object out of response
HTTP/1.1:
GET, POST, HEAD
PUT
  uploads file in entity body to path specified in URL field
DELETE
  deletes file specified in the URL field

## Slide 21: HTTP response message
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
HTML file
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n
Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n
Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...
For more headers:
www.w3.org/Protocols/HTTP/1.1/draft-ietf-http-v11-spec-01.html

## Slide 22: http response status codes
200 OK
  request succeeded, requested object later in this message
301 Moved Permanently
  requested object moved, new location specified later in this message (Location:)
400 Bad Request
  request message not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
In first line in server->client response message.
A few sample codes:

## Slide 23: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80
(default HTTP server port) at cis.poly.edu.
anything typed in sent
to port 80 at cis.poly.edu
telnet cis.poly.edu 80
2. type in a GET HTTP request:
GET /~ross/ HTTP/1.1
Host: cis.poly.edu
by typing this in (hit carriage
return twice), you send
this minimal (but complete)
GET request to HTTP server
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)

## Slide 24: Roadmap
Applications and their needs, vs Internet trasport layer services
The http protcocol
  General description and functionality
  Authentication, cookies and related aspects
  Caching andp roxies
(continuation with more applications: next lecture)

## Slide 25: User-server interaction: authentication
Authentication goal: control access to server documents
http is stateless: client must present authorization in each request
authorization: typically name, password
  authorization: header line in request
  if no authorization presented, server refuses access, sends
    WWW authenticate:
    header line in response
client
server
usual http request msg
401: authorization req.
WWW authenticate:
usual http request msg
+ Authorization:line
usual http response msg
usual http request msg
+ Authorization:line
usual http response msg
time
Browser caches name & password so
that user does not have to repeatedly enter it.

## Slide 26: Cookies: keeping “state”
client
server
usual http request msg
usual http response +
Set-cookie: 1678
usual http request msg
cookie: 1678
usual http response msg
usual http request msg
cookie: 1678
usual http response msg
cookie-
specific
action
cookie-
spectific
action
server
creates ID
1678 for user
entry in backend
database
access
access
Cookie file
amazon: 1678
ebay: 8734
Cookie file
ebay: 8734
Cookie file
amazon: 1678
ebay: 8734
one week later:

## Slide 27: Cookies (continued)
cookies can bring:
authorization
shopping carts
recommendations
user session state
Cookies and privacy:
cookies permit sites to learn a lot about you
you may supply name and e-mail to sites
search engines use cookies to learn yet more
advertising companies obtain info across sites
aside

## Slide 28: Roadmap
Applications and their needs, vs Internet trasport layer services
The http protcocol
  General description and functionality
  Authentication, cookies and related aspects
  Caching and proxies
(continuation with more applications: next lecture)

## Slide 29: Conditional GET: client-side caching
Goal: don’t send object if client has up-to-date stored (cached) version
client: specify date of cached copy in http request
  If-modified-since: <date>
server: response contains no object if cached copy up-to-date:
  HTTP/1.0 304 Not Modified
client
server
http request msg
If-modified-since: <date>
http response
HTTP/1.0
304 Not Modified
object
not
modified
http request msg
If-modified-since: <date>
http response
HTTP/1.1 200 OK
…
<data>
object
modified

## Slide 30: Web Caches (proxy server)
user configures browser: Web accesses via web cache
client sends all http requests to web cache; the cache(proxy) server
  if object at web cache, return object in http response
  else request object from origin server (or from next cache), then return http response to client
Hierarchical, cooperative caching, ICP: Internet Caching Protocol (RFC2187)
Goal: satisfy client request without involving origin server
client
Proxy
server
client
http request
http request
http response
http response
http request
http response
http request
http response
origin
server
origin
server

## Slide 31: Why Web Caching?
Assume: cache is “close” to client (e.g., in same network)
smaller response time: cache “closer” to client
decrease traffic to distant servers
  link out of institutional/local ISP network often bottleneck
Important for large data applications (e.g. video,…)
Performance effect:
origin
servers
public
Internet
institutional
network
10 Mbps LAN
1.5 Mbps
access link
institutional
cache
E(delay)=hitRatio*LocalAccDelay + (1-hitRatio)*RemoteAccDelay

## Slide 32: Caching example:
origin
servers
public
Internet
institutional
network
100Mbps LAN
1.54 Mbps
access link
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
  i.e. avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
LAN utilization: 1.5%
access link utilization = 99%
total delay = Internet delay + access delay + LAN delay
= 2 sec + minutes + quite_small
problem!

## Slide 33: Caching example: faster access link
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
  i.e. avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
LAN utilization: 1.5%
access link utilization = 99%
total delay = Internet delay + access delay + LAN delay
= 2 sec + minutes + usecs
origin
servers
1.54 Mbps
access link
154 Mbps
154 Mbps
msecs
Cost: increased access link speed (not cheap!)
9.9%
public
Internet
institutional
network
100Mbps LAN

## Slide 34: Caching example: install local cache
institutional
network
100Mbps LAN
origin
servers
1.54 Mbps
access link
local web
cache
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
  i.e. avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
LAN utilization: 1.5%
access link utilization
total delay
?
?
How to compute link
utilization, delay?
Cost: web cache (cheap!)
public
Internet

## Slide 35: Caching example: install local cache
Calculating access link utilization, delay with cache:
suppose cache hit rate is 0.4
  40% requests satisfied at cache, 60% requests satisfied at origin
origin
servers
1.54 Mbps
access link
access link utilization:
  60% of requests use access link
data rate to browsers over access link = 0.6*1.50 Mbps = .9 Mbps
  utilization = 0.9/1.54 = .58
total delay
  = 0.6 * (delay from origin servers) +0.4 * (delay when satisfied at cache)
  = 0.6 (2.01) + 0.4 (~msecs)
  = ~ 1.2 secs
  less than with 154 Mbps link (and cheaper too!)
public
Internet
institutional
network
100Mbps LAN
local web
cache

## Slide 36: Roadmap
Applications and their needs, vs Internet trasport layer services
The http protcocol
  General description and functionality
  Authentication, cookies and related aspects
  Caching andp roxies
(continuation with more applications: next lecture)