## Slide 1: Chapter 5: DataLink Layer
Course on Computer Communication and Networks, CTH/GU
The slides are adaptation of the slides made available by the authors of the course’s main textbook
Slides with darker background are for extra information or background/context

## Slide 2: Link layer: context
Datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
Each link protocol provides different services
  e.g., may or may not provide RDT over link
transportation analogy
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 3: Where is the link layer implemented?
in each and every host
link layer implemented in “adapter” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical

## Slide 4: Adapters communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, RDT, flow control, etc.
receiving side
  looks for errors, RDT, flow control, etc
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 5: Link layer services
framing, link access:
  encapsulate datagram into frame (header, trailer)
    Link-layer addresses in frame headers to identify source, dest
      different from IP address!
  channel access if shared medium
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
    seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates; error detection and correction applicable
error detection:
  receiver detect errors caused by signal attenuation, noise.
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
flow control:
  pacing between adjacent sending and receiving nodes

## Slide 6: Link Layer
5.1 Introduction and services
5.3 Multiple access protocols
(5.2 Error detection and correction )
*grey items will be treated as complement, in subsequent lecture
LAN technology
5.4.2 Ethernet
5.4.3 Interconnection
5.4.1 Link-Layer Addressing
5.7 A day in the life of a web request
5.5 Link Virtualization: ATM and MPLS)

## Slide 7: access links, protocols
two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch, host
broadcast (shared wire or medium), eg
  old-fashioned Ethernet
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 8: i.e. (Multiple access)
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 9: An ideal multiple access protocol
given: broadcast channel of rate R bps
desired outcome:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple

## Slide 10: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 11: Channel Partitioning MAC protocols: TDMA, FDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
  example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle
FDMA: frequency division multiple access
each station assigned fixed frequency band
unused transmission time in frequency bands goes idle
  example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
frequency bands

## Slide 12: Channel Partitioning CDMA
CDMA: Code Division Multiple Access
allows each station to transmit over the entire frequency spectrum all the time.
simultaneous transmissions are separated using coding theory.
used mostly in wireless broadcast channels (cellular, satellite, etc) – we will study it in the wireless context
has been ”traditionally” used in the military
Observe:
MUX = speak person-to-person in designated space
CDMA = ”shout” using different languages: the ones who know the language will get what you say

## Slide 13: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 14: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 15: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only at slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame (from upper layer protocol), it transmits in next slot
  if no collision: ok
  if collision: node retransmits frame in each subsequent slot with prob. p until success

## Slide 16: Slotted ALOHA
Pros
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons
collisions, wasting slots
idle slots
clock synchronization

## Slide 17: Slotted Aloha efficiency
Q: max fraction of
successful transmissions?
A: Suppose N stations, each transmits in slot with probability p
  prob. successful transmission is:
  P[specific node succeeds]= p (1-p)(N-1)
  P[any of N nodes succeeds]
= N p (1-p)(N-1)
Efficiency : long-run fraction of successful slots (many nodes, all with many frames to send)

## Slide 18: Pure Aloha vs slotted Aloha
P(success by any of N nodes) = N p . (1-p)2N =
i.e. N p P(no other node transmits in [p0-1,p0] .
P(no other node transmits in [p0,p0+1]
=(as n -> infty …)
1/(2e) = .18
S = throughput = “goodput”
(success rate)
G = offered load = #frames per frame-time
0.5
1.0
1.5
2.0
0.1
0.2
0.3
0.4
Pure Aloha
Slotted Aloha

## Slide 19: CSMA: Carrier Sense Multiple Access
CSMA: listen before transmit:
If channel sensed busy, defer transmission
  back-off, random interval
If/when channel sensed idle:
  p-persistent CSMA: transmit immediately with probability p; with probablility 1-p retry after random interval
  non-persistent CSMA: transmit after random interval
human analogy: don’t interrupt others!

## Slide 20: CSMA collisions
collisions can occur:
Due to propagation delay, two nodes may not hear each other’s transmission
collision:
entire packet transmission
time wasted
spatial layout of nodes along ethernet
note:
role of distance and propagation delay (d)in determining collision
(collision-detection delay <= 2d)

## Slide 21: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
colliding transmissions aborted, reducing channel wastage
persistent or non-persistent retransmission
collision detection:
easy in wired LANs: measure signal
  strengths, compare transmitted,
  received signals
different in wireless LANs:
  transmitter/receiver not “on”
  simultaneously; collision at the
  receiver matters, not the sender
human analogy: the polite
conversationalist

## Slide 22: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 23: Trade-off in MAC:
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, bandwidth allocated even if only 1 active node!
Random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 24: “Taking Turns” MAC protocols
Token passing:
control token-frame passed from one node to next sequentially.
not pure broadcast
concerns:
  token overhead
  latency
  single point of failure (token)
other: token bus, take-turns + reservation; see extra slides @ end of lecture

## Slide 25: Summary of MAC protocols
What do you do with a shared media?
  Channel Partitioning, by time, frequency or code
    Time Division, Frequency Division
  Random partitioning (dynamic),
    ALOHA, S-ALOHA, CSMA, CSMA/CD
    carrier sensing: easy in some technologies (wire), hard in others (wireless)
    CSMA/CD used in Ethernet
    CSMA/CA used in 802.11 (to be studied in wireless)
  Taking Turns
    polling, token passing
    Bluetooth, FDDI, IBM Token Ring

## Slide 26: Link Layer
5.1 Introduction and services
5.3Multiple access protocols
(5.2 Error detection and correction )
*grey items will be treated as complement, in subsequent lecture
LAN technology
5.4.2 Ethernet
5.4.3 Interconnection
5.4.1 Link-Layer Addressing
5.7 A day in the life of a web request
5.5 Link Virtualization: ATM and MPLS)

## Slide 27: Ethernet
“dominant” wired LAN technology:
cheap $20 for 100Mbs!
first widely used LAN technology
Simpler, cheaper than token LANs and ATM
Kept up with speed race: 10 Mbps – 100 Gbps
Metcalfe’s Ethernet
sketch

## Slide 28: Ethernet: uses CSMA/CD
A: sense channel, if idle
  then {
  transmit and monitor the channel;
      If detect another transmission
      then {
      abort and send jam signal;
        update # collisions;
        delay as required by exponential backoff algorithm;
        goto A
        }
      else {done with the frame; set collisions to zero}
    }
  else {wait until ongoing transmission is over and goto A}

## Slide 29: Ethernet’s CSMA/CD (more)
Jam Signal: make sure all other transmitters are aware of collision; 48 bits;
Exponential Backoff:
Goal: adapt retransmission attempts to estimated current load
  heavy load: random wait will be longer
first collision: choose K from {0,1}
  (delay is K x frame-transmission time)
after m (<10) collisions: choose K from {0,…, 2^m}…
after ten or more collisions, choose K from {0,1,2,3,4,…,1023}

## Slide 30: Ethernet (CSMA/CD) Limitation
Recall: collision detection interval = 2*Propagation delay along the LAN
This implies a minimum frame size and/or a maximum wire length
Critical factor:
  a = 2 * propagation_delay / frame_transmission_delay

## Slide 31: Star topology
bus topology popular through mid 90s
  all nodes in same collision domain (can collide with each other)
today: star topology prevails (more bps, shorter distances)
  Hub or active switch in center
  (more in a while)
switch
bus: coaxial cable
star

## Slide 32: Ethernet Frame Structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Preamble: 7 bytes with pattern 10101010 followed by one byte with pattern 10101011
  to synchronize receiver and sender clock rates
Addresses: 6 bytes, frame is received by all adapters on a LAN and dropped if address does not match
Type: indicates the higher layer protocol, mostly IP but others may be supported
CRC: checked at receiver, if error is detected, the frame is simply dropped

## Slide 33: 802.3 Ethernet Standards: Link & Physical Layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10G bps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twisted
pair) physical layer

## Slide 34: Ethernet: Unreliable, connectionless
connectionless: No handshaking between sending and receiving NICs
unreliable: receiving NIC doesn’t send acks or nacks to sending NIC
  stream of datagrams passed to network layer can have gaps (missing datagrams)
  gaps will be filled if app is using TCP
  otherwise, app will see gaps

## Slide 35: Link Layer
5.1 Introduction and services
5.3Multiple access protocols
(5.2 Error detection and correction )
*grey items will be treated as complement, in subsequent lecture
LAN technology
5.4.2 Ethernet
5.4.3 Interconnection
5.4.2 Link-Layer Addressing
5.7 A day in the life of a web request
5.5 Link Virtualization: ATM and MPLS)

## Slide 36: Interconnecting with hubs
Hubs are essentially physical-layer repeaters:
  bits coming from one link go out all other links
  at the same rate (no frame buffering)
no CSMA/CD at hub: adapters detect collisions (one large collision domain)
Extends distance between nodes
Can’t interconnect different standards, e.g. 10BaseT & 100BaseT
hub
hub
hub
hub
http://www.youtube.com/watch?v=reXS_e3fTAk&feature=related (video link)

## Slide 37: Switch: multiple simultaneous transmissions
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
forwarding: how to know LAN segment on which to forward frame?
  looks like a routing problem…

## Slide 38: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 39: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */

## Slide 40: Switch Learning: example
Suppose C sends a frame to D and D replies with a frame to C
C sends frame, switch has no info about D, so floods
  switch notes that C is on port 1
  frame ignored on upper LAN
  frame received by D
D generates reply to C, sends
  switch sees frame from D
  switch notes that D is on interface 2
  switch knows C on interface 1, so selectively forwards frame out via interface 1
switch

## Slide 41: Switch: traffic isolation
switch installation breaks subnet into LAN segments
switch filters packets:
  same-LAN-segment frames not usually forwarded onto other LAN segments
  segments become separate collision domains
hub
hub
hub
switch
collision domain
collision domain
collision domain

## Slide 42: Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 43: Summary comparison

## Slide 44: Link Layer
5.1 Introduction and services
5.3Multiple access protocols
(5.2 Error detection and correction )
*grey items will be treated as complement, in subsequent lecture
LAN technology
5.4.2 Ethernet
5.4.3 Interconnection
5.4.1 Link-Layer Addressing
5.7 A day in the life of a web request
5.5 Link Virtualization: ATM and MPLS)

## Slide 45: LAN Addresses
32-bit IP address:
network-layer address
used to get datagram to destination network (recall IP network definition)
LAN (or MAC or physical) address:
to get datagram from
  one interface to another
  physically-connected
  interface (same network)
48 bit MAC address
  (for most LANs)
  burned in NIC’s ROM
  (sometimes configurable)
Broadcast address =
FF-FF-FF-FF-FF-FF

## Slide 46: LAN Address (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
(a) MAC address: like People’s Names or PersonalNum’s
(b) IP address: like postal address
MAC flat address => portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  depends on network to which one attaches

## Slide 47: Recall earlier routing discussion
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
look up net. address of B, find B on same net. as A
link layer sends datagram to B inside link-layer frame
A’s MAC
addr
B’s MAC
addr
A’s IP
addr
B’s IP
addr
IP payload
datagram
frame
frame source,
dest address
datagram source,
dest address

## Slide 48: ARP: Address Resolution Protocol
Each IP node (Host, Router) on LAN has ARP table
  ARP Table: IP/MAC address mappings
    < IP address; MAC address; TTL>
  < ………………………….. >
    TTL (Time To Live): time to cache (typically 20 min); afterwards:
  A broadcasts ARP query pkt, containing B's IP address
  B receives ARP packet, replies to A with its (B's) physical layer address
  A caches (saves) IP-to-physical address pairs until they time out
    soft state: information that times out (goes away) unless refreshed
Question: how to determine
MAC address of B
given B’s IP address?
Broadcast address =
FF-FF-FF-FF-FF-FF

## Slide 49: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
assume A knows B’s IP address
two ARP tables in router R, one for each IP network (LAN)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
A
74-29-9C-E8-FF-55
222.222.222.221
88-B2-2F-54-1A-0F
B
222.222.222.222
49-BD-D2-C7-56-2A

## Slide 50
A creates IP datagram with source A, destination B
  Network layer finds out I should be forwarded to R
A uses ARP to get R’s MAC address for 111.111.111.110
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
A’s NIC sends frame
R’s NIC receives frame
R removes IP datagram from Ethernet frame, sees its destined to B
R uses ARP to get B’s MAC address
R creates frame containing A-to-B IP datagram; sends to B
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
A
74-29-9C-E8-FF-55
222.222.222.221
88-B2-2F-54-1A-0F
B
222.222.222.222
49-BD-D2-C7-56-2A
This is a really important
example – make sure you
understand!

## Slide 51: Link Layer
5.1 Introduction and services
5.3Multiple access protocols
(5.2 Error detection and correction )
*grey items will be treated as complement, in subsequent lecture
LAN technology
5.4.2 Ethernet
5.4.3 Interconnection
5.4.1 Link-Layer Addressing
5.7 A day in the life of a web request
5.5 Link Virtualization: ATM and MPLS)

## Slide 52: Review questions for this part
  Why both link-level and end-end reliability?
Medium access methods: how they work, pros and cons
  Partitioning
  Random access
  Reservation
Aloha vs CSMA/CD
Ethernet: protocol, management of collisions, connections
Switches vs routers
Addressing in link layer

## Slide 53: Extra slides/topics

## Slide 54: IEEE 802.4 Standard (General Motors Token Bus) (not in must-study material)
Contention systems limitation: worst-case delay until successful transmission is unlimited => not suitable for real-time traffic
Solution: token-passing, round robin
token = special control frame; only the holding station can transmit; then it passes it to another station, i.e. for token bus, the next in the logical ring
4 priority classes of traffic, using timers
Logical ring-maintenance: distributed strategy
  Robust, somehow complicated though

## Slide 55: IEEE Standard 802.5 (Token Ring) (not in must-study material)
Motivation: instead of complicated token-bus, have a physical ring
Principle: Each bit arriving at an interface is copied into a 1-bit buffer (inspected and/or modified); then copied out to the ring again.
  copying step introduces a 1-bit delay at each interface.

## Slide 56: Token Ring operation
to transmit a frame, a station is required to seize the token and remove it from the ring before transmitting.
bits that have propagated around the ring are removed from the ring by the sender (the receiver in FDDI).
After a station has finished transmitting the last bit of its frame, it must regenerate the token.

## Slide 57: IEEE 802.5 Ring: Maintenance (not in must-study material)
Centralised: a “monitor” station oversees the ring:
generates token when lost
cleans the ring when garbled/orphan frames appear
If the monitor goes away, a convention protocol ensures that another station is elected as a monitor (e.g. the one with highest identity)
If the monitor gets ”mad”, though…..

## Slide 58: IEEE 802.5 Ring: Priority Algorithm (not in must-study material)
Station S
upon arrival of frame f:
  set prior(f) := max{prior(f), prior(S)}
  forward(f)
upon arrival of T
  if prior(T)>prior(S) then forward(T)
  else send own frame f with prior(f):=0
    wait until f comes back
    prior(T):=prior(f)
    forward(T)

## Slide 59: Reservation-based protocols
Distributed Polling – Bit-map protocol:
time divided into slots
begins with N short reservation slots
  station with message to send posts reservation during its slot
  reservation seen by all stations
  reservation slot time equal to channel end-end propagation delay (why?)
after reservation slots, message transmissions ordered by known priority

## Slide 60: Switches (bridges): cont.
Link Layer devices: operate on frames, examining header and selectively forwarding frame based on its destination
  filtering: same-LAN-segment frames not forwarded to other seg’s
Advantages:
  Isolates collision domains:
    higher total max throughput
    no limit on number of nodes nor distances
  Can connect different net-types (translational, …)
  Transparent: no need for any change to hosts LAN adapters
forwarding: how to know LAN segment on which to forward frame?
  looks like a routing problem…
switch