## Slide 1: Chapter 7 Multimedia networking + (ch 3-5) VC networks Congestion control
Course on Computer Communication and Networks, CTH/GU
The slides are adaptation of the slides made available by the authors of the course’s main textbook

## Slide 2
multimedia applications: network audio and video
(“continuous media”)

## Slide 3: Multimedia: audio
analog audio signal sampled at constant rate
  telephone: 8,000 samples/sec
  CD music: 44,100 samples/sec
example: 8,000 samples/sec, 256 quantized values: 64,000 bps
receiver converts bits back to analog signal:
  some quality reduction
example rates
CD: 1.411 Mbps
MP3: 96, 128, 160 kbps
Internet telephony: 5.3 kbps and up
time
audio signal amplitude
analog
signal
quantized value of
analog value
quantization error
sampling rate
(N sample/sec)

## Slide 4: Multimedia: video
video: sequence of images displayed at constant rate
  e.g. 24 images/sec
digital image: array of pixels
  each pixel represented by bits
coding: use redundancy within and between images to decrease # bits used to encode image
  spatial (within image)
  temporal (from one image to next)
……………………...…
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 5: Multimedia: video
……………………...…
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i
CBR: (constant bit rate): video encoding rate fixed
VBR: (variable bit rate): video encoding rate changes as amount of spatial, temporal coding changes
examples:
  MPEG 1 (CD-ROM) 1.5 Mbps
  MPEG2 (DVD) 3-6 Mbps
  MPEG4 (often used in Internet, < 1 Mbps)

## Slide 6: Multimedia networking: 3 application types
streaming, stored audio, video
  streaming: can begin playout before downloading entire file
  stored (at server): can transmit faster than audio/video will be rendered (implies storing/buffering at client)
  e.g., YouTube, Netflix, Hulu
streaming live audio, video
  e.g., live sporting event, …
conversational voice/video over IP
  interactive nature of human-to-human conversation limits delay tolerance
  e.g., Skype

## Slide 7: MM Networking Applications
Fundamental characteristics:
typically delay sensitive
  end-to-end delay
  delay jitter
loss tolerant: infrequent losses cause minor glitches
antithesis with data, which are loss intolerant but delay tolerant.
  Jitter is the variability
  of packet delays within
  the same packet stream

## Slide 8: Multimedia Over Today’s Internet
“best-effort service”
no guarantees on delay, loss
Today’s Internet multimedia applications
use application-level techniques to mitigate
(as best possible) effects of delay, loss
But you said multimedia apps require
Delay/jitter (ie bandwidth) guarantees to be
effective!
?
?
?
?
?
?
?
?
?
?
?

## Slide 9: Solution Approaches in IP Networks
To mitigate impact of “best-effort” protocols:
  Several apps use UDP to avoid TCP’s ack-based progress (and slow start)…
  Buffer content at client and control playback to remedy jitter
  Different error control methods (no ack)
  Exhaust all uses of caching, proxys, etc
  Adapt compression level to available bandwidth
  add more bandwidth
Scalability? May need other methods…

## Slide 10: Multimedia Applications, Services, Needs, …
Application Classes, challenges
Today’s representative technology
  recovery from jitter and loss
  Streaming protocols
  (Overlays) CDN: content distribution networks
Improving timing guarantees in Networks (also related with congestion-control)
  Packet scheduling and policing
Two generally different approaches
  The VC (ATM) approach (incl. material from Ch 3, 4, 5)
  Internet approach: Int-serv + RSVP, Diff-serv

## Slide 11: Streaming: recovery from jitter
constant bit
rate video
transmission
Cumulative data
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
client-side buffering and playout delay: compensate for network-added delay, delay jitter

## Slide 12: Client-side buffering, playout
variable fill
rate, x(t)
client application
buffer, size B
playout rate,
e.g., CBR r
buffer fill level, Q(t)
video server
client
1. Initial fill of buffer until playout begins at tp
2. playout begins at tp,
3. buffer fill level varies over time as fill rate x(t) varies and playout rate r is constant

## Slide 13: Client-side buffering, playout
playout buffering: average fill rate (x), playout rate (r):
x < r: buffer eventually empties (causing freezing of video playout until buffer again fills)
x > r: buffer will not empty, provided initial playout delay is large enough to absorb variability in x(t)
initial playout delay tradeoff: buffer starvation less likely with larger delay, but larger delay until user begins watching
variable fill
rate, x(t)
client application
buffer, size B
playout rate,
e.g., CBR r
buffer fill level, Q(t)
video server

## Slide 14: Internet Phone’s Playout Delay
… or dynamic:
estimate network delay +variance (as in TCP’s retransmission timeout) ;
adjust playout-delay at the beginning of each talkspurt
will cause silent periods to be compressed and elongated by a small amount; not noticeable in speech
Might be fixed: chunk timestamped t is played out (at the receiver) at time t + q (assuming it arrived)
Observe: delay-loss trade-off
  large q: less packet loss
  small q: better interactive experience

## Slide 15: Recovery From Packet Loss (Forward Error Correction)
Piggybacking Lower Quality Stream

## Slide 16: Recovery From Packet Loss/FEC (cont)
3. Interleaving: no redundancy, but can cause delay in playout beyond Real Time requirements
  Upon loss, have a set of partially filled chunks
  playout time must adapt to receipt of group
    Divide 20 msec of audio data into smaller units of 5 msec each and interleave

## Slide 17: Multimedia Applications, Services, Needs, …
Application Classes, challenges
Today’s representative technology
  recovery from jitter and loss (eg IP telephony)
  Streaming protocols
  (Overlays) CDN: content distribution networks
Improving timing guarantees in Networks (also related with congestion-control)
  Packet scheduling and policing
Two generally different approaches
  The VC (ATM) approach (incl. material from Ch 3, 4, 5)
  Internet approach: Int-serv + RSVP, Diff-serv

## Slide 18: Real-Time Protocol (RTP) RFC 3550
RTP specifies packet structure for carrying audio, video data
  payload type (encoding)
  sequence numbering
  time stamping
RTP does not provide any mechanism to ensure timely data delivery or other guarantees
RTP encapsulation only seen at end systems
RTP packets encapsulated in UDP segments
interoperability: if two Internet phone applications run RTP, then they may be able to work together

## Slide 19: Streaming multimedia: UDP
server sends at rate appropriate for client
  often: send rate = encoding rate = constant rate
  transmission rate can be oblivious to congestion levels
short playout delay (2-5 seconds) to remove network jitter
error recovery: application-level, time-permitting
RTP [RFC 2326]: multimedia payload types
BUT: UDP may not go through firewalls

## Slide 20: Streaming multimedia: HTTP
multimedia file retrieved via HTTP GET
send at maximum possible rate under TCP
fill rate fluctuates due to TCP congestion control, retransmissions (in-order delivery)
larger playout delay: smooth TCP delivery rate
HTTP/TCP passes more easily through firewalls
variable rate, x(t)
TCP send buffer
video
file
TCP receive buffer
application playout buffer
server
client

## Slide 21: Streaming multimedia: DASH: Dynamic, Adaptive Streaming over HTTP
server:
  divides video file into multiple chunks
  each chunk stored, encoded at different rates
  manifest file: provides URLs for different chunks
client:
  periodically measures server-to-client bandwidth
  consulting manifest, requests one chunk at a time, at appropriate coding rate
    can choose different coding rates at different points in time (depending on available bandwidth at time)
1.5 Mbps encoding
28.8 Kbps encoding

## Slide 22: Multimedia Applications, Services, Needs, …
Application Classes, challenges
Today’s representative technology
  recovery from jitter and loss (eg IP telephony)
  Streaming protocols
  (Overlays) CDN: content distribution networks (caching/proxies approach)
Improving timing guarantees in Networks (also related with congestion-control)
  Packet scheduling and policing
Two generally different approaches
  The VC (ATM) approach (incl. material from Ch 3, 4, 5)
  Internet approach: Int-serv + RSVP, Diff-serv

## Slide 23: Content distribution networks(CDNs)
Content replication
Challenging to stream large files from single origin server in real time to hundreds of 1000 or more end hosts
A solution: replicate content at several/many servers
  content downloaded to CDN servers ahead of time
  content “close” to user avoids impairments (loss, delay) of sending content over long paths
  CDN server typically in edge/access network
  Resembles overlay networks in P2P applications
origin server
CDN distribution node
CDN server
in S. America
CDN server
in Europe
CDN server
in Asia
Video link: http://vimeo.com/26469929

## Slide 24: CDN: “simple” content access scenario
Bob (client) requests video http://netcinema.com/6Y7B23V
video stored in CDN at http://KingCDN.com/NetC6y&B23V
netcinema.com
KingCDN.com
1
1. Bob gets URL for for video http://netcinema.com/6Y7B23V
from netcinema.com
web page
2
2. resolve http://netcinema.com/6Y7B23V
via Bob’s local DNS
netcinema’s
authorative DNS
3
3. netcinema’s DNS returns URL
http://KingCDN.com/NetC6y&B23V
4
4&5. Resolve
http://KingCDN.com/NetC6y&B23
via KingCDN’s authoritative DNS, which returns IP address of KIingCDN
server with video
5
6. request video from
KINGCDN server,
streamed via HTTP
KingCDN
authoritative DNS

## Slide 25: Case study: Netflix
1
1. Bob manages Netflix account
Netflix registration,
accounting servers
Amazon cloud
Akamai CDN
Limelight CDN
Level-3 CDN
2
2. Bob browses
Netflix video
3
3. Manifest file
returned for
requested video
4. DASH streaming
upload copies of multiple versions of video to CDNs
Netflix uploads studio master to 3rd party cloud
  create multiple version of movie (different encodings) in cloud
upload versions from cloud to 3rd party CDNs; user downloads the suitable encoding from them

## Slide 26: Summary: Internet Multimedia: bag of tricks
use UDP to avoid TCP congestion control (delays) for time-sensitive traffic; or multiple TCP connections (DASH)
  Buffering and client-side adaptive playout delay: to compensate for delay
  error recovery (on top of UDP)
    FEC, interleaving, error concealment
CDN: bring content closer to clients
server side matches stream bandwidth to available client-to-server path bandwidth
  chose among pre-encoded stream rates
  dynamic server encoding rate

## Slide 27: Multimedia Applications, Services, Needs, …
Application Classes, challenges
Today’s representative technology
  recovery from jitter and loss (eg IP telephony)
  (Overlays) CDN: content distribution networks
  Streaming protocols
Improving timing guarantees in Networks (also related with congestion-control)
  Packet scheduling and policing
Two generally different approaches
  The VC (ATM) approach (incl. material from Ch 3, 4, 5)
  Internet approach: Int-serv + RSVP, Diff-serv

## Slide 28: Improving timing/bandwidth guarantees in Networks
Aka Quality of Service (QoS): agreement on
  Traffic characteristics (packet rate, sizes, …)
  Network service guarantees (delay, jitter, loss rate, …)
model for resource sharing and congestion studies: Questions
  Distinguish traffic?
  Control offered load? (isolate different ”streams”?)
  Resources? (utilization)
  Control acceptance of new sessions?

## Slide 29: Principles for QoS for networking
  Packet classification
  Traffic shaping/policing (enforce contract terms)
  Packet scheduling (resource=bandwidth allocation)
  Admission control (will not study methods here)

## Slide 30: Where does this fit in?

## Slide 31: Where does this fit in?
Scheduling = choosing the next packet for transmission on a link (= allocate bandwidth)

## Slide 32: Packet Scheduling Policies: FIFO
FIFO: in order of arrival to the queue
  if buffer full: a discard policy determines which packet to discard among the arrival and those already queued

## Slide 33: Packet Scheduling Policies: Priority queueing
Priority Queuing: classes have different priorities; priority may depend on explicit marking or other header info, eg IP source or destination, type of packet, etc.
  Transmit a packet from the highest priority class with a non-empty queue

## Slide 34: Scheduling Policies: Weighted Fair Queueing
Weighted Fair Queuing: generalized Round Robin, including priorities (weights)
  provide each class with a differentiated amount of service
  class i receives a fraction of service wi/(wj)
ore on packet scheduling: work-conserving policies, delays, …

## Slide 35: Policing Mechanisms
Idea: shape the packet traffic (the network provider does traffic policing, ie monitors/enforces the ”shape” agreed).
Traffic shaping, to limit transmission rates:
  (Long term) Average Rate (e.g.100 packets per sec or 6000 packets per min), crucial aspect is the interval length
  Peak Rate: e.g., 6000 p p minute Avg and 1500 p p sec Peak
  (Max.) Burst Size: Max. number of packets sent consecutively, ie over a very short period of time

## Slide 36: Policing Mechanisms: Pure Leaky Bucket
Idea: eliminates bursts completely; may cause unnecessary packet losses

## Slide 37: Policing Mechanisms:LeakyToken Bucket
Idea: packets sent by consuming tokens produced at constant rate r
  limit input to specified Burst Size (b= bucket capacity) and Average Rate (max admitted #packets over time period t is b+rt).
  to avoid still much burstiness, put a leaky bucket -with higher rate; why?- after the token bucket)

## Slide 38: Policing Mechanisms: token bucket
Another way to illustrate token buckets:

## Slide 39: Policing: the effect of buckets
input
output pure leaky bucket, 2MBps
output token bucket 250KB, 2MBps
output token bucket 500KB, 2MBps
output token bucket 750KB, 2MBps
output 500KB, 2MBps token bucket feeding 10MBps leaky bucket

## Slide 40: Multimedia Applications, Services, Needs, …
Application Classes, QoS, challenges
Today’s representative technology
  recovery from jitter and loss (eg IP telephony)
  (Overlays) CDN: content distribution networks
  Streaming protocols
Improving QoS in Networks (also related with congestion-control)
  Packet scheduling and policing
Two generally different approaches
  The VC (ATM) approach (incl. material from Ch 3, 4, 5)
  Internet approach: Int-serv + RSVP, Diff-serv

## Slide 41: (Virtual Circuit example) ATM: Asynchronous Transfer Mode nets
Internet:
today’s de facto standard for global data networking
1980’s:
telco’s develop ATM: competing network standard for carrying high-speed voice/data
ATM principles:
virtual-circuit networks: switches maintain state for each “call”
small (48 byte payload, 5 byte header) fixed length cells (like packets)
  fast switching
  small size good for voice
Assume low error-rates, do not perform error control (enhance speed)
well-defined interface between “network” and “user” (think of classic telecom)
?

## Slide 42: Recall: switching fabrics
ATM switches: VC technology
  Virtual channels, virtual circuits
    Based on Banyan crossbar switches
ATM routing: as train travelling (hence no state for each ”stream/passenger”, but for each ”train”)

## Slide 43: ATM cell (small packet)
48-byte payload
  Why?: small payload -> short cell-creation delay for digitized voice
  halfway between 32 and 64 (compromise!)
Header: 5bytes
  VCI: virtual channel ID
  PT: Payload type (e.g. Resource Management cell versus data cell)
  CLP: Cell Loss Priority bit
    CLP = 1 implies low priority cell, can be discarded if congestion
  HEC: Header Error Checksum
Cell header
Cell format

## Slide 44: Example VC technology ATM Network service models:
Service
Model
Constant Bit Rate
VariableBR
(RT/nRT)
Available BR
UndefinedBR
Bandwidth
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
yes
yes
no
no
Order
yes
yes
yes
yes
Timing
yes
yes
no
no
Congestion
feedback
no
congestion
no
congestion
yes
no
Guarantees ?
With ABR you can get min guaranteed capacity and better, if possible; with UBR you can get better, but you may be thrown out in the middle 
Example
voice
Video/
“streaming”
www-browsing
Background file transfer

## Slide 45: ATM Bit Rate Services

## Slide 46: ATM Congestion Control
Several different strategies are used:
Admission control and resource reservation: reserve resources when opening a VC; traffic shaping and policing (use bucket-like methods)
Rate-based congestion control: (especially for ABR traffic) similar to choke packets (option also provided in IP (ICMP) also, but not really used in implementations); idea = give feedback to the sender and intermediate stations on the min. available (= max. acceptable) rate on the VC.

## Slide 47
ATM model motivated MPLS (multiprotocol label switching) for traffic engineering (cf extra notes)

## Slide 48: Multimedia Applications, Services, Needs, …
Application Classes, QoS, challenges
Today’s representative technology
  recovery from jitter and loss (eg IP telephony)
  (Overlays) CDN: content distribution networks
  Streaming protocols
Improving QoS in Networks (also related with congestion-control)
  Packet scheduling and policing
Two generally different approaches
  The VC (ATM) approach (incl. material from Ch 3, 4, 5)
  Int-serv + RSVP, Diff-serv

## Slide 49: Recall: Solution Approaches in IP Networks
  Bag of tricks, large responsibility on applications ….
  Is there an alternative way?

## Slide 50: Intserv: QoS guarantee scenario
Resource reservation per individual application session
  call setup, signaling (RSVP)
    Maintains state a la VC (but soft state,)
      responsibility at the client to renew reservations
    traffic, QoS declaration
    per-element admission control
  QoS-sensitive scheduling (e.g., WFQ)
request/
reply

## Slide 51: RSVP: resource reservation protocol
RSVP: a leading candidate for signaling protocol
  allows reservations for bandwidth in multicast trees
  is receiver-oriented (the receiver of a
    data flow initiates and maintains the
    resource reservation for the flow).
  Maintains soft-state
    receivers renew interest regularly
  does not specify how the network
    provides the reserved bandwidth, only
    allows the applications to reserve it.
  is not a routing protocol; it depends on
    an underlying routing protocol to
    determine the routes for the flows; when a route changes,
    RSVP re-reserves resources.
  does not define the admission test, but it assumes that the routers perform such a test and that RSVP can interact with the test.

## Slide 52: Back to Internet bandwidth guarantee support: alternatively?
Concerns with Intserv:
Scalability: signaling, maintaining per-flow router state difficult with large number of flows
Diffserv approach:
Don’t define service classes, provide functional components to build service classes
  Network core: stateless, simple
  Combine flows into aggregated flows
  Classification, shaping, admission at the network edge

## Slide 53: Diffserv Architecture
Edge router:
per-flow traffic management
marks packets as in-profile and out-profile
Core router:
per class traffic management
buffering and scheduling based on marking at edge
preference given to in-profile packets
scheduling
.
.
.
r
b
marking

## Slide 54
Edge-router Packet Marking
class-based marking: packets of different classes marked differently
intra-class marking: conforming portion of flow marked differently than non-conforming one
Packet is marked in the Type of Service (TOS) in IPv4, and Traffic Class in IPv6
profile: pre-negotiated rate A, bucket size B
packet marking at edge based on per-flow profile
Possible usage of marking:
User packets
Rate A
B

## Slide 55: DiffServ Core Functions
Forwarding: according to “Per-Hop-Behavior” (PHB) specified for the particular packet class; PHB is strictly based on classification marking
  PHB does not specify what mechanisms to use to ensure required PHB performance behavior
  Examples:
    Class A gets x% of outgoing link bandwidth over time intervals of a specified length
    Class A packets leave before packets from class B
Advantage:
No state info to be maintained by routers

## Slide 56: Summary
Internet core and transport protocols do not provide guarantees for multimedia streaming traffic
Applications take matters into own hands
  Bag of tricks and interesting evolving methods
Another type of service at the core (VC-like) would imply a different situation
  But then the internet core would be different

## Slide 57: Reading list, review questions, further study
Chapter 7
3.6.2
5.5.1
R7: 5, 6, 7, 8, 12, 14, 17,
Upkar Varshney, Andy Snow, Matt McGivern, and Christi Howard. 2002. Voice over IP. Commun. ACM 45, 1 (January 2002), 89-96. DOI=10.1145/502269.502271 http://doi.acm.org/10.1145/502269.502271
Jussi Kangasharju, James Roberts, Keith W. Ross, Object replication strategies in content distribution networks, Computer Communications, Volume 25, Issue 4, 1 March 2002, Pages 376-383, ISSN 0140-3664, http://dx.doi.org/10.1016/S0140-3664(01)00409-1. (http://www.sciencedirect.com/science/article/pii/S0140366401004091)
K.L Johnson, J.F Carr, M.S Day, M.F Kaashoek, The measured performance of content distribution networks, Computer Communications, Volume 24, Issue 2, 1 February 2001, Pages 202-206, ISSN 0140-3664, http://dx.doi.org/10.1016/S0140-3664(00)00315-7. (http://www.sciencedirect.com/science/article/pii/S0140366400003157)
Eddie Kohler, Mark Handley, and Sally Floyd. 2006. Designing DCCP: congestion control without reliability. SIGCOMM Comput. Commun. Rev. 36, 4 (August 2006), 27-38. DOI=10.1145/1151659.1159918 http://doi.acm.org/10.1145/1151659.1159918

## Slide 58: Extra slides/notes

## Slide 59: The Internet: virtualizing networks
1974: multiple unconnected nets
  ARPAnet
  data-over-cable networks
  packet satellite network (Aloha)
  packet radio network
… differing in:
  addressing conventions
  packet formats
  error recovery
  routing
ARPAnet
satellite net
"A Protocol for Packet Network Intercommunication",
V. Cerf, R. Kahn, IEEE Transactions on Communications,
May, 1974, pp. 637-648.

## Slide 60: The Internet: virtualizing networks
Gateway:
“embed internetwork packets in local packet format”
route (at internetwork level) to next gateway
ARPAnet
satellite net
gateway
Internetwork layer (IP):
addressing: internetwork appears as single, uniform entity, despite underlying local network heterogeneity
network of networks

## Slide 61: Cerf & Kahn’s Internetwork Architecture
What is virtualized?
two layers of addressing: internetwork and local network
new layer (IP) makes everything homogeneous at internetwork layer
underlying local network technology
  Cable, satellite, 56K telephone modem
  Ethernet, other LAN
  ATM/ MPLS (Multiprotocol Label Switching Protocol)
… “invisible” at internetwork layer. Looks like a link layer technology to IP

## Slide 62: e.g. IP-Over-ATM
“Classic” IP over eg Ethernet
3 “networks” (e.g., LAN segments)
MAC (eg802.3) and IP addresses
IP over ATM
replace “network” (e.g., LAN segment) with ATM network
ATM addresses (as MAC addresses), IP addresses
ATM
network
Ethernet
LANs
Ethernet
LANs

## Slide 63: IP-Over-ATM
AAL
ATM
phy
phy
Eth
IP
ATM
phy
ATM
phy
app
transport
IP
AAL
ATM
phy
app
transport
IP
Eth
phy
AAL: ATM adaptation layer intended for transport layer functionality (with AAL1-4 services: cons/var/avail/undefined bit-rate traffic) but implementations did not allow such use; AAL5 made for use under IP….

## Slide 64: Multiprotocol label switching (MPLS)
initial goal: speed up IP forwarding by using fixed length label (instead of IP address) to do forwarding
  borrowing ideas from Virtual Circuit (VC) approach (a’la ATM)
  but IP datagram still keeps IP address!
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
S
TTL
20
3
1
5

## Slide 65: MPLS capable routers
a.k.a. label-switched router
forwards packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
signaling protocol needed to set up forwarding
  RSVP-TE
  forwarding possible along paths that IP alone would not allow (e.g., source-specific routing) !!
  use MPLS for traffic engineering
must co-exist with IP-only routers

## Slide 67: Adaptive Playout Delay (1)
Goal: minimize playout delay, keeping late loss rate low
Approach: adaptive playout delay adjustment:
  estimate network delay, adjust playout delay at beginning of each talk spurt.
  silent periods compressed and elongated.
  chunks still played out every 20 msec during talk spurt.
dynamic estimate of average delay at receiver:
where u is a fixed constant (e.g., u = .01).

## Slide 68: Adaptive playout delay (2)
also useful to estimate average deviation of delay, vi :
estimates di , vi calculated for every received packet
(but used only at start of talk spurt
for first packet in talk spurt, playout time is:
where K is positive constant
remaining packets in talkspurt are played out periodically

## Slide 70: Streaming
Audio/Video file is segmented and sent over TCP or UDP;
User interactive control provided, e.g. Real Time Streaming Protocol (RTSP)
Helper Application: displays content, (typically requested via a Web browser); e.g. RealPlayer; typical functions:
  Decompression
  Jitter removal
  Error correction: use redundant packets to be used for reconstruction of original stream
  GUI for user control

## Slide 71: Real-Time Protocol (RTP) & RT Control Protocol (RTCP)
standard packet format for real-time application
  Payload Type: 7 bits: 128 possible types of encoding; eg PCM, MPEG2 video, GSM, etc. (sender can change in the middle of session)
  Sequence Number: to detect packet loss
  Timestamp: sampling instant of first byte in packet; to remove jitter introduced by the network
  Synchronization Source identifier (SSRC): id for the source of a stream; assigned randomly by the source
Real-Time Control Protocol (RTCP): specifies report packets exchanged between sources and destinations, with statistics (# packets sent/lost, inter-arrival jitter
  Can be used to modify sender transmission rates

## Slide 73: SIP Service Initiation Protocol
SIP long-term vision
All phone/video conference calls take place over the Internet
People are identified by names or e-mail addresses, rather than by phone numbers.
You can reach the callee, no matter where the callee roams, no matter what IP device the callee is currently using.
What does it do:
Determine current IP address of callee.
  Maps mnemonic identifier to current IP address
Setting up/ending a call
  Provides also mechanisms so that caller and callee can agree on media type and encoding.
Call management
  Add new media streams during call
  Change encoding during call
  Invite others
  Transfer and hold calls

## Slide 74: Setting up a call to known IP address
Alice’s SIP invite message indicates her port number & IP address+encoding
Bob’s 200 OK message (could also reject, say “busy”, etc) indicates his port number, IP address & preferred encoding (GSM)
SIP messages can be sent over TCP or UDP; here over RTP/UDP.
HTTP message syntax (but SIP maintains state)
Default SIP port number: 5060.

## Slide 75: Example name translation, user location
Caller jim@umass.edu places a
call to keith@upenn.edu
Jim sends INVITE to umass SIPproxy.
(2) Proxy forwards request to upenn registrar server.
(3) upenn server returns redirect response, indicating that it should try keith@eurecom.fr
(4) umass proxy sends INVITE to eurecom registrar.
(5) eurecom registrar forwards INVITE to 197.87.54.21, which is running keith’s SIP client.
(6-8) SIP response sent back
(9) media sent directly between clients.
(follows pretty much the DNS inquiry structure)

## Slide 76: Token bucket + WFQ…
…can be combined to provide upper bound on packet delay in queue:
bi packets in queue, packets are serviced at a rate of at least R · wi/ (wj) packets per second, then the time until the last packet is transmitted is at most
bi /(R · wi/ (wj))

## Slide 78: ATM ABR congestion control
RM (resource management) cells:
interspersed with data cells
bits in RM cell set by switches (“network-assisted”)
  NI bit: no increase in rate (mild congestion)
  CI bit: congestion indication two-byte ER (explicit rate) field in RM cell
  congested switch may lower ER value in cell
  sender’ send rate thus minimum supportable rate on path
ABR: available bit rate:
“elastic service”
if path “underloaded”:
  sender should use available bandwidth
if path congested:
  sender throttled to minimum guaranteed rate

## Slide 79: Traffic Shaping and Policing in ATM
Enforce the QoS parameters: check if Peak Cell Rate (PCR) and Cell Delay Variation (CDVT) are within the negotiated limits:
Generic Cell Rate Algo: introduce:
expected next time for a successive cell, based on T = 1/PCR
border time L ( = CDVT) < T in which next transmission may start (but never before T-L)
A nonconforming cell may be discarded, or its Cell Loss Priority bit be set, so it may be discarded in case of congestion

## Slide 80: ATM Adaptation (Transport) Layer: AAL
”suitability” has not been very successful
computer science community introduced AAL5, (simple, elementary protocol), to make the whole ATM stack usable as switching technology for data communication under IP!
Basic idea: cell-based VCs need to be ”complemented ”to be supportive for applications.
Several ATM Adaptation Layer (AALx) protocols defined, suitable for different classes of applications
  AAL1: for CBR (Constant Bit Rate) services, e.g. circuit emulation
  AAL2: for VBR (Variable Bit Rate) services, e.g., MPEG video
  .....

## Slide 81: ATM: network or link layer?
Vision: end-to-end transport: “ATM from desktop to desktop”
  ATM is a network technology
Reality: used to connect IP backbone routers
  “IP over ATM”
  ATM as switched link layer, connecting IP routers

## Slide 83: Network support for multimedia