## Slide 1: Data networking technologies in Smart Grids
Giorgos Georgiadis
10/12/2013

## Slide 2: Introduction
 | SONET - Synchronous Optical Network WDM - Wavelength Division Multiplexing Satellite/VSAT IP Radio | Twisted pair / Fiber optics BPL - Broadband over Power Lines WiMax - Worldwide Interoperability for Microwave Access GPRS | 
 | Ethernet rules~ | Ethernet rules! (IEC 61850) | Ethernet rules? Hint: not always
“Here be SCADA”
Communication
technologies
?
Communication
protocols
?
1

## Slide 3: Overview
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
Protocols @ Distribution’s last mile
2

## Slide 4: PHY/DataLink protocols
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LowPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
Ethernet
  Not much to say
HomePlug
  Honorable mention: popular home automation protocol
  Powerline based
  Speed: ~200mbps
  Otherwise, vanilla protocol:
    i.e. using TDMA,
    Two kinds of nodes,
    …
3

## Slide 5: PHY/DataLink protocols
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LowPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
IEEE 802.15.4
  Radio based, usually 2.4GHz
  Small packets (<=127bytes)
  Medium speed (~250kbps)
  Originally DSSS
  Topologies supported:
    Star
    Peer-to-peer
  Roles supported:
    Full-function device
    Reduced-function device
4

## Slide 6: Higher protocols
6LoWPAN
  “IPv6 over LoW Power wireless Area Networks”
  Builds on 802.15.4, IPv6
  Aimed at low power devices (sensors, controllers)
  Topologies
    Star, peer-to-peer + Mesh
  Many Challenges:
    IP packets >=1280bytes (!)
    128bit IP addresses
    …
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
5

## Slide 7: Higher protocols
ZigBee
  Builds on 802.15.4, but not IP
  Aimed at low power devices too (sensors, controllers)
    Speed 250kbps
    Packet 127bytes
    Battery powered devices (supports sleep)
  Topologies supported
    Mesh (jump to: example)
  Roles supported
    Coordinator, router, end node
  Different profiles exist:
    ZigBee Home Automation
    Zigbee Smart Energy
    Zigbee IP, ...
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
6

## Slide 8: Higher protocols
More protocols, same story:
  XMPP, BACNet, LonWorks, Modbus, …
  Wired
  Proprietary, build around specific companies (BACNet, LonWorks) or legacy protocols (Modbus)
  Today gateway devices to “break out” to Ethernet are in use
  Simple topologies (i.e bus), same roles as before
But what is the connecting thread over all?
  Open standards!
  Internet! (of Things?)
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
8

## Slide 9: Towards interoperability
OpenADR
  ADR: Advanced Metering Response
  Trying to ‘unify’ different solutions in a high level protocol
  Formalizing:
    Roles
    Messages
    Device detection
  Simple topologies (i.e bus), same roles as before
REST-based APIs
  I.e. Costrained Application Protocol
  Ultimately, HTTP-based
  Verb oriented: GET, PUT, DELETE, …
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
9

## Slide 10: Towards interoperability
Ethernet/IP-based integration
  Remember:
    Radio band: 2.4GHz (WiFI, ZigBee, 6LoWPAN)
    Similar topologies, roles
    Made for low energy devices, but flops/watt/kr increase!
    Ethernet gateways commonly used
  Solution: make them (formally) interoperable
    ZigBee Smart Energy v2.0
    ZigBee, WiFi, HomePlug on board
    6LoWPAN coming soon
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
10

## Slide 11: Conclusion
Ethernet + misc communication technologies
Ethernet vs non-ethernet
  Why?
    Design for low energy devices (smaller packets, lower comm speed)
    Peer to peer, mesh topologies
  Now + Future?
    Devices’ specs catching up
    Importance of being connected (to the Internet?)
    Topologies still important (i.e. reliability)
    Will probably remain radio-based
11

## Slide 12: Thank you!
Questions/comments?