## Slide 1: Chapter 4: Network Layer Part A
Course on Computer Communication and Networks, CTH/GU
The slides are adaptation of the slides made available by the authors of the course’s main textbook

## Slide 2: Network layer
Consider transporting a segment from sender to receiver
sending side: encapsulates segments into datagrams
receiving side: delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 3: Roadmap
understand principles of network layer services:
  forwarding versus routing
  network layer service models
  how a router works
  The Internet Network layer: IP, Addressing & related
routing
  path selection)
  instantiation, implementation in the Internet
Today
Next

## Slide 4
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
Interplay between routing and forwarding
routing algorithm determines
path through network
forwarding table determines
local forwarding at this router

## Slide 5: Network service model
Q: What service model for “channel” carrying packets from sender to receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of packets:
in-order delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet time-spacing

## Slide 6: Connection, connection-less service
datagram network provides network-layer connectionless service (Internet model)
virtual-circuit network provides network-layer connection service (not in Internet)
analogous to TCP/UDP connection-oriented / connectionless transport-layer services, but:
  service: host-to-host
  no choice: network provides one or the other
  implementation: in network core

## Slide 7: Virtual circuits:
“source-to-dest path behaves almost like telephone circuit”
call setup, teardown for each call before data can flow
  signaling protocols to setup, maintain, teardown VC (ATM, frame-relay, X.25; not in IP)
each packet carries VC identifier (not destination host)
every router maintains “state” for each passing connection
resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 8: VC implementation
a VC consists of:
  path from source to destination
  VC numbers, one number for each link along path
  entries in forwarding tables in routers along path
packet belonging to VC carries VC number (rather than dest address)
VC number can be changed on each link.
  new VC number comes from forwarding table

## Slide 9: VC forwarding table
12
22
32
1
2
3
VC number
interface
number
Incoming interface Incoming VC # Outgoing interface Outgoing VC #
1 12 3 22
2 63 1 18
3 7 2 17
1 97 3 87
… … … …
forwarding table in
northwest router:
VC routers maintain connection state information!

## Slide 10: Datagram networks (the Internet model)
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 11: Internet Datagram forwarding table
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so rather than list individual destination address
list range of addresses
(aggregate table entries)

## Slide 12: Datagram forwarding table
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up nicely?

## Slide 13: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address (more on this coming soon)
longest prefix matching
Link interface
0
1
2
3

## Slide 14: Datagram or VC network: why?
Internet (datagram)
data exchange among computers
  “elastic” service, no strict timing req.
many link types
  different characteristics
  uniform service difficult
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
VC (eg ATM: a past’s vision of the future’s ww-network)
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network

## Slide 15: Roadmap
understand principles of network layer services:
  forwarding versus routing
  network layer service models
  how a router works
  The Internet Network layer: IP, Addressing & related
routing
  path selection)
  instantiation, implementation in the Internet
Today
Next

## Slide 16: Router architecture overview
two key router functions:
run routing algorithms/protocol (eg: RIP, OSPF, BGP; more on these next lecture)
forwarding datagrams from incoming to outgoing link
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware)
routing, management
control plane (software)
forwarding tables computed,
pushed to input ports

## Slide 17: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
switching:
given datagram dest., lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric

## Slide 18: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics:
memory
memory
bus
crossbar

## Slide 19: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 20: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 21: Switching via interconnection network
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 22: Switching Via An Interconnection Network
Overcome bus bandwidth limitations
Banyan networks, other interconnection nets (also used in processors-memory interconnects in multiprocessors)
  Advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric (ATM-network principle).
Cisco 12000: switches at 60 Gbps
crossbar

## Slide 23: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 24: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
  queueing (delay) and loss due to output port buffer overflow!
scheduling discipline chooses among queued datagrams for transmission (more on packet scheduling later)
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing

## Slide 25: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets move
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 26: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C (due to Little’s law)
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N

## Slide 27: Example contemporary routers
Cisco Catalyst 3750E
Stackable (can combine units)
1 Gbit/s ports 64 Gbit/s bandwidth
13 Mpps (packets per second)
12,000 address entries
Price: from 100 kSEK
HP ProCurve 6600-24G-4XG Switch
1 Gbit/s, 10 Gbps
Up to 75 Mpps (64-byte packets)
Latency: < 2.4 µs (FIFO 64-byte packets) 10,000 entries
Price approx. 50 kSEK
Notes: TO

## Slide 28: Roadmap
understand principles of network layer services:
  forwarding versus routing
  network layer service models
  how a router works
  The Internet Network layer: IP, Addressing & related
routing
  path selection)
  instantiation, implementation in the Internet
Today
Next

## Slide 29: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 30: IPv4 datagram format
ver
length
32 bits
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head. len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
data
(variable length,
typically a TCP
or UDP segment)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data (prio)
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 31: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet and wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 32: Subnets
IP address:
  subnet part - high order bits (variable number)
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 33: Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: eg /24
defines how to find the subnet part of the address …
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 34: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 35: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 36: Subnets, masks, calculations
Example subnet: 192.168.5.0/24
 | Binary form | Dot-decimal notation
IP address | 11000000.10101000.00000101.10000010 | 192.168.5.130
Subnet mask | 11111111.11111111.11111111.00000000 --------24 first bits set to 1------ | 255.255.255.0
Network prefix: (bitwise AND of address, mask) | 11000000.10101000.00000101.00000000 | 192.168.5.0
Host part (similar calculation, with eg a ”mask” where the 32 – 24 last bits set to 1) | 00000000.00000000.00000000.10000010 | 0.0.0.130

## Slide 37: Classless Address: example
37
    An ISP has an address block 122.211.0.0/16
    A customer needs max. 6 host addresses,
    ISP can e.g. allocate: 122.211.176.208/29
      3 bits enough for host part
    subnet mask 255.255.255.248
 | Dotted Decimal | Last 8 bits
Network | 122.211.176.208 | 11010000
1st address | 122.211.176.209 | 11010001
…………. | ………………… | …………
6th address | 122.211.176.214 | 11010110
Broadcast | 122.211.176.215 | 11010111
2013 Ali Salehson, Chalmers, CSE Networks and Systems

## Slide 38: CIDR Address Mask
38
CIDR Notation Dotted Decimal
/1 128.0.0.0
/2 192.0.0.0
/3 224.0.0.0
/4 240.0.0.0
/5 248.0.0.0
/6 252.0.0.0
/7 254.0.0.0
/8 255.0.0.0
/9 255.128.0.0
/10 255.192.0.0
/11 255.224.0.0
/12 255.240.0.0
/13 255.248.0.0
/14 255.252.0.0
/15 255.254.0.0
/16 255.255.0.0
CIDR Notation Dotted Decimal
/17 255.255.128.0
/18 255.255.192.0
/19 255.255.224.0
/20 255.255.240.0
/21 255.255.248.0
/22 255.255.252.0
/23 255.255.254.0
/24 255.255.255.0
/25 255.255.255.128
/26 255.255.255.192
/27 255.255.255.224
/28 255.255.255.240
/29 255.255.255.248
/30 255.255.255.252
/31 255.255.255.254
/32 255.255.255.255
2013 Ali Salehson, Chalmers, CSE Networks and Systems

## Slide 39: IP addresses: how to get one?
Q: How does a host get IP address?
Hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
Display address information:
  Windows: ipconfig /all

## Slide 40: IP addresses: how to get one?
hard-coded by system admin in a file
  (Windows: control-panel->network->configuration->tcp/ip->properties; UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address:
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 41: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 42: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 43: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0 (your IP addr)
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Q:Why a request msg?
Several DHCP servers may answer and offer addresses
Notes: Mod TO

## Slide 44: DHCP: more than an IP address
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 45: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space; eg:
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23
3 bits, 8 networks

## Slide 46: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 47: (Well, it was not really the last word…) NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers
(it is all about extending the IP address space)

## Slide 48: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 49: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 50: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 51: NAT: network address translation
16-bit port-number field:
  64k simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  address shortage should instead be solved by IPv6

## Slide 52: NAT traversal problem
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible address: 138.76.29.7
solution1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (123.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
Solution 2: automate the above through a protocol (universal plug-and-play)
Solution 3: through a proxy/relay (will discuss in connection to p2p applications)
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
client
?

## Slide 53: NAT traversal problem
solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATed host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration
10.0.0.1
NAT
router
IGD

## Slide 54: Getting a datagram from source to dest.

## Slide 55: Getting a datagram from source to dest.
IP datagram:
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
misc
fields
source
IP addr
dest
IP addr
data
datagram remains unchanged, as it travels source to destination
addr fields of interest here
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
forwarding table in A

## Slide 56: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
look up net. address of B
find B is on same net. as A (B and A are directly connected)
link layer will send datagram directly to B (inside link-layer frame)
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
misc
fields
223.1.1.1
223.1.1.3
data

## Slide 57: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
Starting at A, dest. E:
look up network address of E
E on different network
routing table: next hop router to E is 223.1.1.4
link layer is asked to send datagram to router 223.1.1.4 (inside link-layer frame)
datagram arrives at 223.1.1.4
continued…..
misc
fields
223.1.1.1
223.1.2.3
data

## Slide 58: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Arriving at 223.1.4, destined for 223.1.2.2
look up network address of E
E on same network as router’s interface 223.1.2.9
  router, E directly attached
link layer sends datagram to 223.1.2.2 (inside link-layer frame) via interface 223.1.2.9
datagram arrives at 223.1.2.2!!! (hooray!)
misc
fields
223.1.1.1
223.1.2.3
data
network router Nhops interface
223.1.1 - 1 223.1.1.4
223.1.2 - 1 223.1.2.9
223.1.3 - 1 223.1.3.27
Dest. next

## Slide 59: Roadmap
understand principles of network layer services:
  forwarding versus routing
  network layer service models
  how a router works
  The Internet Network layer: IP, Addressing & related
    ICMP, IPv6
routing
  path selection)
  instantiation, implementation in the Internet
Today
Next

## Slide 60: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 61: Traceroute and ICMP
source sends series of UDP segments to dest
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when nth set of datagrams arrives to nth router:
  router discards datagrams
  and sends source ICMP messages (type 11, code 0)
  ICMP messages includes name of router & IP address
when ICMP messages arrive, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 62: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed
  128-bit addresses (2128 = 1038 hosts)
  Standard subnet size: 264 hosts

## Slide 63: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 64: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 65: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram

## Slide 66: Tunneling (6in4 – static tunnel)
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4
Notes: Mod TO – real solution is Teredo RFC 4380, where [D+E] is a Teredo server and the tunnel uses UDP port 3544. Supported by most modern systems.

## Slide 67: Roadmap
understand principles of network layer services:
  forwarding versus routing
  network layer service models
  how a router works
  The Internet Network layer: IP, Addressing & related
routing
  path selection)
  instantiation, implementation in the Internet
Today
Next

## Slide 68: Reading instructions
Main textbook: careful: 4.1-4.6, quick/optional: 4.7
Further, optional study: cf embedded, no-ppt-show slides

## Slide 69: Review questions for this part
network layer service models
  Contrast virtual circuit and datagram routing (simplicity, cost, purposes, what service types they may enable)
forwarding versus routing
  Explain the interplay between routing and forwarding
how a router works
  What is inside a router? How/where do queueing delays happen inside a router? Where/why can packets be dropped at a router?
What is subnet? What is subnet masking?
  Train/exercise masking calculations
Explain how to get an IP packet from source to destination
Explain how NAT works.

## Slide 70: Some complementary material /video-links
How does PGP choose its routes http://www.youtube.com/watch?v=RGe0qt9Wz4U&feature=plcp
IP addresses and subnets http://www.youtube.com/watch?v=ZTJIkjgyuZE&list=PLE9F3F05C381ED8E8&feature=plcp
Some taste of layer 2: no worries if not all details fall in place, need the lecture also to grasp them. The lecture will be held next week
Hubs, switches, routers http://www.youtube.com/watch?v=reXS_e3fTAk&feature=related
What is a broadcast + MAC address http://www.youtube.com/watch?v=BmZNcjLtmwo&feature=plcp
Broadcast domains: http://www.youtube.com/watch?v=EhJO1TCQX5I&feature=plcp

## Slide 71: Extra slides

## Slide 72: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?
Internet model being extented: Intserv, Diffserv
(will study these later on)

## Slide 73: NAT traversal problem
client want to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible NATted address: 138.76.29.7
solution 1 (manual): statically configure NAT to forward incoming connection requests at given port to server
  e.g., (123.76.29.7, port 2500) always forwarded to 10.0.0.1 port 2500
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
Client
?

## Slide 74: NAT traversal problem
solution 2 (protocol) : Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATted host to:
  learn public IP address (138.76.29.7)
  enumerate existing port mappings
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
IGD

## Slide 75: NAT traversal problem
solution 3 (application): relaying (used in Skype)
  NATed server establishes connection to relay
  External client connects to relay
  relay bridges packets between two connections
10.0.0.1
NAT
router
138.76.29.7
Client
1. connection to
relay initiated
by NATted host
2. connection to
relay initiated
by client
3. relaying
established

## Slide 76: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits to identify + order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 77: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8