## Slide 1: Course on Computer Communication and Networks Lecture 12 Continuously evolving Internet-working Part B: QoS, traffic engineering, SDN, IoT
EDA344/DIT 423, CTH/GU

## Slide 2: Internet protocol stack layers&protocols
Application: protocols supporting network applications
  http (web), smtp (email), p2p, streaming, CDN, …
transport: process2process (end2end) data transfer
  UDP, TCP
network: routing of datagrams (independent data-packets), connecting different physical networks
  IP addressing, routing protocols, virtualization, virtualization, …
link: data transfer between neighboring (physically connected) hosts
  Ethernet, WiFi, …
physical: bit-transmission on the physical medium between neighboring nodes
application
transport
network
link
physical
TCP
UDP

## Slide 3: Timing/bandwidth guarantees in networks
aka Quality of Service (QoS): 2-party agreement (NW user – NW provider) on
Traffic characteristics (packet rate, sizes, …)
Network service guarantees (delay, jitter, loss rate, …)
Model for resource sharing and congestion studies: questions/principles for QoS in Network Core
Distinguish traffic?
Control offered load? (isolate different ”streams”?)
Allocate: resources? (utilization)
Control acceptance of new sessions?
Tasks for the NW core:
Packet classification & scheduling (bandwidth allocation)
Traffic shaping/policing (enforce contract terms)
Admission control

## Slide 4: Let’s hit the road again: Roadmap
NW support for multimedia / QoS: [Ch. 9.5 (7.5 6/e) ]
Improving timing/QoS guarantees in Networks (also related with congestion-control): Packet scheduling and policing
A VC (ATM) approach [incl. Ch 3.7.2 (6e 3.62-3.6.3)]
Internet approaches
  Diff-serv, Int-serv + RSVP,
  Traffic Engineering MPLS [incl. ch. 6.5 (6/e 5.5)]
SDN [ch 4.4, 5.5 (cf separate notes @pingpong docs, if you do not have access to 7e ]
Internet-of-Things in evolution: more types of traffic/devices… [optional study, just browse example protocols mentioned]

## Slide 5: Where does this go in?
Scheduling = choosing the next packet for transmission on a link (= allocate bandwidth)
if buffer full: a discard policy determines which packet to discard among the arrival and those already queued

## Slide 6: Packet Scheduling example: Weighted Fair Queueing
Weighted Fair Queuing: generalized Round Robin, including priorities (weights)
  provide each class with a differentiated amount of service
  class i receives a fraction of service wi/(wj)
There are a lot more decision options about packet scheduling: work-conserving policies, delays, …

## Slide 7: Policing Mechanisms
Idea: shape the packet traffic :network provider does traffic policing, ie enforces the ”shape” agreed.
Traffic shaping, to limit transmission rates:
  (Long term) Average Rate (e.g.100 pkts/sec or 6000 packets per min)
  Peak Rate: e.g.1500 pkts/sec peak
  (Max.) Burst Size: Max. number of packets sent consecutively, ie over a very short period of time

## Slide 8: Policing Mechanisms: LeakyToken Bucket
Idea: packets sent by consuming tokens that are produced at constant rate r
  limit input’s
    Burst Size (b= bucket capacity)
    Average Rate (max admitted #packets over time period t is b+rt).
Another way to illustrate token buckets:

## Slide 9: Policing: the effect of buckets
input
output 0KB token leaky bucket, 2MBps
output 250KB token leaky bucket, 2MBps
output 500KB token leaky bucket, 2MBps
output 750KB token leaky bucket, 2MBps
output token leaky bucket 500KB, 2MBps, feeding 0KB, 10MBps token leaky bucket
to futher limit burstiness,
use a second leaky bucket with higher rate

## Slide 10: Roadmap
NW support for multimedia / QoS: [Ch. 9.5 (7.5 6/e) ]
Improving timing/QoS guarantees in Networks (also related with congestion-control): Packet scheduling and policing
A VC (ATM) approach [incl. Ch 3.7.2 (6e 3.62-3.6.3)]
Internet approaches
  Diff-serv, Int-serv + RSVP,
  Traffic Engineering MPLS [incl. ch. 6.5 (6/e 5.5)]
SDN [ch 4.4, 5.5 (cf separate notes @pingpong docs, if you do not have access to 7e ]
Internet-of-Things in evolution: more types of traffic/devices… [optional study, just browse example protocols mentioned]

## Slide 11: Virtual Circuit example: ATM: Asynchronous Transfer Mode nets
Internet ‘s IP:
today’s de facto standard for global data networking
1980’s:
telco’s develop ATM specifications: competing network standard for carrying high-speed voice/data
ATM principles:
virtual-circuit networks: switches maintain state for each “call”
small (48 byte payload, 5 byte header) fixed length cells (like packets)
  fast switching
  small size good for voice
well-defined interface between “network” and “user” (think of classic telecom)

## Slide 12: Example VC technology ATM Network service models (i.e. transport layer services):
Service
Model
Constant Bit Rate
VariableBR
(RT/nRT)
Available BR
UndefinedBR
Bandwidth
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
yes
yes
no
no
Order
yes
yes
yes
yes
Timing
yes
yes
no
no
Congestion
control
Admission
control
Admission
control
Yes, feedback
discard pkts
Guarantees ?
With ABR you can get min guaranteed capacity and better, if possible; with UBR you can get better, but you may be thrown out in the middle 
Example
voice
Video/
“streaming”
www-browsing
Background file transfer

## Slide 13: ATM (VC) Congestion Control (hand-in-hand with Bandwidth reservation) Several different strategies in place :
Rate-based congestion control: (ABR traffic)
  idea = feedback to the sender and intermediate stations on the available (= max. acceptable) rate on the VC.
  similar to ”choke packets” (option provided in ICMP, which is not used in implementations…)
Admission control and resource reservation (CBR and VBR traffic:
  reserve resources when opening a VC; traffic shaping and policing (use bucket-like methods)

## Slide 14: Roadmap
NW support for multimedia / QoS: [Ch. 9.5 (7.5 6/e) ]
Improving timing/QoS guarantees in Networks (also related with congestion-control): Packet scheduling and policing
A VC (ATM) approach [incl. Ch 3.7.2 (6e 3.62-3.6.3)]
Internet approaches
  Diff-serv, Int-serv + RSVP,
  Traffic Engineering MPLS [incl. ch. 6.5 (6/e 5.5)]
SDN [ch 4.4, 5.5 (cf separate notes @pingpong docs, if you do not have access to 7e ]
Internet-of-Things in evolution: more types of traffic/devices… [optional study, just browse example protocols mentioned]

## Slide 15: Diffserv proposed Architecture
Edge router: marking
per-aggr-flow traffic management
  marks packets as in-profile and out-profile
Core router: scheduling
per class traffic scheduling
  based on marking at edge
  preference given to in-profile packets
scheduling
.
.
.
r
b
marking
Internet bandwidth-guarantee support possibilities?
Diffserv approach: provide functional components to build service classes
  Network core: stateless, simple
  Combine into aggregated flows, classification, shaping, admission: @ network edge

## Slide 16
Edge-router Packet Marking
-Class-based marking: packets of different classes marked differently
  Profile within class: pre-negotiated rate A, bucket size B
Packet is marked in the Type of Service (TOS) in IPv4, and Traffic Class in IPv6
User packets
Rate A
B
Forwarding: according to “Per-Hop-Behavior” (PHB) strictly based on classification marking
  PHB does not specify mechanisms to ensure required PHB performance
  E.g.:
    Class A gets x% of bandwidth over time intervals of a specified length
    Class A packets leave before class B packets
Advantage:
No state info to be maintained by routers
DiffServ Core Functions

## Slide 17: Another approach: Intserv: QoS guarantee scenario
Resource reservation per individual application session (admission control, continuous)
call setup, signaling (RSVP)
  Maintains state a la VC (but soft state, ie times out)
    responsibility at the client to renew reservations
  Requires QoS-sensitive scheduling (e.g., WFQ)
request/
reply

## Slide 18: Roadmap
NW support for multimedia / QoS: [Ch. 9.5 (7.5 6/e) ]
Improving timing/QoS guarantees in Networks (also related with congestion-control): Packet scheduling and policing
A VC (ATM) approach [incl. Ch 3.7.2 (6e 3.62-3.6.3)]
Internet approaches
  Diff-serv, Int-serv + RSVP,
  Traffic Engineering MPLS [incl. ch. 6.5 (6/e 5.5)]
SDN [ch 4.4, 5.5 (cf separate notes @pingpong docs, if you do not have access to 7e ]
Internet-of-Things in evolution: more types of traffic/devices… [optional study, just browse example protocols mentioned]

## Slide 19: Recall the Internet approach : virtualizing networks
Gateway:
“embed internetwork packets in local packet format”
route (at internetwork level) to next gateway
ARPAnet
satellite net
gateway
Internetwork layer (IP):
addressing: internetwork appears as single, uniform entity, despite underlying local network heterogeneity
network of networks

## Slide 20: What happened? E.g. ATM: network or link layer?
Vision: end-to-end transport: “ATM from desktop to desktop”
  ATM is a network technology
Reality:
used to connect IP backbone routers ….
… or IP over ATM
replace “network” (e.g., LAN segment) with ATM network, (ATM + IP addresses)
  Run datagram routing on top of virtual-circuit routing ….
ATM
network
Ethernet
LANs

## Slide 21: Cerf & Kahn’s Internetwork Architecture
What is virtualized?
two layers of addressing: internetwork and local network
new layer (IP) makes everything homogeneous at internetwork layer
underlying local network technology
  Cable, satellite, 56K telephone modem
  Ethernet, other LAN
  ATM
  More recent: MPLS (Multiprotocol Label Switching Protocol): for traffic engineering
… “invisible” at internetwork layer. Looks like a link layer technology to IP

## Slide 22
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing approach…)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Traffic engineering: difficulties with traditional Internet routing
Notes: Note: implicit assumption here: destination based forwarding

## Slide 23
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route blue and red traffic differently?
A: can’t do it (with destination based forwarding, and LS, DV routing)
Traffic engineering: difficulties with traditional Internet routing
Notes: Note: implicit assumption here: destination based forwarding

## Slide 24: Multiprotocol label switching (MPLS) in IP networks: VC-inspired
goal: utilize multiple S-T paths simultaneously
  borrow ideas from Virtual Circuit (VC) approach but IP datagram still keeps IP address
label-switched router
  forwards packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS protocol’s forwarding table distinct from IP forwarding tables
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
S
TTL
20
3
1
5
MPLS router must co-exist
with IP-only routers

## Slide 25: MPLS versus IP paths
R2
D
R3
R4
R5
A
R6
IP-only
router
IP routing: path to destination determined by destination address alone
MPLS and
IP router
MPLS routing: path can be based on source and dest. address
  fast reroute: precompute backup routes in case of link failure or congestion (eg for CDN distribution)
entry router (R4) can use different MPLS routes to A based, e.g., on source address
(needs MPLS-capable routers)

## Slide 26: MPLS forwarding tables
R1
R2
D
R3
R4
R5
0
1
0
0
A
R6
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
10 A 0
12 D 0
1
in out out
label label dest interface
8 6 A 0
0
8 A 1
Flexibilty allows Traffic Engineering (adapting Routing to suit different purposes; relates to Software-defined Networks)

## Slide 27: Roadmap
NW support for multimedia / QoS: [Ch. 9.5 (7.5 6/e) ]
Improving timing/QoS guarantees in Networks (also related with congestion-control): Packet scheduling and policing
A VC (ATM) approach [incl. Ch 3.7.2 (6e 3.62-3.6.3)]
Internet approaches
  Diff-serv, Int-serv + RSVP,
  Traffic Engineering MPLS [incl. ch. 6.5 (6/e 5.5)]
SDN [ch 4.4, 5.5 (cf separate notes @pingpong docs, if you do not have access to 7e ]
Internet-of-Things in evolution: more types of traffic/devices… [optional study, just browse example protocols mentioned]

## Slide 28
Recall: Traditional Internet, per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 29
data
plane
control
plane
Recall: logically separated control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA
compute tables seperately
and distribute

## Slide 30: Analogy: mainframe to PC evolution*
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
* Slide courtesy: N. McKeown

## Slide 31
Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized“ flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
4. programmable control applications
routing
access control
load
balance

## Slide 32
SDN perspective: data plane switches
Data plane switches
fast, simple, for data-plane forwarding in H/W
switch flow table: computed by controller
API for table-based switch control (e.g., OpenFlow)
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 33
SDN perspective: SDN controller
SDN controller (network OS):
maintains network state information
interacts with network control applications “above” (northbound API)
interacts with network switches “below” (southbound API)
implemented as distributed system for performance, scalability, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 34
SDN perspective: control applications
network-control apps:
“brains” of control: for control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 35
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Zooming in: components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API

## Slide 36: Roadmap
NW support for multimedia / QoS: [Ch. 9.5 (7.5 6/e) ]
Improving timing/QoS guarantees in Networks (also related with congestion-control): Packet scheduling and policing
A VC (ATM) approach [incl. Ch 3.7.2 (6e 3.62-3.6.3)]
Internet approaches
  Diff-serv, Int-serv + RSVP,
  Traffic Engineering MPLS [incl. ch. 6.5 (6/e 5.5)]
SDN [ch 4.4, 5.5 (cf separate notes @pingpong docs, if you do not have access to 7e ]
Internet-of-Things in evolution: more types of traffic/devices… [optional study, just browse example protocols mentioned]

## Slide 37: Recall: Internet & its context….
approx 10 yrs ago
continuous evolution ….
Multimedia

## Slide 38: Example: Data networking technologies in Smart Grids
 | SONET - Synchronous Optical Network WDM - Wavelength Division Multiplexing Satellite/VSAT IP Radio | Twisted pair / Fiber optics BPL - Broadband over Power Lines WiMax - Worldwide Interoperability for Microwave Access GPRS | 
 | Ethernet rules~ | Ethernet rules! (IEC 61850) | Ethernet rules? Hint: not always
“Here be SCADA”
Communication
technologies
?
Communication
protocols
?
Slides: Giorgos Georgiadis

## Slide 39: Approximate overview of shaping new stacks
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoW PAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
Protocols @ Distribution’s last mile
Slides: Giorgos Georgiadis
(see extra slides for more refs&notes)

## Slide 40: Summary & Study list
Internet core and transport protocols do not provide guarantees for multimedia streaming traffic
Applications/edge take matters into own hands
  New, evolving methods; new proposals for transport protocols
Another type of service @ core (VC-like) would imply a different situation
  Internet core is re-shaping, for long time … (Intserv & Diffserv, Traffic engineering, SDN,)
Internet-of-Things in evolution
  even more types of traffic, new needs ….
NW support for multimedia / QoS: [Ch. 9.5 (7.5 6/e) ]
Improving timing/QoS guarantees in Networks (also related with congestion-control): Packet scheduling and policing
A VC (ATM) approach [incl. Ch 3.7.2 (6e 3.62-3.6.3)]
Internet approaches
  Diff-serv, Int-serv + RSVP,
  Traffic Engineering MPLS [incl. ch. 6.5 (6/e 5.5)]
SDN [ch 4.4, 5.5 (cf separate notes @pingpong docs, if you do not have access to 7e ]
Internet-of-Things in evolution: more types of traffic/devices… [optional study, just browse example protocols mentioned]

## Slide 41: Review questions
Describe the relation between bandwidth allocation and congestion control
Describe a common traffic policing mechanism and give examples of its use.
Motivate the need that led to MPLS.
Describe the concept of SDN.
SDN: what is the role of control plane, the data plane and network control applications?

## Slide 42: Extra slides/notes for further study

## Slide 43: Token bucket + WFQ…
…can be combined to provide upper bound on packet delay in queue:
bi packets in queue, packets are serviced at a rate of at least R · wi/ (wj) packets per second, then the time until the last packet is transmitted is at most
bi /(R · wi/ (wj))

## Slide 44: ATM cell (small packet)
48-byte payload
  Why?: small payload -> short cell-creation delay for digitized voice
  halfway between 32 and 64 (compromise!)
Header: 5bytes
  VCI: virtual channel ID
  PT: Payload type (e.g. Resource Management cell versus data cell)
  CLP: Cell Loss Priority bit
    CLP = 1 implies low priority cell, can be discarded if congestion
  HEC: Header Error Checksum
Cell header
Cell format

## Slide 45: ATM ABR congestion control
RM (resource management) cells:
interspersed with data cells
bits in RM cell set by switches (“network-assisted”)
  NI bit: no increase in rate (mild congestion)
  CI bit: congestion indication two-byte ER (explicit rate) field in RM cell
  congested switch may lower ER value in cell
  sender’ send rate thus minimum supportable rate on path
ABR: available bit rate:
“elastic service”
if path “underloaded”:
  sender should use available bandwidth
if path congested:
  sender throttled to minimum guaranteed rate

## Slide 46: Traffic Shaping and Policing in ATM
Enforce the QoS parameters: check if Peak Cell Rate (PCR) and Cell Delay Variation (CDVT) are within the negotiated limits:
Generic Cell Rate Algo: introduce:
expected next time for a successive cell, based on T = 1/PCR
border time L ( = CDVT) < T in which next transmission may start (but never before T-L)
A nonconforming cell may be discarded, or its Cell Loss Priority bit be set, so it may be discarded in case of congestion

## Slide 47: ATM Adaptation (Transport) Layer: AAL
”suitability” has not been very successful
computer science community introduced AAL5, (simple, elementary protocol), to make the whole ATM stack usable as switching technology for data communication under IP!
Basic idea: cell-based VCs need to be ”complemented ”to be supportive for applications.
Several ATM Adaptation Layer (AALx) protocols defined, suitable for different classes of applications
  AAL1: for CBR (Constant Bit Rate) services, e.g. circuit emulation
  AAL2: for VBR (Variable Bit Rate) services, e.g., MPEG video
  .....

## Slide 48: IP-Over-ATM
AAL
ATM
phy
phy
Eth
IP
ATM
phy
ATM
phy
app
transport
IP
AAL
ATM
phy
app
transport
IP
Eth
phy
AAL: ATM adaptation layer intended for transport layer functionality (with AAL1-4 services: cons/var/avail/undefined bit-rate traffic) but implementations did not allow such use; AAL5 made for use under IP….
felaktig dribbling

## Slide 49: RSVP: resource reservation protocol
RSVP: a leading candidate for signaling protocol
  allows reservations for bandwidth in multicast trees
  is receiver-oriented (the receiver of a
    data flow initiates and maintains the
    resource reservation for the flow).
  Maintains soft-state
    receivers renew interest regularly
  does not specify how the network
    provides the reserved bandwidth, only
    allows the applications to reserve it.
  is not a routing protocol; it depends on
    an underlying routing protocol to
    determine the routes for the flows; when a route changes,
    RSVP re-reserves resources.
  does not define the admission test, but it assumes that the routers perform such a test and that RSVP can interact with the test.

## Slide 50: Network support for multimedia

## Slide 51
Software defined networking (SDN)
Internet network layer: historically has been implemented via distributed, per-router approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different “middleboxes” for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane

## Slide 52: Data networking technologies in Smart Grids
Presentation by
Giorgos Georgiadis
(former CTH / curr. Bosch R&D)

## Slide 53: Recall: Internet & its context….
approx 10 yrs ago
continuous evolution ….
Multimedia

## Slide 54: Introduction
 | SONET - Synchronous Optical Network WDM - Wavelength Division Multiplexing Satellite/VSAT IP Radio | Twisted pair / Fiber optics BPL - Broadband over Power Lines WiMax - Worldwide Interoperability for Microwave Access GPRS | 
 | Ethernet rules~ | Ethernet rules! (IEC 61850) | Ethernet rules? Hint: not always
“Here be SCADA”
Communication
technologies
?
Communication
protocols
?
1
Fig. Giorgos Georgiadis

## Slide 55: Approximate overview of shaping new stacks
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoW PAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
Protocols @ Distribution’s last mile

## Slide 56: PHY/DataLink protocols
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LowPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
Ethernet
  Not much to say
HomePlug
  Honorable mention: popular home automation protocol
  Powerline based
  Speed: ~200mbps
  Otherwise, vanilla protocol:
    i.e. using TDMA,
    Two kinds of nodes,
    …
3

## Slide 57: PHY/DataLink protocols
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LowPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
IEEE 802.15.4
  Radio based, usually 2.4GHz
  Small packets (<=127bytes)
  Medium speed (~250kbps)
  Originally DSSS
  Topologies supported:
    Star
    Peer-to-peer
  Roles supported:
    Full-function device
    Reduced-function device
4

## Slide 58: Higher protocols
6LoWPAN
  “IPv6 over LoW Power wireless Area Networks”
  Builds on 802.15.4, IPv6
  Aimed at low power devices (sensors, controllers)
  Topologies
    Star, peer-to-peer + Mesh
  Many Challenges:
    IP packets >=1280bytes (!)
    128bit IP addresses
    …
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
5

## Slide 59: Higher protocols
ZigBee
  Builds on 802.15.4, but not IP
  Aimed at low power devices too (sensors, controllers)
    Speed 250kbps
    Packet 127bytes
    Battery powered devices (supports sleep)
  Topologies supported
    Mesh (jump to: example)
  Roles supported
    Coordinator, router, end node
  Different profiles exist:
    ZigBee Home Automation
    Zigbee Smart Energy
    Zigbee IP, ...
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
6

## Slide 60: Higher protocols
More protocols, same story:
  XMPP, BACNet, LonWorks, Modbus, …
  Wired
  Proprietary, build around specific companies (BACNet, LonWorks) or legacy protocols (Modbus)
  Today gateway devices to “break out” to Ethernet are in use
  Simple topologies (i.e bus), same roles as before
But what is the connecting thread over all?
  Open standards!
  Internet! (of Things?)
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
8

## Slide 61: Towards interoperability
OpenADR
  ADR: Advanced Metering Response
  Trying to ‘unify’ different solutions in a high level protocol
  Formalizing:
    Roles
    Messages
    Device detection
  Simple topologies (i.e bus), same roles as before
REST-based APIs
  I.e. Costrained Application Protocol
  Ultimately, HTTP-based
  Verb oriented: GET, PUT, DELETE, …
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
9

## Slide 62: Towards interoperability
Ethernet/IP-based integration
  Remember:
    Radio band: 2.4GHz (WiFI, ZigBee, 6LoWPAN)
    Similar topologies, roles
    Made for low energy devices, but flops/watt/kr increase!
    Ethernet gateways commonly used
  Solution: make them (formally) interoperable
    ZigBee Smart Energy v2.0
    ZigBee, WiFi, HomePlug on board
    6LoWPAN coming soon
OpenADR REST-based (i.e. CoAP) |  | ZigBee | 6LoWPAN | HomePlug
XMPP BACNet LonWorks Modbus | WiFi |  |  | 
Proprietary | Ethernet / Gigabit Ethernet | IEEE 802.15.4 |  | Proprietary, part 2: HomePlug
10

## Slide 63: Conclusion
Ethernet + misc communication technologies
Ethernet vs non-ethernet
  Why?
    Design for low energy devices (smaller packets, lower comm speed)
    Peer to peer, mesh topologies
  Now + Future?
    Devices’ specs catching up
    Importance of being connected (to the Internet?)
    Topologies still important (i.e. reliability)
    Will probably remain radio-based
11