## Slide 1: Course on Computer Communication and Networks Lecture 4 Chapter 3; Transport Layer, Part A
EDA344/DIT 423, CTH/GU

## Slide 2: Transport services and protocols
provide communication services to app-layer protocols
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 3: Parenthesis: On last week’s questions
Q: Types of services that a transport layer may need to provide.
  Which of those are provided by in the Internet transport layer protocols?
Services i.e. properties
  No-loss
  In-order delivery
  Timeliness i.e. latency, bandwidth guarantees

## Slide 4: Internet transport-layer protocols
Reliable, in-order delivery: TCP
also provides
  connection setup
  flow control
  + care for the health of the network (aka TCP’s congestion control)
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport
Best effort (can be unreliable, unordered) delivery: UDP
  no-frills extension of “best-effort” IP
Recall: best-effort datagram service
Transport Layer services not available in the Internet:
  Delay/bandwidth guarantees. Why?
  When the (successful due to simplicity) TCP/IP protocol stack was defined, no foreseeable need for such applications in an inter-net.

## Slide 5: Roadmap
Transport Layer: Learning goals:
understand principles of transport layer services:
  addressing, multiplexing/demultiplexing
  reliable data transfer
  flow control
  congestion control (not really a Transport-layer issue --some study in connection to transport layer since it is there in TCP; more in connection with RealTime traffic)
instantiation and implementation in the Internet
Transport layer services in Internet
Addressing, multiplexing/demultiplexing
Connectionless, unreliable transport: UDP
Principles of reliable data transfer
Next lecture: connection-oriented transport: TCP
  reliable transfer
  flow control
  connection management
  TCP congestion control

## Slide 6: Addressing: Multiplexing/demultiplexing (+ recall encapsulation)
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
gathering data, enveloping data
with header (later used for
demultiplexing)
Multiplexing at send host:
Recall: segment - unit of data exchanged between transport layer entities
  aka TPDU: transport protocol data unit

## Slide 7: Addressing
Host receives IP datagrams
  Datagram (i.e. IP packet) has source IP address, destination IP address
  datagram carries transport-layer segment
  segment has source, destination port number
Host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 8: UDP addressing – demultiplexing + example
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?
when host receives UDP segment:
directs UDP segment to socket with that port #
IP datagrams with same dest. port # (but perhaps different source IP addresses or source port numbers will be directed) to the same socket

## Slide 9: TCPConnection-oriented (TCP) addressing/demux + example
server may support many simultaneous TCP sockets:
one socket per connection
each identified by its own 4-tuple
E.g. web servers have different sockets for each connecting client
TCP socket identified by 4-tuple:
source IP address, source port number
dest IP address, dest port number
transport
application
physical
link
network
P3
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
client: IP address A
client: IP address C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
server: IP address B
(Demux) Receiver uses all 4 values to direct segment to appropriate socket

## Slide 10: TCP demux: Threaded web server
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server

## Slide 11: Roadmap
Transport layer services
Addressing, multiplexing/demultiplexing
Connectionless, unreliable transport: UDP
principles of reliable data transfer
Next lecture: connection-oriented transport: TCP
  reliable transfer
  flow control
  connection management
  TCP congestion control

## Slide 12: UDP: User Datagram Protocol [RFC 768]
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others

## Slide 13: UDP: segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP datagram format
length
checksum
length, in bytes of UDP datagram, including header
Must do the addressing job
no connection establishment (which could add delay)
simple: no connection state at sender, receiver
small header size
no congestion control: UDP can blast away segments faster (than TCP)
why is there a UDP?
UDP used by:
DNS
SNMP
More discussion later…

## Slide 14: UDP Checksum[RFC 1071]: check bit flips
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
Wraparound:
Add to final
sum
checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum == checksum field value:
  NO - error detected (report error to app or discard)
  YES - no error detected.
    But maybe (rarely) errors nonetheless? More later ….
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 15: Roadmap
Transport layer services
Addressing, multiplexing/demultiplexing
Connectionless, unreliable transport: UDP
principles of reliable data transfer
Next lecture: connection-oriented transport: TCP
  reliable transfer
  flow control
  connection management
  TCP congestion control

## Slide 16: Principles of reliable data transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
top-10 list of important networking topics!

## Slide 17: Reliable data transfer (RDT): getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 18: RDT:
A sends one page at a time;
How do A & B do their job if MMS connection…
…is reliable?
…might introduce errors?
…might lose MMSs?
S application: Author
Writes and Sends pages
R application: publisher
Receives & publishes written pages
S transport: secretary Alice
Must send pages on behalf of author
S transport: secretary Bob
Receives pages;
Must pass on to publisher in-order
Bidirectional 1-page-at-a-time-MMS connection

## Slide 19: Reliable data transfer: getting started
We will:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
use finite state machines (FSM) to specify sender, receiver behaviour
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 20: rdt1.0: reliable transfer & reliable channel
underlying channel perfectly reliable
  no bit errors, no loss of packets
separate FSMs for sender, receiver:
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 21: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
New mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  feedback: control msgs (ACK,NAK) from receiver to sender

## Slide 22: rdt2.0: FSM specification
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L

## Slide 23: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 24: rdt2.0: error scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 25: Recall: RDT (Reliable Data Transfer, aka error control)
A sends one page at a time;
How do A & B do their job if MMS connection…
…is reliable?
…might introduce errors?
…might lose MMSs?
S application: Author
Writes and Sends pages
R application: publisher
Receives & publishes written pages
S transport: secretary Alice
Must send pages on behalf of author
S transport: secretary Bob
Receives pages;
Must pass on to publisher in-order
Bidirectional 1-page-at-a-time-MMS connection

## Slide 26: rdt3.0: channels with errors and loss
We saw: how ack+retransmit can solve problems with errors
New assumption: underlying channel can also lose packets (data, ACKs)
approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
  requires countdown timer

## Slide 27: Recall: RDT (Reliable Data Transfer, aka error control)
A sends one page at a time;
How do A & B do their job if MMS connection…
…is reliable?
…might introduce errors?
…might lose MMSs?
  (lost vs too late MMS?)
S application: Author
Writes and Sends pages
R application: publisher
Receives & publishes written pages
S transport: secretary Alice
Must send pages on behalf of author
S transport: secretary Bob
Receives pages;
Must pass on to publisher in-order
Bidirectional 1-page-at-a-time-MMS connection

## Slide 28: rdt3.0 (cont) : channels with errors and loss
We saw: how ack+retransmit can solve problems with errors
New assumption: underlying channel can also lose packets (data, ACKs)
approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
  requires countdown timer
if pkt (or ACK) just delayed (not lost):
  Must handle duplicates ->
handling duplicates:
sender adds sequence number to each pkt
receiver discards (doesn’t deliver upwards) duplicate pkt
For stop&wait 0-1 (ie 1 bit) enough for sequence nr.

## Slide 29: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 30: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1
pkt0
ack1
ack0
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
rcv pkt0
send ack0
(detect duplicate)

## Slide 31: Roadmap
Transport layer services in Internet
Addressing, multiplexing/demultiplexing
Connectionless, unreliable transport: UDP
principles of reliable data transfer
  Efficiency perspective
Next lecture: connection-oriented transport: TCP
  reliable transfer
  flow control
  connection management
  TCP congestion control

## Slide 32: Performance of rdt3.0 (stop&wait)
rdt3.0 is correct, but performance stinks
e.g.: 1 Gbps channel, 15 ms prop. delay, 8000 (1KB) bit packet:
Dtrans =
L
R
8000 bits
109 bits/sec
=
=
8 microsecs
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 33: Performance of rdt3.0 (cont)
  Utilization (fraction of time sender busy sending, or fraction of utilized bandwidth ):
Ie  approx. 300 kbps effective throughput over a 1 Gbps channel
network protocol limits use of physical resources!

## Slide 34: Is RDT necessarily that slow/inefficient?

## Slide 35: Pipelined protocols
pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver

## Slide 36: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!

## Slide 37: Pipelined protocols: ack-based error control
if data is lost, two generic forms of pipelined protocols: go-Back-n, selective repeat

## Slide 38: Go-Back-n: sender
“window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs
timer for oldest in-flight pkt
timeout(n): retransmit packet n and all higher seq # pkts in window

## Slide 39: GBn in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
https://media.pearsoncmg.com/aw/ecs_kurose_compnetwork_7/cw/content/interactiveanimations/go-back-n-protocol/index.html

## Slide 40: Selective repeat: sender, receiver windows
receiver individually acknowledges received pkts
  buffers pkts for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  Requires timer for each unACKed pkt

## Slide 41: Selective repeat
…data from above:
if next_pkt_seq # in window, send pkt
…timeout(n):
resend pkt n, restart timer
…ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
Sender: upon…
… pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
If out-of-order: buffer
If in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
…pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
Receiver: upon receiving…

## Slide 42: Selective repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
X
loss
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
record ack3 arrived
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
record ack4 arrived
record ack5 arrived
Q: what happens when ack2 arrives?
https://media.pearsoncmg.com/aw/ecs_kurose_compnetwork_7/cw/content/interactiveanimations/selective-repeat-protocol/index.html

## Slide 43: Roadmap
Transport layer services in Internet
Addressing, multiplexing/demultiplexing
Connectionless, unreliable transport: UDP
principles of reliable data transfer
  Efficiency perspective: pipelined protocols & error control through go-back-n, selective-repeat
    Sequence numbers
Next: connection-oriented transport: TCP
  reliable transfer
  flow control
  connection management
  TCP congestion control

## Slide 44: Selective repeat: Sequence numbers
example:
seq #’s: 0, 1, 2, 3
window size=3
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
receiver can’t see sender side.
receiver behavior identical in both cases!
something’s (very) wrong!
duplicate data accepted as new in (b)
Q: what relationship between seq # size and window size to avoid problem in (b)?

## Slide 45: Roadmap
Transport layer services
Addressing, multiplexing/demultiplexing
Connectionless, unreliable transport: UDP
principles of reliable data transfer
Next: connection-oriented transport: TCP
  reliable transfer
  flow control
  connection management
  TCP congestion control

## Slide 46: Reading instructions chapter 3
KuroseRoss book
Other resources (further, optional study)
  Lakshman, T. V., Upamanyu Madhow, and Bernhard Suter. "Window-based error recovery and flow control with a slow acknowledgement channel: a study of TCP/IP performance." INFOCOM'97. Sixteenth Annual Joint Conference of the IEEE Computer and Communications Societies. Proceedings IEEE. Vol. 3. IEEE, 1997.
  Rizzo, Luigi. "Effective erasure codes for reliable computer communication protocols." ACM SIGCOMM Computer Communication Review 27.2 (1997): 24-36.
  A. Agarwal and M. Charikar, “On the advantage of network coding for improving network throughput,” in Proceedings of the IEEE Information Theory Workshop, Oct. 2004
  Harvey, N. J., Kleinberg, R., & Lehman, A. R. (2006). On the capacity of information networks. IEEE/ACM Transactions on Networking (TON), 14(SI), 2345-2364.
Careful | Quick
3.1, 3.2, 3.4-3.7 | 3.3

## Slide 47: Some review questions on this part
Why do we need an extra protocol, i.e. UDP, to deliver the datagram service of Internets IP to the applications?
Draw space-time diagrams without errors and with errors, for the following, for a pair of sender-receive S-R: (assume only 1 link between them)
  Stop-and-wait: transmission delay < propagation delay and transmission delay > propagation delay
  Sliding window aka pipelined protocol, with window’s transmission delay < propagation delay and window’s transmission delay > propagation delay; illustrate both go-back-n and selective repeat when there are errors
  Show how to compute the effective throughput between S-R in the above cases, when there are no errors
What are the goals of reliable data transfer?
Reliable data transfer: show why we need sequence numbers when the sender may retransmit due to timeouts.
Show how there can be wraparound in a reliable data transfer session if the sequence-numbers range is not large enough.
Describe the go-back-N and selective repeat methods for reliable data transfer

## Slide 48: Extra slides, for further study

## Slide 49: Bounding sequence numbers for stop-and-wait…
… s.t. no wraparound, i.e. we do not run out of numbers: binary value suffices for stop-and-wait:
Proof sketch: assume towards a contradiction that there is wraparound when we use binary seq. nums.
  R expects segment #f, receives segment #(f+2):
    R rec. f+2 => S sent f+2 => S rec. ack for f+1
    => R ack f+1=> R ack f => contradiction
  R expects f+2, receives f:
    R exp. f+2 => R ack f+1 => S sent f+1
    => S rec. ack for f => contradiction

## Slide 50: rdt2.0 has an issue ….
what happens if ACK/NAK corrupted?
sender uncertain what happened at receiver!
Can retransmit : BUT WATCH: possible duplicates!
handling duplicates:
sender retransmits current pkt if hears nothing
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
stop and wait
sender sends one packet,
then waits for receiver
response

## Slide 51: rdt2.1: sender, handles garbled ACK/NAKs
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L

## Slide 52: rdt2.1: receiver, handles garbled ACK/NAKs
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 53: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “expected” pkt should have seq # 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 54: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 55: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L