## Slide 1: Course on Computer Communication and Networks Lecture 6 Network Layer – part 1: Data Plane Chapter 4 (7/e) (6/e Ch4-first part)
EDA344/DIT 423, CTH/GU

## Slide 2: From last week’s review questions
Q: Can an application have reliable data transfer over UDP? If yes how? If no, why?
Student correct A: Yes, if the application layer itself takes care of all the extra functions needed to add reliability on top of UDP’s service
Q: How can an ACK have the same number in the same TCP session?
Student correct A: The ACK will have the same number if the package after [the first acknowledged one] it was lost [or arrives out of order]. The ACK is then retransmitted.
Q: Can a TCP’s session sending rate increase indefinitely?
Student correct A: …there are several limits, how fast the receiver can receive, if a sequence is lost then the sending rate will be halved, and also the limits of the hardware
Student Q: Some people argue that the network layer is more correctly called the internet layer. Why do we use the term network layer instead?

## Slide 3: The Internet: bridging networks
Gateway:
“embed internetwork packets in local packet format”
route (at inter-network level) to next gateway
ARPAnet
satellite net
gateway
Internetwork layer (IP main “actor”):
internetwork appears as single, uniform entity, despite underlying local network heterogeneity
network of networks

## Slide 4: Network layer
Consider transporting a segment from Sender to Receiver
S: encapsulates segments into datagrams
R: delivers segments to transport layer
network layer protocols in every host, router
  examine headers in all datagrams passing through
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 5
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
a b c d
a’ b’ c’ d’
a” b” c” d”
1
2
3
NW layer’s actual job - routing and forwarding
Interplay between the two:
routing algorithm determines
path through network
(control-plane functionality)
forwarding table determines
local forwarding at this router
(data-plane functionality)

## Slide 6: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router: switching fabrique
The Internet Network layer: IP, Addressing & related
(Next) Control, routing
  path selection
  instantiation, implementation in the Internet

## Slide 7: Network service model
Q: What service model for “channel” carrying packets from sender to receiver?
(general networking scope, ie not only Internet-scope)
example services for individual packets:
guaranteed delivery
guaranteed delivery with less than 40 msec
example services for a flow of packets:
in-order delivery
guaranteed min/avg/max arrival rate to flow
datagram network provides network-layer connectionless service
  classic Internet model
virtual-circuit network can provide network-layer connection-oriented service
  not present in classic Internet protocols but efforts to simulate behaviour are being made

## Slide 8: Virtual circuits:
“source-to-dest path behaves almost like telephone circuit”
call setup, teardown for each call before data can flow
  signaling protocols to setup, maintain, teardown VC (ATM, frame-relay, X.25; not in IP)
each packet carries VC identifier (not destination host)
every router maintains “state” for each passing connection
resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 9: Virtual Circuits forwarding table
1
2
3
Incoming VC# in packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
VC routers must maintain
connection state information!

## Slide 10: Datagram networks (the Internet model)
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using only destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 11: Datagram (IP) forwarding table
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so rather than list individual destination address
list range of addresses
(aggregate table entries)

## Slide 12: Datagram or VC network: why?
“Classic” Internet (datagram)
data exchange among computers
  “elastic” service, no strict timing req.
many link types
  different characteristics
  uniform service difficult
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple network core, complexity at edge
VC (eg ATM: a past’s vision of the future’s ww-network)
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  “Classic” telephones
  complexity in the core of network
Re-shaping in progress ….
Software-Defined Networks

## Slide 13: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
How a router works: switching fabrique
The Internet Network layer: IP, Addressing & related
(Next) Control, routing
  path selection
  instantiation, implementation in the Internet

## Slide 14
Per-router (“classic” Internet) control plane
Routing
Algorithm
Individual routing algorithm (control) components in each and every router interact (in the control plane)
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 15
data
plane
control
plane
Logically separated control plane
A distinct (can be centralized/remote/distributed) controller interacts with local control agents (CAs)
  this architecture (Software Defined Networking) can enable new functionality
  (will be discussed more later in the course)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving packet header [more values than just the destination address can be used for the forwarding]

## Slide 16: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related
(Next) Control, routing
  path selection
  instantiation, implementation in the Internet

## Slide 17: Router architecture overview
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware)
routing, management
control plane (software)
forwarding tables computed,
pushed to input ports

## Slide 18: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
switching:
given datagram dest., lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
switch
fabric

## Slide 19: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics:
memory
memory
bus
crossbar

## Slide 20: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 21: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 22: Switching Via an Interconnection Network
Overcome bus bandwidth limitations
Banyan networks, other interconnection nets (also used in multi-processors-memory interconnects)
  Cisco 12000: switches at 60 Gbps
  Example Banyan interconnect: using 3-bit link address
crossbar

## Slide 23: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance
(vs network neutrality)

## Slide 24: Example contemporary routers
Cisco Catalyst 3750E
Stackable (can combine units) 64 Gbps bandwidth
13 Mpps (packets per second)
12,000 address entries
Price: from 100 kSEK
HP ProCurve 6600-24G-4XG Switch
10 Gbps
Up to 75 Mpps (64-byte packets)
Latency: < 2.4 µs (FIFO 64-byte packets) 10,000 address entries
Price approx. 50 kSEK
Notes: TO

## Slide 25: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
How a router works
The Internet Network layer: IP, Addressing & related
(Next) Control, routing
  path selection
  instantiation, implementation in the Internet

## Slide 26: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 27: IPv4 datagram format
ver
length
32 bits
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head. len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
data
(variable length,
typically a TCP
or UDP segment)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data (prio)
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 28: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
How a router works
The Internet Network layer: IP, Addressing & related
  Hierarchical addressing
(Next) Control, routing
  path selection
  instantiation, implementation in the Internet

## Slide 29: IP addressing: introduction
IP address: 32-bit id for host/router interface
interface: connection between host/router and physical link
  routers have multiple interfaces
  end-host typically has 1-2 interfaces (e.g., wired Ethernet and wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 30: Subnets
IP address:
  subnet part: high order bits (variable number)
  host part: low order bits
what’s a subnet ?
  Devices that can physically reach each other without intervening router
  device interfaces have same subnet-part (prefix) of IP address
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 31: Subnets
recipe
to determine the subnets: detach each interface from its host or router, i.e. create islands of isolated networks
each isolated network is a subnet
subnet mask: eg /24
defines how to find the subnet part of the address …
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 32: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 33: Subnets, masks, calculations
Example subnet: 192.168.5.0/24
 | Binary form | Dot-decimal notation
IP address | 11000000.10101000.00000101.10000010 | 192.168.5.130
Subnet mask | 11111111.11111111.11111111.00000000 --------24 first bits set to 1------ | 255.255.255.0
Network prefix: bitwise AND of (address, mask) | 11000000.10101000.00000101.00000000 | 192.168.5.0
Host part (obtained with similar calculation, with a mask having the 8 last bits = 1) | 00000000.00000000.00000000.10000010 | 0.0.0.130

## Slide 34: CIDR Address Masks
34
CIDR Notation Dotted Decimal
/1 128.0.0.0
/2 192.0.0.0
/3 224.0.0.0
/4 240.0.0.0
/5 248.0.0.0
/6 252.0.0.0
/7 254.0.0.0
/8 255.0.0.0
/9 255.128.0.0
/10 255.192.0.0
/11 255.224.0.0
/12 255.240.0.0
/13 255.248.0.0
/14 255.252.0.0
/15 255.254.0.0
/16 255.255.0.0
CIDR Notation Dotted Decimal
/17 255.255.128.0
/18 255.255.192.0
/19 255.255.224.0
/20 255.255.240.0
/21 255.255.248.0
/22 255.255.252.0
/23 255.255.254.0
/24 255.255.255.0
/25 255.255.255.128
/26 255.255.255.192
/27 255.255.255.224
/28 255.255.255.240
/29 255.255.255.248
/30 255.255.255.252
/31 255.255.255.254
/32 255.255.255.255
2013 Ali Salehson, Chalmers, CSE Networks and Systems

## Slide 35: Classless Address: example
35
    An ISP has an address block 122.211.0.0/16
    A customer needs max. 6 host addresses,
    ISP can e.g. allocate: 122.211.176.208/29
      3 bits enough for host part
    subnet mask 255.255.255.248
 | Dotted Decimal | Last 8 bits
Network | 122.211.176.208 | 11010000
1st address | 122.211.176.209 | 11010001
…………. | ………………… | …………
6th address | 122.211.176.214 | 11010110
Broadcast | 122.211.176.215 | 11010111
Reserved addresses
RFC 3021 “The network address itself {<Network-number>, 0} is an
obsolete form of directed broadcast, but it may still be used by older hosts.”

## Slide 36: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
How a router works
The Internet Network layer: IP, Addressing & related
  Hierarchical addressing
  How to get addresses
(Next) Control, routing
  path selection
  instantiation, implementation in the Internet

## Slide 37: IP addresses: how to get one (for an end-host)?
hard-coded by system admin in a file
Windows: control-panel->network->configuration->tcp/ip->properties;
UNIX: /etc/rc.config
DHCP returns more than just allocated IP address:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)
DHCP: Dynamic Host Configuration Protocol: dynamically get address:
  host broadcasts “DHCP discover” msg
  DHCP server (in same subnet) responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg
DHCP

## Slide 38: IP addresses: how to get one (net-part)?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space; eg:
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23
3 bits, 8 networks

## Slide 39: Hierarchical Addressing: Route Aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP #1
Organization 0
Organization 7
Internet
Organization 1
ISP #2
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing information
The “outside” does not need to know about subnets.

## Slide 40: Forwarding: longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
longest prefix matching
Link interface
0
1
2
3

## Slide 41: IP Addressing: the last word...
Q: How does an ISP get block of addresses?
A: ICANN: http://www.icann.org/
Internet Corporation for Assigned Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes
ISPs obtain IP addresses from a
Local Internet Registry (LIR) or
National Internet Registry (NIR),
their appropriate Regional Internet Registry (RIR, 5 worldwide).

## Slide 42: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
How a router works
The Internet Network layer: IP, Addressing & related
  Hierarchical addressing
  How to get addresses
  NAT
(Next) Control, routing
  path selection
  instantiation, implementation in the Internet

## Slide 43: (Well, it was not really the last word…) NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or destination in this
network have 10.0.0/24 address for source,
destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7, different source port numbers
(it is all about extending the IP address space; it also “hides” addresses)

## Slide 44: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 45: NAT: network address translation
16-bit port-number field:
  64k simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should in principle process up to layer 3
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  address shortage should instead be solved by IPv6

## Slide 46: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
How a router works
The Internet Network layer: IP, Addressing & related
  Hierarchical addressing
  How to get addresses
  NAT
  IPv6
(Next) Control, routing
  path selection
  instantiation, implementation in the Internet

## Slide 47: IPv6: motivation
initial motivation: 32-bit address space almost completely allocated.
additional motivation: header format must help to:
  speed processing/forwarding
  distinguishing types of traffic (for potentially different services)
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed
  128-bit addresses (2128 = 1038 hosts)
  Standard subnet size: 264 hosts

## Slide 48: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field

## Slide 49: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  how can the network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram

## Slide 50: Tunneling (6in4 – static tunnel)
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4
Notes: Mod TO – real solution is Teredo RFC 4380, where [D+E] is a Teredo server and the tunnel uses UDP port 3544. Supported by most modern systems.

## Slide 51: IPv6: adoption
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  20 years and counting!
  think of application-level changes in last 20 years: www, streaming media, social media, skype, …
  Why?

## Slide 52: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
How a router works
The Internet Network layer: IP, Addressing & related
  Hierarchical addressing
  How to get addresses
  NAT
  IPv6
(Next) Control, routing
  path selection
  instantiation, implementation in the Internet

## Slide 53: Reading instructions Network Layer (incl. next lecture)
KuroseRoss book
Careful | Quick
6/e: 4.1-4.6 7/e: 4.1-4.3, 5.2-5.4, 5.5, 5.6, [new- SDN, data and control plane 4.4, 5.5: in subsequent lectures, connecting to multimedia/streaming Study material available through the pingpong-system] | 6/e: 4.7 7/e: 5.7

## Slide 54: Review questions for this part
network layer service models
  Contrast virtual circuit and datagram routing (simplicity, cost, purposes, what service types they may enable)
forwarding versus routing
  Explain the interplay between routing and forwarding
how a router works
  What is inside a router? How/where do queueing delays happen inside a router? Where/why can packets be dropped at a router?
What is subnet? What is subnet masking?
  Practice masking calculations, dividing address spaces
Explain how to get an IP packet from source to destination
Explain how NAT works.

## Slide 55: Some complementary material /video-links
IP addresses and subnets http://www.youtube.com/watch?v=ZTJIkjgyuZE&list=PLE9F3F05C381ED8E8&feature=plcp
How does PGP choose its routes http://www.youtube.com/watch?v=RGe0qt9Wz4U&feature=plcp
Some taste of layer 2: no worries if not all details fall in place, need the lectures also to grasp them.
Hubs, switches, routers http://www.youtube.com/watch?v=reXS_e3fTAk&feature=related
What is a broadcast + MAC address http://www.youtube.com/watch?v=BmZNcjLtmwo&feature=plcp
Broadcast domains: http://www.youtube.com/watch?v=EhJO1TCQX5I&feature=plcp

## Slide 56: Extra slides

## Slide 57: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?
Internet models being extented
(will study these later on)

## Slide 58: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 59: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets move
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 60: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 61: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0 (your IP addr)
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Q:Why a request msg?
Several DHCP servers may answer and offer addresses
Notes: Mod TO

## Slide 62: NAT traversal problem
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible address: 138.76.29.7
solution1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (123.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
Solution 2: automate the above through a protocol (universal plug-and-play)
Solution 3: through a proxy/relay (will discuss in connection to p2p applications)
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
client
?

## Slide 63: NAT traversal problem
solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATed host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration
10.0.0.1
NAT
router
IGD

## Slide 64: NAT traversal problem
solution 3 (application): relaying (used in Skype)
  NATed server establishes connection to relay
  External client connects to relay
  relay bridges packets between two connections
10.0.0.1
NAT
router
138.76.29.7
Client
1. connection to
relay initiated
by NATted host
2. connection to
relay initiated
by client
3. relaying
established

## Slide 65: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits to identify + order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 66: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 67: Getting a datagram from source to dest.

## Slide 68: Getting a datagram from source to dest.
IP datagram:
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
misc
fields
source
IP addr
dest
IP addr
data
datagram remains unchanged, as it travels source to destination
addr fields of interest here
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
forwarding table in A

## Slide 69: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
look up net. address of B
find B is on same net. as A (B and A are directly connected)
link layer will send datagram directly to B (inside link-layer frame)
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
misc
fields
223.1.1.1
223.1.1.3
data

## Slide 70: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
Starting at A, dest. E:
look up network address of E
E on different network
routing table: next hop router to E is 223.1.1.4
link layer is asked to send datagram to router 223.1.1.4 (inside link-layer frame)
datagram arrives at 223.1.1.4
continued…..
misc
fields
223.1.1.1
223.1.2.3
data

## Slide 71: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Arriving at 223.1.4, destined for 223.1.2.2
look up network address of E
E on same network as router’s interface 223.1.2.9
  router, E directly attached
link layer sends datagram to 223.1.2.2 (inside link-layer frame) via interface 223.1.2.9
datagram arrives at 223.1.2.2!!! (hooray!)
misc
fields
223.1.1.1
223.1.2.3
data
network router Nhops interface
223.1.1 - 1 223.1.1.4
223.1.2 - 1 223.1.2.9
223.1.3 - 1 223.1.3.27
Dest. next