## Slide 1: Course on Computer Communication and Networks Lecture 1 Chapter 1: Introduction Part A: Internet, Protocol Layering and Data
CTH EDA344/ GU DIT 420

## Slide 2: Roadmap
What’s the Internet
  Nuts&bolts view
  Service view
  Distinction between network edge and network core
Layers of abstraction, protocols
ISO/OSI & Internet layer structure
Data communication through layers: physical and logical view

## Slide 3: the Internet: “nuts and bolts” view (1)
millions of connected (computing) devices: hosts = end systems
  running network apps
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
fiber, copper, radio, satellite
transmission rate = bandwidth
Connecting devices, eg routers: forward packets (chunks of data)

## Slide 4: ”Fun” internet appliances in “Internet of things”
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Tweet-a-watt:
monitor energy use

## Slide 5: the Internet: “nuts and bolts” view (2)
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, Ethernet
Internet: “network of networks”
  loosely hierarchical
Home network
Institutional network
Mobile network
Global ISP
Regional ISP

## Slide 6: the Internet: service view
communication infrastructure enables distributed applications:
  Web, VoIP, email, games, e-commerce, file sharing
communication services provided to apps:
  Reliable, in-order data delivery from source to destination
  “best effort” (unreliable) data delivery

## Slide 7: A closer look at (any big) network’s structure:
network edge: applications and hosts
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks

## Slide 8: Roadmap
What’s the Internet
  Nuts&bolts view
  Service view
  Distinction between network edge and network core
Layers of abstraction, protocols
ISO/OSI & Internet layer structure
Data communication through layers: physical and logical view

## Slide 9
Networks are complex and evolving….
  Hosts, routers, links
  Services, applications
  Hardware, software
  Networks of Networks
  ….
Question:
Is there any hope of organizing structure, study, development of networks?

## Slide 10: Terminology: Layers, Protocols, Interfaces
Layer n on a host carries a conversation with layer n on another host
  host-to-host interface: defines messages exchanged with peer entity
  Logical communication, protocol
  Each layer implements services
  via its own internal-layer actions
  relying on services by layer below
  It provides services to the upper layer (shielding from implementation details)
  service interface: across layers in same host
Fig. A. Tanenbaum Computer Networks
  Logical communication, protocol
  Logical communication, protocol
  Logical communication, protocol

## Slide 11: What’s a protocol?
Examples: a human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
req.
TCP connection
reply.
Get http://gaia.cs.umass.edu/index.htm
<file>
time
host-to-host interface: defines
messages exchanges with peer entity: format, order of msgs
actions todo on msg transmission, receipt

## Slide 12: Another example: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
System architecture: set of layers, interfaces
Protocol stack: protocol implementation

## Slide 13: Why layering?
Dealing with complex systems:
structure allows to identificaty & relate of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance/es
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system

## Slide 14: Roadmap
What’s the Internet
  Nuts&bolts view
  Service view
  Distinction between network edge and network core
Layers of abstraction, protocols
ISO/OSI & Internet layer structure
Data communication through layers: physical and logical view

## Slide 15: Layering – Some “history”: The OSI Reference Model
ISO (International Standards Organization) defined the OSI (Open Systems Interconnect) model to help vendors create interoperable network implementation
``X dot" series (X.25, X. 400, X.500) OSI model implementation (protocol stack)
Fig. Steen, Sips : Computer and Network organization

## Slide 16: Internet protocol stack layers&protocols
Application: protocols supporting network applications
  http (web), smtp (email), p2p, streaming…
transport: process2process (end2end) data transfer protocols
  UDP, TCP
network: routing of datagrams (independent data-packets), connecting different physical networks
  IP addressing, routing protocols, virtualization, virtualization, virtualization……
link: protocols for data transfer between neighboring ( ie physically connected) network nodes
  Ethernet, WiFi, …
physical: protocols for bit-transmission/receipt on the physical medium between neighboring network nodes
application
transport
network
link
physical
UDP
TCP

## Slide 17: Internet protocol stack
Architecture simple but not as thoroughly thought as OSI‘s
  no clear distinction between interface-design and implementations;
Internet stack “missing”:
  Presentation layer: interpret meaning of data, e.g., encryption, compression,
  Session layer: synchronization, checkpointing, …
  Transport protocols with timing guarantees
  these services, if needed, must be implemented in application
Successful protocol suite (de-facto standard)
  was there when needed (OSI implementations were too complicated)
  freely distributed with UNIX
Accumulating some “fat” around its waist though…
Internet standards
RFC: Request for comments
IETF: Internet Engineering Task Force

## Slide 18: Roadmap
What’s the Internet
  Nuts&bolts view
  Service view
  Distinction between network edge and network core
Layers of abstraction, protocols
ISO/OSI & Internet layer structure
Data communication through layers: physical and logical view

## Slide 19: Layered communication: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
Logical communication
Physical communication

## Slide 20: Chapter 1a: Summary
We discussed
what’s the Internet
what’s a protocol?
protocol layers, service models
We will continue (next lecture) with
Network edge & network core services & functionality overview
More on Internet structure overview
  access nets, physical media
  backbones, NAPs, ISPs
Performance concerns: delays, loss
Security concerns
To provide :
context, overview, “feel” of networking
A point of reference for context in the “zoom-in” discussions to come

## Slide 21: Reading instructions (incl.next lecture)
Careful | Quick
6/e, 7/e: 1.3, 1.4, 1.5 | the rest
1. Kurose Ross book
Extra Reading (optional)
Computer and Network Organization: An Introduction,
by Maarten van Steen and Henk Sips, Prentice Hall
(very good introductory book for non-CSE students)

## Slide 22: Review questions
Review questions from Kurose-Ross book, chapter 1 (for basic study)
6/e, 7/e: R11, R12, R13, R16, 17, R18, R19, R20, R21, R22, R23, R24, R25, R28.
Extra questions, for further study: delay analysis in packet switched networks:
http://www.comm.utoronto.ca/~jorg/teaching/ece466/material/466-SimpleAnalysis.pdf