## Slide 1: An Introduction to Software-Defined Networking (SDN)
Zhang Fu
Ericsson Research

## Slide 2: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
Use cases
Challenges and research problems
Little touch on Openflow

## Slide 3: Reviewing traditional networking
Network layers
Application layer
transport layer
network layer
Data-link layer
physical layer
Application layer
transport layer
network layer
Data-link layer
physical layer
source
destination
Why layers? Good abstraction, transparency…
switch
router

## Slide 4: Reviewing traditional networking
Design principles of Internet
  Simple
  Intelligent end-points
  Distributed control
Resulting in huge complex network and hard to manage
Billions of computers
Tens of thousands of ASes
Great business for selling routers

## Slide 5: Reviewing traditional networking
Complex routers
Million of lines of source code
Hard to extend
Tens of billions of transistors
10Gbytes RAM
Power Hungry
Vertically integration with many complex functions: OSPF, BGP, multicast, QoS, Traffic Engineering, NAT, firewalls, MPLS…
Hardware
Router
Software

## Slide 6: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
Use cases
Challenges and research problems
Little bite of Openflow

## Slide 7: Example: oscillation problem
Link cost equals the amount of carried traffic
A
D
C
B
1
1+e
e
0
e
1
1
0
0
initially
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
A
D
C
B
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
How to achieve optimal routing dynamically?

## Slide 8: Traffic engineering: difficult
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 9: Traffic engineering: difficult
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route yellow and red traffic differently?
A: can’t do it (with destination based forwarding, and LS, DV routing)
Notes: Note: implicit assumption here: destination based forwarding

## Slide 10: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
Use cases
Challenges and research problems
Little touch on Openflow

## Slide 11: Software development VS Network diagnosing
Various tools for code analysis, verification, debugging
Software Specification
Testing
Coding
Diagnosing tools? Ping, traceroute, SNMP
Networking Specification
Testing ?
Coding ?
The life cycle for network protocols is much longer than that for software
Timely research does not find its way into practice

## Slide 12: Network substrate
We want to mimic the success in software industry
  Has simple common substrate
  Building OS on top the hardware, which enables easy deployment of networking applications
SDN
A network in which the control plane is physically separate from the data plane.
A single control plane controls several forwarding devices.

## Slide 13: Network substrate
Router Example
  Basic job of the router: receiving packets, checking the routing table, forwarding the packets out
  In order to build the routing table, the router has to understand BGP, OSPF, RIP, etc.
  What about getting the routing table from somewhere else?

## Slide 14: Separate data and control plane
hardware
software
hardware
software
hardware
software
hardware
software

## Slide 15: Separate data and control plane
hardware
hardware
hardware
hardware
software
software
software
software
Control plane

## Slide 16: Separate data and control plane
hardware
hardware
hardware
hardware
Control plane

## Slide 17: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
Use cases
Challenges and research problems
Little touch on Openflow

## Slide 18: SDN architecture

## Slide 19: SDN architecture
The data plane consists of network elements, which expose their capabilities to the control plane via southbound interface
The SDN applications are in the application plane and communicate their network requirements toward the control plane via northbound interface
The control plane sits in the middle
  translate the applications’ requirements and exerts low-level control over the network elements
  Provide network information to the applications
  Orchestrate different applications

## Slide 20: Data-plane
Data sources and sinks
Traffic forwarding/processing engine
  May have the ability to handle some types of protocol, e.g. ARP, LLDP.
Provide interfaces communicating to the control plane
  Programmatic control of all functions offered by the network element
  Capability advertisement
  Event notification

## Slide 21
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 22: Control-plane
Logically centralized
Core functionality
  Topology and network state information
  Device discovery
  Path computation
  Security mechanism
Coordination among different controllers
Interfaces to the application plane

## Slide 23
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API

## Slide 24: Application-plane
Applications specify the resources and behaviors required from the network, with the context of business and policy agreement
It may need to orchestrate multiple-controllers to achieve the objectives, (Cloudify, Unify)
Programming languages help developing applications.

## Slide 25
SDN perspective: control applications
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SND controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 26: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
Use cases
Challenges and research problems
Little touch on Openflow

## Slide 27: Use cases
Traffic engineering
  Avoid congestion
  Adaptive to different policies, QoS
Mobility and wireless
  Seamless mobility
  SDN based Core network
Security
  Packets going through a set checking boxes
Data center networking
  Enhancing link utilization
  Saving energy

## Slide 28: Example: mitigating attacks
Checking the validity of packets by middle boxes
Internet
How to route the packets through a series of middle boxes?

## Slide 29: Example: service chaining
DPI
FW
NAT
Cache
Proxy
IDS
Internet
Operator network
DPI
FW
NAT
Cache
Proxy
IDS
Operator network
SFF
SFF
Internet

## Slide 30: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
Use cases
Challenges and research problems
Little touch on Openflow

## Slide 31: Challenges and research problems
Switch design
  Find common abstraction
  Flow table capacity
  Throughput
Controller platform
  Distributed vs centralized
  Flexibility
Dependability and security
  Attack to data plane
  Attack to control plane
  Trust, privacy issues

## Slide 32: Roadmap
Reviewing traditional networking
Examples for motivating SDN
Enabling networking as developing softwares
SDN architecture
Use cases
Challenges and research problems
Little touch on Openflow

## Slide 33: Openflow
An southbound standard:
Provide specification to implement Openflow-enabled forwarding devices
Communication channel between data and control plane
  TCP used to exchange messages
New versions are keeping released

## Slide 34: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 35: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller

## Slide 36: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
OpenFlow Controller

## Slide 37: In-band VS out-band Control
How to setup the communication channels between the SWs and the controller?
  Out-band control: building a separate network connecting management ports of SDN switches with the controller. This network is out of the control by the SDN switches. It has to implement traditional L2/L3 routing protocols.
  In-band control: the control network has overlap with the data network, in other words, the control traffic may share same network with the data traffic
Data network
controller
Control network
out-band control
controller
Data network
in-band control

## Slide 38: Setup the communication channels between the SWs and the controller
Out-band control, the SWs just initiate the TCP connection through the dedicated port connecting to the control network. The address of the controller is preconfigured in a file or can be retrieved through e.g. DHCP [2]
In-band control
  If the data network is a complete SDN network, then some rules have to be preinstalled into the switch for bootstrapping. For instance, allowing ARP traffic for the MAC of the controller or gateway, allowing for DHCP packets and TCP traffic from/to the controller. These rules have highest priority then the rules from the controller
  If the data network is a hybrid SDN network, then initially the connection can be setup like the out-band scenario. Later, the controller may setup rules for the control traffic in order to make the connection more reliable.
Some examples of out-band control: google B4; in-band control: OVS

## Slide 39: Topology discovery
How does the controller discover the network topology?
  In the literature, LLDP was proposed to discover the links among switches, however that cannot help with host discovery
  For the host discovery, SDN relies on that the hosts send packets, then the switches forward the first packet to the controller, therefore, the controller knows which switch connects which host via which port.
  To get the information of which host connects to which SW, we may let the hosts to send some packets (e.g. LLDP, ICMP) to the switch, then the switch can report this to the controller.

## Slide 40
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
S1, experiencing link failure using OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra’s routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes
4

## Slide 41
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
Controller uses OpenFlow to install new tables in switches that need updating
6

## Slide 42
topology
manager
Basic Network Service Functions
REST API
OpenFlow 1.0
…
SNMP
OVSDB
forwarding
manager
switch
manager
host
manager
stats
manager
Network service apps
Service Abstraction Layer (SAL)
Access
Control
Traffic
Engineering
…
OpenDaylight (ODL) controller
ODL Lithium controller
network apps may be contained within, or be external to SDN controller
Service Abstraction Layer: interconnects internal, external applications and services

## Slide 43
Network
control apps
…
REST API
ONOS
distributed core
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
Intent
statistics
devices
hosts
links
paths
flow rules
topology
ONOS controller
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling

## Slide 44: Mininet
Provide tools to create virtualized network with OVS
CLI for manipulating network dynamically
Virtualized hosts
Controllers: POX, Ryu, Opendaylight, etc.
CONTROLLER
Virtual
Switch
Virtual
Switch
h
h
h
h
Openflow traffic
App

## Slide 45
mininet$ sudo mn *** Creating network *** Adding controller *** Adding hosts: h1 h2 *** Adding switches: s1 *** Adding links: (h1, s1) (h2, s1) *** Configuring hosts h1 h2 *** Starting controller c0 *** Starting 1 switches s1 ... *** Starting CLI:
mininet> pingall *** Ping: testing ping reachability h1 -> h2 h2 -> h1 *** Results: 0% dropped (2/2 received) mininet> dpctl dump-flows *** s1 ------------------------------------------------------------------------ NXST_FLOW reply (xid=0x4): cookie=0x0, duration=38.192s, table=0, n_packets=1, n_bytes=98, idle_timeout=60, idle_age=38, priority=65535,icmp,in_port=2,vlan_tci=0x0000,dl_src=d6:13:79:41:63:43,dl_dst=7e:6c:76:0d:89:c9,nw_src=10.0.0.2,nw_dst=10.0.0.1,nw_tos=0,icmp_type=0,icmp_code=0 actions=output:1 cookie=0x0, duration=38.190s, table=0, n_packets=1, n_bytes=98, idle_timeout=60, idle_age=38, priority=65535,icmp,in_port=2,vlan_tci=0x0000,dl_src=d6:13:79:41:63:43,dl_dst=7e:6c:76:0d:89:c9,nw_src=10.0.0.2,nw_dst=10.0.0.1,nw_tos=0,icmp_type=8,icmp_code=0 actions=output:1 cookie=0x0, duration=38.189s, table=0, n_packets=1, n_bytes=98, idle_timeout=60, idle_age=38, priority=65535,icmp,in_port=1,vlan_tci=0x0000,dl_src=7e:6c:76:0d:89:c9,dl_dst=d6:13:79:41:63:43,nw_src=10.0.0.1,nw_dst=10.0.0.2,nw_tos=0,icmp_type=0,icmp_code=0 actions=output:2 cookie=0x0, duration=38.192s, table=0, n_packets=1, n_bytes=98, idle_timeout=60, idle_age=38, priority=65535,icmp,in_port=1,vlan_tci=0x0000,dl_src=7e:6c:76:0d:89:c9,dl_dst=d6:13:79:41:63:43,nw_src=10.0.0.1,nw_dst=10.0.0.2,nw_tos=0,icmp_type=8,icmp_code=0 actions=output:2 cookie=0x0, duration=33.190s, table=0, n_packets=1, n_bytes=42, idle_timeout=60, idle_age=33, priority=65535,arp,in_port=1,vlan_tci=0x0000,dl_src=7e:6c:76:0d:89:c9,dl_dst=d6:13:79:41:63:43,arp_spa=10.0.0.1,arp_tpa=10.0.0.2,arp_op=2 actions=output:2 cookie=0x0, duration=38.193s, table=0, n_packets=1, n_bytes=42, idle_timeout=60, idle_age=38, priority=65535,arp,in_port=2,vlan_tci=0x0000,dl_src=d6:13:79:41:63:43,dl_dst=7e:6c:76:0d:89:c9,arp_spa=10.0.0.2,arp_tpa=10.0.0.1,arp_op=2 actions=output:1 cookie=0x0, duration=33.191s, table=0, n_packets=1, n_bytes=42, idle_timeout=60, idle_age=33, priority=65535,arp,in_port=2,vlan_tci=0x0000,dl_src=d6:13:79:41:63:43,dl_dst=7e:6c:76:0d:89:c9,arp_spa=10.0.0.2,arp_tpa=10.0.0.1,arp_op=1 actions=output:1

## Slide 46: References
"The road to SDN" http://queue.acm.org/detail.cfm?ref=rss&id=2560327
Kreutz, D., Ramos, F. M., Verissimo, P. E., Rothenberg, C. E., Azodolmolky, S., & Uhlig, S. (2015). Software-defined networking: A comprehensive survey.proceedings of the IEEE, 103(1), 14-76.
“SDN Architecture 1.0 - Open Networking Foundation”, https://www.opennetworking.org/images/stories/downloads/sdn-resources/technical-reports/TR_SDN_ARCH_1.0_06062014.pdf
Openflow specification v1.0, https://www.opennetworking.org/images/stories/downloads/sdn-resources/onf-specifications/openflow/openflow-spec-v1.0.0.pdf
Mininet, mininet.org
POX controller, http://www.noxrepo.org/