## Slide 1: Course on Computer Communication and Networks Lecture 2 Chapter 1: Introduction: Part B: Network structure, performance, security prelude
CTH EDA344/GU DIT 420

## Slide 2: A closer look at network structure:
mobile network
global ISP
regional ISP
home
network
institutional
network
network edge: hosts:
run application programs e.g. Web, email, …
… based on network services available
access networks:
connect end-hosts to the Internet (edge routers)
through physical media: wired, wireless links
network core:
interconnected routers
network of networks

## Slide 3
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
link
physical
router
switch
network edge: hosts:
run application programs e.g. Web, email, …
… based on network services available
access networks:
connect end-hosts to the Internet (edge routers)
through physical media: wired, wireless links
network core:
interconnected routers
network of networks
Types of communication service available by the transport layer @ Internet:
connection-oriented: reliable, in-order data delivery (TCP)
connectionless: “best effort”, arbitrary order data-delivery (UDP)
Q: How & based on what “core” functionality?
  (…main Q for the Internet….)
A closer look at network structure:
UDP
TCP

## Slide 4: Roadmap
Zooming into core
  Ways of data transfer
  Routing
  Performance: delays (& loss)
  …. throughput
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 5: The Network Core
mesh of interconnected routers
fundamental question: how is data transferred through net?
  packet-switching: data sent thru net in discrete “chunks”

## Slide 6: Network Core: Packet Switching
A
B
C
10 Mbs
Ethernet
1.5 Mbs
45 Mbs
D
E
queue of packets
waiting for output
link
Application messages divided into packets
packets share network resources
resources used as needed
store and forward:
packets move one hop at a time
  transmit over link; wait turn at next link

## Slide 7: Alternative Core: Circuit Switching (analogue telephony)
End-end resources dedicated for “call”
dedicated resources (link bandwidth, switch capacity): no sharing
circuit-like (guaranteed) performance
call setup required
Example video for Circuit vs packet switching
  http://www.youtube.com/watch?v=Dq1zpiDN9k4&feature=related

## Slide 8: Packet switching versus circuit switching
1 Mbit link
each user/connection:
  100Kbps when “active”
  active 10% of time (bursty behaviour)
circuit-switching how many users/connections can be multiplexed?:
  10
packet switching
  with n= 35 users:
  P( k > 10 active) < 0.0004
   almost all of the time, same queuing behaviour as in circuit switching)
Packet switching allows more users to use the network!
n users
1 Mbps link
Hint: The probability of k out of n users active (p=0.1 in our example)
Q: what happens with > 35 users?
Still circuit-like behavior?
Traffic intensity:
(aggregated
input rate/bandwidth)

## Slide 9: Roadmap
Zooming into core
  Ways of data transfer
  Routing
  Performance: delays, (& loss) …
  …. throughput
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 10: (Can we combine the benefits of CS & PS?) Routing and network-core main design issue
What is routing’s role? find routes from source to destination
path selection algorithms
Important design issue/type of service offered at network layer:
  datagram network:
    destination address determines next hop
    routes may change during session
  virtual circuit network: resource reservation+sharing!!
    path determined at call setup, remains fixed thru session
    “bridging” packet-switching with circuit switching
    routers can prioritize, must maintain per-session state
Simple to implement & maintain
(Internet main approach)
Expensive, but better to build guarantees

## Slide 11: Roadmap
Zooming into core
  Ways of data transfer
  Routing
  Performance: delays, (& loss) …
  …. throughput
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 12: Delay in packet-switched networks
1. nodal processing:
  check bit errors
  determine output link
2. queuing
  time waiting at output link for transmission
  depends on congestion level of router
A
B
propagation
transmission
nodal
processing
queueing
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s

## Slide 13: Visualize delays: packet switching
store and forward behavior visualization
fig. Gorry Fairhurst
time to send bits into link = L/R
propagation delay = d/s

## Slide 14: Queueing delay (revisited) …
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite! Queues may grow unlimited, packets can be lost
La/R ~ 0
La/R -> 1

## Slide 15: Delays and packet loss
Link queue (aka buffer) has finite capacity
packet arriving to full queue dropped (aka lost)
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 16: Roadmap
Zooming into core
  Ways of data transfer
  Routing
  Performance: delays, (& loss)…
  …. throughput
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 17: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe

## Slide 18: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
link on end-end path that constrains end-end throughput
bottleneck link

## Slide 19: … “Real” Internet delays and routes (1)…
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 20: …“Real” Internet delays and routes (2)…
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no reponse (probe lost, router not replying)
trans-oceanic
link

## Slide 21: Roadmap
Zooming into core
  Ways of data transfer
  Routing
  Performance: delays, (& loss) …
  …. throughput
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 22: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 23: Access net: digital subscriber line (DSL)
central office
ISP
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    Multiplexing data/voice over DSL phone line to Internet/telephone net
  Transmission rates:
    < 2.5 Mbps upstream (typically < 1 Mbps)
    < 24 Mbps downstream (typically < 10 Mbps)
DSL
modem
splitter
DSL access
multiplexer

## Slide 24
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
ISP
cable modem
termination system
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream, 2 Mbps upstream
network of cables, attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office
Access net: cable network

## Slide 25
Access net: home network
to/from headend or central office
Modem or fiber box
router, firewall, NAT
wired Ethernet (100 Mbps)
wireless access
point (54 Mbps)
wireless
devices
often combined
in single box

## Slide 26: Enterprise access networks (Ethernet)
typically used in companies, universities, etc
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 27: Wireless access networks
shared wireless access network connects end system to router
  “adhoc” or via base station aka “access point”
wireless LANs (10’s m)
  802.11b/g (WiFi): 11 or 54 Mbps
wider-area wireless access (10’s km)
  provided by telco operator
  ~1-10 Mbps over cellular system
  3G, 4G, 5Gevolving (for IoT)
base
station
mobile
hosts
router

## Slide 28: Physical Media
physical link: transmitted data bit propagates across link
  guided media:
    signals propagate in solid media: copper, fiber
  unguided media:
    signals propagate freely e.g., radio
R: link transmission rate
host
1
2
packets, e.g.
L bits each
  aka link capacity,
  aka link bandwidth

## Slide 29: Guided physical Media: coax, fiber, twisted pair
Coaxial cable:
wire (signal carrier) within a wire (shield)
broadband: multiple channels multiplexed on cable (HFC, cable TV)
Fiber optic cable:
low attenuation: fewer repeaters
low error rate: light pulses immune to electromagnetic noise
high-speed operation: e.g., 10-100 Gps
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5/6: more twists, higher insulation: 100-1000 Mbps/10 Gbps

## Slide 30: Unguided Physical media: Radio Properties: Attenuation, Multipath propagation
Signal can fade with distance, can get obstructed, can take many different paths between sender and receiver due to reflection, scattering, diffraction
signal at sender
signal at receiver
radio links (Mbps): terrestrial microwave, LAN/WiFi, wide-area/cellular, satellite

## Slide 31: Roadmap
Zooming into core
  Ways of data transfer
  Routing
  Performance: delays, (& loss)…
  …. throughput
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 32: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 33: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…

## Slide 34: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP

## Slide 35: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
access
net

## Slide 36: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
But if one global ISP is viable business, there will be competitors …. which must be interconnected
IXP
peering link
Internet exchange point
(approx. 400 in the world)
IXP

## Slide 37: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
… and regional networks may arise to connect access nets to ISPs

## Slide 38: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
Content provider network
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users

## Slide 39: Internet structure: network of networks
at center: small # of well-connected large networks
“tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT, Telia), national & international coverage
content provider network (e.g., Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
IXP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP

## Slide 40: Internet structure: network of networks
a packet passes through many networks
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 41: Roadmap
Zooming into core
  Ways of data transfer
  Routing
  Performance: delays, …
  …. throughput, loss
Network/Internet structure complemented:
  access net, physical media
  backbones, NAPs, ISPs
Security prelude

## Slide 42: Network Security Prelude
The field of network security is about:
  how adversaries can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  Security considerations in all layers!

## Slide 43: Bad guys can put malware into hosts via Internet
Malware can get in host from a virus, worm, or trojan horse.
Spyware malware can record keystrokes, web sites visited, upload info to collection site.
Infected host can be enrolled in a botnet, used for spam and DDoS attacks.
Malware is often self-replicating: from an infected host, seeks entry into other hosts

## Slide 44: Bad guys can sniff packets
Packet sniffing:
  Shared/broadcast medium (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets passing by
A
B
C
src:B dest:A payload
Wireshark software used for end-of-chapter labs is a (free) packet-sniffer
NOTE: be aware that it is inappropriate to use outside the scope of the lab

## Slide 45: Bad guys can use false source addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload

## Slide 46: Bad guys can record and playback
record-and-playback: sniff sensitive info (e.g., password), and use later
  password holder is that user from system point of view
A
B
C
src:B dest:A user: B; password: foo

## Slide 47: Chapter 1: Summary
Covered a “ton” of material!
what’s the Internet
what’s a protocol?
protocol layers, service models
network edge (types of service)
network core (ways of transfer, routing)
performance, delays, loss
access net, physical media
backbones, NAPs, ISPs
Security concerns
(history: read more in corresponding section, interesting & fun )
In order to have:
context, overview, “feel” of networking
A point of reference for context in the focused discussions to come

## Slide 48: Reading instructions (incl.next lecture)
Careful | Quick
6/e, 7/e: 1.3, 1.4, 1.5 | the rest
1. Kurose Ross book
Extra Reading (optional)
Computer and Network Organization: An Introduction,
by Maarten van Steen and Henk Sips, Prentice Hall
(very good introductory book for non-CSE students)

## Slide 49: Review questions
Review questions from Kurose-Ross book, chapter 1 (for basic study)
6/e, 7/e: R11, R12, R13, R16, 17, R18, R19, R20, R21, R22, R23, R24, R25, R28.
Extra questions, for further study: delay analysis in packet switched networks:
http://www.comm.utoronto.ca/~jorg/teaching/ece466/material/466-SimpleAnalysis.pdf