## Slide 1: Course on Computer Communication and Networks Lecture 7 Network Layer, Chapter 4 (6/e) - Part B (7/e Ch5)
EDA344/DIT 420, CTH/GU

## Slide 2: Network layer
Consider transporting a segment from sender to receiver
sending side: encapsulates segments into datagrams
receiving side: delivers segments to transport layer
network layer protocols in every host, router
  examines header fields in all datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 3
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
a b c d
a’ b’ c’ d’
a” b” c” d”
1
2
3
NW layer’s job - routing and forwarding
Interplay between the two:
routing algorithm determines
path through network
(control-plane functionality)
forwarding table determines
local forwarding at this router
(data-plane functionality)

## Slide 4: Roadmap Network Layer
PREVIOUS Lect.
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related: IPv4, maskig&forwarding, obtaining an IP address, DHCP, NAT, IPv6
Now: Control, routing
path selection/routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
instantiation, implementation in the Internet routing protocols
  RIP
  OSPF
  BGP
ICMP (control protocol)

## Slide 5: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
N = set of “Nodes” routers = { u, v, w, x, y, z }
E = set of “Edges” links = { (u,v), (u,x), (u,w), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
Question: What is the least-cost path between u and z?
Cost of link xw is c(x,w) = 3
Cost of link could be always 1 hop, or related directly to delay or inversely to bandwidth, or any other metric
Routing algorithm: finds least-cost path
Cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)

## Slide 6: Routing Algorithm Classification
Global or decentralized?
Global:
all routers have complete and global knowledge about topology, and all link-costs
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
exchange of info with neighbors
Iteratively calculate the least-cost paths to other routers
Static or dynamic routing?
Static:
routes change slowly over time, manually configured
Dynamic:
routes change more quickly
  periodic update, or
  in response to link-cost changes

## Slide 7: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related
Control, routing
path selection/routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
instantiation, implementation in the Internet routing protocols
  RIP
  OSPF
  BGP
ICMP (control protocol)

## Slide 8: A Link-State (LS) Routing Algorithm
Dijkstra’s shortest path algo
link costs known to all nodes
  Each node floods “link state multicasts” with costs to its neighbors etc
  all nodes get same info
Each node computes least cost paths from itself to all other nodes
  gives forwarding table for that node
iterative: after k iterations, knows least cost path to k destinations

## Slide 9: Dijsktra’s Algorithm at node u
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent (directly attached neighbor) to u
5 then D(v) = c(u,v)
6 else D(v) = 
7
8 Loop
9 find node w not in N' such that D(w) is a minimum
10 add node w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min{ D(v), D(w) + c(w,v) }
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes N in N'
c(x,y): link cost from x to y. Initially cost(x,y) = ∞ if not direct neighbors
D(v): Distance; current value of cost of path from source to destination v
p(v): predecessor node, i.e. previous node that is neighbor of v along current path from the source to node v
N': set of Nodes whose least cost path definitively known

## Slide 10: Dijkstra’s algorithm: example node u
Step
0
1
2
3
4
5
N'
u
ux
uxv
uxvy
uxvyw
uxvywz
D(v),p(v)
2,u
2,u
D(w),p(w)
5,u
4,x
4,x
3,y
D(x),p(x)
1,u
D(y),p(y)

2,x
2,x
D(z),p(z)



4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
v w x y z

## Slide 11: Dijkstra’s algorithm: forwarding table
u
y
x
w
v
z
Resulting shortest-path tree from node u as root:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
via link
Resulting forwarding table in u:
cost
2
1
2
3
4
Root

## Slide 12: Dijkstra’s algorithm, discussion
Algorithm complexity: n nodes
each iteration: need to check all nodes, not in N’
n(n+1)/2 comparisons: Order of (n2)
Oscillations possible:
e.g., if link cost = delay-based or traffic-based, dynamically variable metric
must avoid these metrics
But:
Good for small networks
Link-cost changes are not frequent, more stable network
Faster to converge when changes in link-costs

## Slide 13: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related
Control, routing
path selection/routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
instantiation, implementation in the Internet routing protocols
  RIP
  OSPF
  BGP
ICMP (control protocol)

## Slide 14: Distance Vector (DV) Algorithm
Bellman-Ford Equation:
Define
dx(y) := cost of least-cost path from x to y
If v is any neighbor to x with link cost c(x,v) and has dv(y) as least-cost path to y
Then the DV estimate:
dx(y) = min { c(x,v) + dv(y) }
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 15: Distance vector (DV) algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:

## Slide 16: Bellman-Ford: example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
Node x that achieves minimum is the next
hop in least-cost path to z ➜ forwarding table
BF equation says:
Nodes v, x & w are the neighbors of u

## Slide 17
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2

## Slide 18
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3

## Slide 19: DV: link cost changes (good news)
Link cost changes: decreased cost
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good news
travels fast”
x
z
1
4
50
y
1
At time t0, y detects the link-cost change, updates its DV,
and informs its neighbors.
At time t1, z receives the update from y and updates its table.
It computes a new least cost to x and sends its neighbors its DV.
At time t2, y receives z’s update and checks its distance table.
y’s least costs do not change and hence y does not send any
update to z.

## Slide 20: DV: link cost changes (bad news)
Link cost changes: increased cost
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes!
  y already knows z has cost 5 to reach x
  y therefore announces cost 6 to reach x
  z announces cost is now 7, etc..
Poisoned reverse:
If z routes through y to get to x:
  z tells y its (z’s) distance to x is infinite (so y won’t route to x via z)
x
z
1
4
50
y
60
“bad news travels slow”

## Slide 21: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) messages sent
DV: exchange between neighbors only, until convergence
Convergence due to changes
LS:
  may have oscillations
  fast convergence
DV:
  may be routing loops
  count-to-infinity problem
  slow convergence
Robustness: what happens if router malfunctions?
LS:
  each node computes only its own table
  limited damage
DV:
  node can advertise incorrect path cost
  each node’s table used by others
    error propagates through network

## Slide 22: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related
Control, routing
path selection/routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
instantiation, implementation in the Internet routing protocols
  RIP
  OSPF
  BGP
ICMP (control protocol)

## Slide 23: Hierarchical Routing
scale: millions of destinations!
can’t store all destinations in routing tables!
LS routing info exchange would swamp links!
DV would never terminate
administrative autonomy
Internet = network of networks
each network administrator may want to control routing in its own network
Our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 24: Interconnected ASs
intra-AS sets entries for internal destinations
inter-AS sets entries for external destinations
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
Forwarding table configured by both intra- and inter-AS routing algorithms
border router
at “edge” of its own AS
aggregate routers into regions, “autonomous systems” (AS)
  Internet: > 39,000 AS

## Slide 25: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related
Control, routing
path selection/routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
instantiation, implementation in the Internet routing protocols
  RIP
  OSPF
  BGP
ICMP (control protocol)

## Slide 26: Intra-AS Routing
also known as Interior Gateway Protocols (IGP)
most common Intra-AS routing protocols:
  RIP: Routing Information Protocol [DV]
  OSPF: Open Shortest Path First [LS]
  EIGRP: Enhanced Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 27: RIP ( Routing Information Protocol)
distance vector algorithm
included in BSD-UNIX Distribution 4.3 in 1982
distance metric: number of hops (max = 15 hops)
Version 1 classful and version 2 classless
D
C
B
A
u
v
w
x
y
z
destination hops
u 0
v 1
w 1
x 2
y 2
z 1
From router A to subnets:

## Slide 28: RIP Table processing
RIP routing tables managed by application-level process called routed (route daemon)
advertisements periodically sent in UDP packets (port 520) using broadcast (or multicast, RIP v.2)
physical
link
network forwarding
(IP) table
transport
(UDP)
routed
physical
link
network
(IP)
transport
(UDP)
routed
forwarding
table

## Slide 29: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related
Control, routing
path selection/routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
instantiation, implementation in the Internet routing protocols
  RIP
  OSPF
  BGP
ICMP (control protocol)

## Slide 30: OSPF (Open Shortest Path First)
“open”: just means publicly available (RFC 2328)
uses Link State algorithm
  complete topology map built at each node
  route computation using Dijkstra’s algorithm
  works in larger networks (hierarchical structure with areas)
OSPF advertisements sent within area via flooding.
  carried in OSPF messages directly over IP with protocol number 89 (no UDP- or TCP-transport)
  sent at least every 30 minutes

## Slide 31: OSPF features
security: all OSPF messages can be authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed
Send HELLO messages to establish adjacencies with neighbors to check operational links
hierarchical OSPF in large domains.

## Slide 32: Hierarchical OSPF
boundary router
backbone router
Area 1
Area 2
Area 3
backbone
area
border
routers
internal
routers

## Slide 33: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related
Control, routing
path selection/routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
instantiation, implementation in the Internet routing protocols
  RIP
  OSPF
  BGP
ICMP (control protocol)

## Slide 34: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol)
  the de facto standard routing protocol on the Internet
  Complex protocol
  Communicates over TCP port 179 with authentication
BGP provides each AS a means to:
  Obtain prefix reachability information from neighboring ASs.
  Propagate reachability information to all AS-internal routers.
  Determine “good” routes to prefixes based on reachability information and policy.

## Slide 35: BGP basics
pairs of routers (BGP peers) exchange routing info over semi-permanent TCP connections: BGP sessions
  BGP sessions need not correspond to physical links.
  advertising paths to different destination network prefixes (“path vector” protocol)
when AS3 advertises a prefix to AS1:
  AS3 promises it will forward datagrams towards that prefix.
  AS3 can aggregate prefixes in its advertisement
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP
message

## Slide 36: Distributing Reachability Info
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
eBGP
message
With “external BGP” eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
  1c can then use “internal BGP” iBGP to distribute new prefix info to all routers in AS1
  1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP session
when router learns of new prefix, it creates entry for prefix in its forwarding table.
eBGP session
iBGP session
eBGP
message

## Slide 37: Path attributes & BGP routes
advertised prefix includes BGP attributes.
  prefix + attributes = “route”
two important attributes:
  AS-PATH: contains ASs through which prefix can be reached: e.g., AS3, AS1
  NEXT-HOP: indicates specific AS router to next-hop AS. E.g. 1b
when gateway router receives route advertisement, uses import policy to accept or decline.
  May or may not accept/announce everything to/from peers
Router may learn about more than 1 route to some prefix. Router selects route based on:
  Policy decision
  Shortest AS_PATH
  Closest NEXT_HOP router

## Slide 38: BGP routing policy example (1)
A,B,C are provider networks
x,w,y are customers (of provider networks)
x is dual-homed: attached to two networks
  x does not want to route from B via x to C
  .. so x will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 39: BGP routing policy example (2)
A advertises to B path A-w
B advertises to x path B-A-w
Should B advertise path B-A-w to C? no
  B gets no “revenue” for routing C-B-A-w since neither w nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers…
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 40: Growth of the BGP table: 1994 to Present
http://bgp.potaroo.net

## Slide 41: Why different Intra- & Inter-AS routing?
Policy:
Inter-AS: admin wants control over how its traffic routed, who routes through its net.
Intra-AS: single admin, so no policy decisions needed
Scale:
hierarchical routing saves routing table size, reduced update traffic
Performance:
Inter-AS: policy may dominate over performance
Intra-AS: can focus on performance

## Slide 42
data
plane
control
plane
Recall SDN: Logically organized control plane
A distinct (can be remote/distributed) controller interacts with local control agents (CAs)
  this architecture (SDN) can enable new functionality (will be studied later in the course)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 43: Roadmap Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related
Control, routing
path selection/routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
instantiation, implementation in the Internet routing protocols
  RIP
  OSPF
  BGP
ICMP (control protocol)

## Slide 44: ICMP: Internet Control Message Protocol
Control and error messages from network layer.
All IP implementations must have ICMP support.
ICMP messages carried in IP datagrams
used by hosts & routers to communicate network-level control information and error reporting
  Error reporting: e.g., unreachable network, host, ..
  Example: (used by ping command)
    Sends ICMP echo request
    Receives ICMP echo reply
Any ICMP error message may never generate a new one.

## Slide 45: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 46: Traceroute and ICMP
source sends series of UDP segments (=probes) to destination
  first set has TTL =1,second TTL=2, etc.
when datagram in nth set arrives to n-th router:
  router discards it and reports error (TTL expired) sends source ICMP message (type 11, code 0)
  ICMP message include name of router & IP address
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 47: Summary Network Layer
Forwarding versus routing
Network layer service models
  Network layer architecture (shift): Software-Defined Networks
Inside a router
The Internet Network layer: IP, Addressing & related
Control, routing
path selection/routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
instantiation, implementation in the Internet routing protocols
  RIP
  OSPF
  BGP
ICMP (control protocol)
NEXT: Link Layer

## Slide 48: Reading instructions Network Layer (incl. prev. lecture)
KuroseRoss book
Careful | Quick
5/e,6/e: 4.1-4.6 7/e: 4.1-4.3, 5.2-5.4, 5.5, 5.6, [new- SDN, data and control plane 4.4, 5.5: in subsequent lectures, connecting to multimedia/streaming Study material through the pingpong-system] | 5/e,6/e: 4.7, 7/e: 5.7

## Slide 49: Some complementary material /video-links
IP addresses and subnets http://www.youtube.com/watch?v=ZTJIkjgyuZE&list=PLE9F3F05C381ED8E8&feature=plcp
How does PGP choose its routes http://www.youtube.com/watch?v=RGe0qt9Wz4U&feature=plcp
Some taste of layer 2: no worries if not all details fall in place, need the lectures also to grasp them.
Hubs, switches, routers http://www.youtube.com/watch?v=reXS_e3fTAk&feature=related
What is a broadcast + MAC address http://www.youtube.com/watch?v=BmZNcjLtmwo&feature=plcp
Broadcast domains: http://www.youtube.com/watch?v=EhJO1TCQX5I&feature=plcp

## Slide 50: Extra slides

## Slide 51
w
4
v
x
u
5
3
7
4
y
8
z
2
7
9
3
Dijkstra’s algorithm: example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 52: Distance vector (DV) algorithm
Basic idea:
distributed, asynchronous, iterative
from time-to-time, each node sends to neighbors only its own distance vector DV estimate
When a node x receives new DV estimate from neighbor v, it updates its own DV using Bellman-Ford equation:
dx(y) ← minv {c(x,v) + dv(y)} for each node y ∊ N
Under normal conditions, when information comes in about new link costs:
  The estimate dx(y) converge to the actual least cost
  Routing table recalculated
  New results sent out to all neighbors

## Slide 53: RIP advertisements
distance vectors are exchanged among neighbors every 30 sec via Response Message (also called advertisement)
each advertisement: list of up to 25 destination subnets within AS
If no advertisement heard after 180 sec  neighbor or link declared dead (unreachable).
  Routes via neighbor invalidated
  New advertisements sent to other neighbors
  Link failure info propagates to entire network
  Poisoned reverse used with max hop count 15
  Infinite distance is 16 hops
RIP v.2 also supports route aggregation (1998)

## Slide 54: Hierarchical OSPF
two-level hierarchy: local areas, one backbone (area 0).
  Link-state advertisements only in area
  each node has detailed area topology; only knows direction (shortest path) to subnets in other areas.
area border routers: “summarize” subnets in own area, advertise to other area border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’s.

## Slide 55: BGP messages
BGP messages exchanged using TCP.
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous message; also used to close connection

## Slide 56: Getting a datagram from source to dest.

## Slide 57: Getting a datagram from source to dest.
IP datagram:
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
misc
fields
source
IP addr
dest
IP addr
data
datagram remains unchanged, as it travels source to destination
addr fields of interest here
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
forwarding table in A

## Slide 58: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
look up net. address of B
find B is on same net. as A (B and A are directly connected)
link layer will send datagram directly to B (inside link-layer frame)
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
misc
fields
223.1.1.1
223.1.1.3
data

## Slide 59: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
Starting at A, dest. E:
look up network address of E
E on different network
routing table: next hop router to E is 223.1.1.4
link layer is asked to send datagram to router 223.1.1.4 (inside link-layer frame)
datagram arrives at 223.1.1.4
continued…..
misc
fields
223.1.1.1
223.1.2.3
data

## Slide 60: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Arriving at 223.1.4, destined for 223.1.2.2
look up network address of E
E on same network as router’s interface 223.1.2.9
  router, E directly attached
link layer sends datagram to 223.1.2.2 (inside link-layer frame) via interface 223.1.2.9
datagram arrives at 223.1.2.2!!! (hooray!)
misc
fields
223.1.1.1
223.1.2.3
data
network router Nhops interface
223.1.1 - 1 223.1.1.4
223.1.2 - 1 223.1.2.9
223.1.3 - 1 223.1.3.27
Dest. next