Snow simulation
The material method is on point

---
Introduction
- Types of snow
  - Wet / dry
  - Powder / chunky
- Specialized solutions
- Elasto-plasticity
- Extensive background
  - Physics
  - Computer graphics
  - PIC/FLIP
    - Particle-in-cell
    - Fluid-implicit-particle
[Speaker Notes: Alternating Rigid/Deforming solid and fluid Specialized solutions * sandlike fluid * rigid Elastic is returning to original form (Rubber) Plastic is keeping deformed state (Metal)]

---
Introduction 2
Return of the equations
- Elasto-plastic energy density function
- Hardening coefficient, ξ
- Critical Compression / Stretch, θc / θs
- Young's Modulus, E0
%PSI ( bold F sub E, bold F sub P ) = %mu ( bold F sub P ) left ldline bold F sub E - bold R sub E right rdline sup 2 sub F + {%lambda ( bold F sub P )} over 2 ( J sub E - 1 ) sup 2
%lambda ( bold F sub P ) = %lambda sub 0 func e^{ %xi (1 - J sub P ) }
%mu ( bold F sub P ) = %mu sub 0 func e^{ %xi (1 - J sub P ) }
[Speaker Notes: Elastic component and Plastic component Hardening (Xi) controlls breaking speed * How stretchy it is as a plastic * Less is ductile, more is brittle Theta is when the material breaks * Less is powder, more is chunks Young's Modulus is relation between pressure and stress, contributes to breaking speed]

---
Method overview
1. Rasterize particle data to the grid
2. Compute particle volumes and densities
3. Compute grid forces
4. Update grid velocities
5. Collision in the grid
Implicit solve of linear system
1. Update deformation gradient
2. Update particle velocities
3. Collision in particles
4. Update positions

---
1. Data rasterization
ds
- Weighted with a 1D cubic B-spline
- Normalized weights for velocity
m sup n sub i = sum from p m sub p w sup n sub ip
bold v sup n sub i = sum from p bold v sub p m sub p w sup n sub ip over m sup n sub i
[Speaker Notes: Interpolation using weights, i.e. the b-spline Velocity needs to be normalized to conserve momentum]

---
2. Particle volume and density
m sup 0 sub i over h sup 3
- Using cell density:
- Particle volume estimation:
sds
ρ sup 0 sub p = sum from i m sup 0 sub i {w sup 0 sub ip} over h sup 3
V sup 0 sub p = m sub p over {%rho sup 0 sub p}
[Speaker Notes: Only done once Using cell density to estimate particle density]

---
3. Updating grid forces
sd
{partial %PSI} over {partial bold F sub E}
- Using
- Elastic stress using Cauchy stress tensor
bold f sub i ( bold {hat x} ) = - sum from p { V sup n sub p %sigma sub p nabla w sup n sub ip }
[Speaker Notes: Ties back to the elasto-plastic energy density function, its derivative Uses a second degree tensor called Cauchy stress tensor Tensor is a sort of continuation of vectors, second degree is 2 dimensional, i.e. a matrix]

---
4. Grid velocities
sd
- Simple velocity update
- Not final
bold v sup { `*` } sub i = bold v sup n sub i + %DELTA t { bold f sup n sub i } over { m sub i }
[Speaker Notes: Intermidiate step to computing the final grid velocities f/m is from f = m*a]

---
4. Grid collision
- Collision object types
  - Rigid
  - Deforming
- Sticky collisions
  - Special case: Vertical and under-hanging
sdsd
v sub n = bold v sub rel cdot bold n
bold v sub rel = bold v - bold v sub co
bold v sub t = bold v sub rel - bold n v sub n
bold {v'} sub rel = bold v sub t + %mu { bold v sub t } over { left ldline bold v sub t right rdline }
bold n = nabla %varphi
[Speaker Notes: Phi is object movement Using relative velocity to object If vn is positive, no collision Sticking collision if vt is under treshold Sticky => vrel = 0 Collision objects as level set rigid as stationary level set Deforming as interpolation from level set key frames Transform back v'rel + vco]

---
6. Implicit solve
as
Finalize grid velocities
sum from j ( bold I %delta sub { i j } + %beta %DELTA t sup 2 1 over { m sub i } { partial sup 2 %PHI sup n } over { partial bold {hat x} sub i partial bold {hat x} sub j}) v sup { n+1 } sub j = bold v sup { `*` } sub i
[Speaker Notes: Forces have been applied and collision has been detected and dealt with. Solve system to account for interdependencies between grid cells Result is the final velocity of each cell]

---
7. Deformation gradient
sd
Singular value decomposition
bold F sup { n+1 } sub p = ( bold I + %DELTA t nabla bold v sup { n+1 } sub p ) bold F sup n sub Ep bold F sup n sub Pp = bold { hat F } sup {n+1} sub Ep bold { hat F } sup {n+1} sub Pp
bold { hat F } sup { n+1 } sub Ep = U sub p { hat %SIGMA sub p } V sup T sub p
{ %SIGMA sub p } = clamp( { hat %SIGMA } sub p, [1- %theta sub c, 1 + %theta sub s] )
bold { F } sup { n+1 } sub Ep = U sub p { hat %SIGMA sub p } V sup T sub p ~~ a nd~~ bold { F } sup { n+1 } sub Pp = V sub p { hat %SIGMA } sub p sup -1 U sup T sub p bold F sup { n+1 } sub p
[Speaker Notes: Initially attribute all changes to elastic part Decompose to get Sigma Use Sigma to clamp in the interval of compression / stretch Recompose into elastic and plastic part Can be loosley seen as moving excess to plastic]

---
8. Particle velocities
sd
Alpha at 0.95
bold v sup { n+1 } sub p = ( 1 - %alpha ) bold v sup { n+1 } sub PICp + %alpha bold v sup { n+1 } sub FLIPp
bold v sup { n+1 } sub PICp = sum from i bold v sup { n+1 } sub i w sup n sub ip
bold v sup { n+1 } sub FLIPp = bold v sup n sub p + sum from i ( bold v sup { n+1} sub i - bold v sup n sub i ) w sup n sub ip
[Speaker Notes: Updating particle velocities using a blend between PIC manner and FLIP]

---
8. Particle collisions
- Second collision pass
- Fix discrepancies from interpolation
[Speaker Notes: Same procedure as with grid collisions]

---
10. Final particle update
Particle position updated using:
bold x sup { n+1 } sub p = bold x sup n sub p + %DELTA t bold v sup { n+1 } sub p
[Speaker Notes: Simple update of particle position]

---
Rendering
- Grid density relative material points gives variation
- Volumetric path tracing
- Henyey-Greenstein phase function
- Mie scattering
[Speaker Notes: Cartesian grid measures density relative to the material points gives the ability to render loose and packed snow Volumetric path tracing Uses in- and out-scattering Henyey-Greenstein phase function A function describing how light scatters in a	medium Mie scattering The more physical model of light scattering in general]

---
So.. is it worth it?
FLIP Comparison
- Most popular as Incompressible (Zhu and Bridson)
- Less versatile as a result
- Faster (?)
Limitations
- Hand tuning
- No air interaction
- CPU based
Example	Particles (106)	Grid size	Min per frame
Snowball drop	0.3	600 x 300 x 600	5.2
Snowball smash	0.3	200 x 240 x 600	7.3
Double smash	0.6	800 x 300 x 800	13.3
Snowplow	3.9	150 x 50 x 300	2.1
Rolling snowball	7.2	200 x 240 x 470	35.7
SIGGRAPH	0.75	780 x 120 x 220	4.7
The end	0.58	700 x 120 x 210	3.8
Castle destruction	1.6	360 x 160 x 560	6.0
Walking Character	3	370 x 120 x 300	15.7
Character digging	3.1	280 x 110 x 340	25.8
[Speaker Notes: Zhu and Bridson mention MPM, but refer to it as slow Paper claims to have addressed concerns All constants are hand tuned, but could be calibrated to measured metods No air interaction Powder snow and avalanches Could be generalised to work on sand and other fracture-type materials No GPGPU or SIMD]

---
?

---
Links
- Disney animation - Collection of articles
- Implementation in Python